## Slide 1: MLO Indication of Critical Updates
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Yanjun Sun | Qualcomm Inc. |  |  | 
Date: 2020-04-15

## Slide 2: Problem statement
A non-AP MLD can conserve power by performing basic BSS operations on a single link [1, 2, 3, 4]
MLO framework needs to provide a mechanism that would enable a non-AP MLD to receive updates to the operational parameter(s) for any link of the AP MLD without requiring the non-AP MLD to monitor all links
  Further any update that requires STA to not transmit on a link must be notified immediately.

## Slide 3: Solution Summary
Each AP of an MLD provides an indication of an update to the operational parameter(s) of another AP of the MLD
  Any update that requires silencing of STAs in the reported BSS is explicitly notified on the reporting link

## Slide 4: Indication of an update
An AP’s beacon includes a sequence counter affiliated with its current BSS parameter
  The counter is incremented whenever there is a change to one or more critical operational parameters.
Further, the link information contained in the beacon transmitted by an AP of an MLD carries the most recent value of sequence counter for a reported AP
  Advertising a counter instead of actual element(s) helps keep the beacon size small
Updates to operational parameters such as channel change announcements (CSA, ECSA), (V)HT/HE/EHT Op, (MU-)EDCA parameters, OM notifications etc qualify as critical updates
  Sequence counter similar to the Check Beacon field in TIM frame (See 11.2.3.15)
For example when AP makes a channel change announcement (by including ECSA element), it increments the sequence counter for its BSS.
  Other APs of the MLD advertise the new value of sequence counter

## Slide 5: Retrieving updated parameters
Non-AP MLD maintains a record of the most recently received sequence counter for each set-up link
A STA of a non-AP MLD can probe the reporting AP to retrieve updated parameters for the reported AP
  Benefit: non-AP MLD is not required to wake-up the STA on the reported link
    Works in situations where the BSS on the other link is in silence mode
      see next slide
  AP is recommended to transmit a broadcast Probe Response frame, carrying the profile for the requested link, in response to such a probe request
    Currently allowed (11ai/11ax)
    Helps address Probe storm issue
      i.e., prevents probe request from multiple STAs to retrieve the update

## Slide 6: Do-not-transmit indication
An AP may announce silence time on its BSS
  e.g., Quiet element or Channel Switch Mode=1
  In such case, the counter-based indication is not sufficient
    Non-AP STA MLD must be told right-away that it should not transmit any frames on the silenced channel
For such cases, other APs of the MLD provide an explicit do-not-transmit (DNT) notification on behalf of the silencing AP
  This is achieved by means for a single DNT bit in the per-link profile
Non-AP MLD is required to not transmit any frames on a link for which the AP MLD has indicated silence

## Slide 7: Signaling of critical updates

## Slide 8: Signaling of critical updates
The counter (CSN) for a transmitting link is carried in the EHT Operation element
  In case of Multiple BSSID set, EHT Op element would carry more than one counter (one per BSSID)
    EHT Op IE is common to the MBSSID set
  Limit CSN field size to at most 1 octet
    TBD whether Check Beacon and CSN for transmitting link need to have the same value
The counter (CSN) for other link(s) is carried in RNR IE
  As discussed in 11-20/357, MLO framework needs to make every attempt to prevent beacon bloating [SP#111]
    Therefore it is recommended that ML IE in a Beacon frame doesn’t carry per-AP profiles
    Per-AP profile subelement would introduce several octets of overhead - up to 4 octets per CSN
      [ Sub-element ID(1) + Length(1) + Link ID(1 or 2) + CSN(1) ]
    With MBSSID on various links, the overhead is multiplicative
  RNR is required to be present in a Beacon frame and is required to report each AP of the MLD [SP #95]
    Further RNR also carries MBSSID information
    Therefore it is natural to extend it to carry a counter affiliated with the reported AP [zero overhead]
Further, an indication in the initial portion of the beacon signals an update to the CSN value for any AP of the MLD
  Based on this determination, an associated STA can parse the entire beacon frame to find which AP of the MLD updated its BSS parameters
    A subfield in Capability Information field can provide such early indication of an update.
    Compatible with MBSSID case (nonTxBSSID Capability IE has the same structure)
  Such early indication is signaled over several beacons (e.g., until the DTIM beacon) to increase the likelihood that most associated STAs have seen the indication
    A STA that skips several beacon frames is expected to parse the beacon to determine any updates (baseline behavior).

## Slide 9: Signaling of critical updates
TxBSSID on Link 1 (AP11’s) beacon frame carries nonTxBSSID profile for AP12.
  EHT Op carries CSN for AP11 and AP12
  RNR carries CSN for AP21 and AP22
  Capability Info. field in the Beacon carries indication with respect to TxBSSID (AP11)
  Nontransmitted BSSID Capability Information element in profile for nonTxBSSID (AP12) carries indication with respect to AP12
Beacon frame
RNR
IE
MLA
AP entries
MLD/Common
…
(legacy) IEs for Tx-ing AP
EHT Cap/Op
MBSSID
IE
nonTxBSSID profiles
Capability Info. field
NonTxBSSID Capability Info. IE
CSN for reported APs
CSN for TxBSSID and nonTxBSSIDs
…
 | MLD1 | MLD2
Link 1 | AP11 (T) | AP12 (N)
Link 2 | AP21 (N) | AP22 (T)

## Slide 10: Summary
This contribution provides a mechanism by which a non-AP MLD can gather critical updates for any link of an AP MLD without requiring to monitor each link.
  Proposes to add a bit to signal silencing of a reported AP
  Proposes to define a sequence counter affiliated with critical parameters for each AP of an MLD
    The counter is carried in an AP’s Beacon frame and incremented each time there is an update to critical parameter set.
    The counter value is also advertised by other APs of the MLD
  Aids power-save by enabling a non-AP MLD retrieve BSS parameter updates of any AP of the MLD on the link where the non-AP is performing basic BSS operation

## Slide 11: SP #1
Do you agree that an AP of an AP MLD shall signal a do-not-transmit (DNT) bit affiliated with another AP of its MLD to indicate that the BSS of the reported AP is in silence mode (i.e., no transmissions are permitted on the channel where the reported AP resides).
  Y:
  N:
  A:

## Slide 12: SP #2
Do you agree to update the text in SFD (Motion #115, #SP77) as following:
  Do you support that an AP within an AP MLD shall include in the Beacon and Probe Response frames it transmits the Change Sequence fields that indicate changes of system information for the transmitting AP and other APs within the same AP MLD, where the change sequence field value for the reported each AP is initialized to 0, and is that increments incremented when there is a as the critical update to the operational parameters for that of the reported AP is occurred?
    TBD field(s) to carry the change sequence(s) of the transmitting AP and of non-transmitted BSSIDs (if any)
    The change sequence information for another AP of the MLD shall be carried in a field in the TBTT Information field of the Reduced Neighbor Report element corresponding to that AP.
    A TBD subfield in the Capability Information field of the Beacon frame shall provide an early indication of an update to change sequence information in the RNR for any AP of the reporting AP’s MLD.
      NOTE: For an AP corresponding to nontransmitted BSSID in a multiple BSSID set, the early indication is carried in the Nontransmitted BSSID Capability field (which has the same structure as the Capability Information field) and signals the update to change sequence information in RNR for APs corresponding to the MLD to which the nontransmitted BSSID is affiliated with.
    The signaling of the Change Sequence field is TBD.
    The critical updates are defined in 11.2.3.15 (TIM Broadcast) and the additional update can be added if needed.
    The field is at most 1 octet in length and the value carried in the field is modulo of the maximum value
    NOTE: It is optional for non-AP MLD to decode the subfield in the Capability Information field carrying the early indication
  Y: N: A:

## Slide 13: SP #3
Do you agree that the AP of an AP MLD shall advertise a change sequence counter (CSN) field affiliated with another AP of its MLD and the value of the field shall be the same as the change sequence counter (CSN) field carried in the beacon of the reported AP.
  Note: The name, size, and signaling of the sequence counter is TBD.
  Y:
  N:
  A:

## Slide 14: SP #4
Do you agree that a non-AP MLD that has performed ML setup with an AP MLD shall acquire the most recent BSS parameters for an AP of that AP MLD before the non-AP MLD’s STA on that link transmits a frame on that link?
  Y:
  N:
  A:

## Slide 15: SP #5
Do you agree that a STA of a non-AP MLD may send an individually addressed Probe Request frame to the peer AP on its link, to gather updates to the operational parameter(s) of another AP of the AP MLD with which the non-AP MLD has setup ML setup.
  Y:
  N:
  A:

## Slide 16: SP #6
Do you agree that an AP of an AP MLD should send a broadcast Probe Response frame in response to a Probe Request frame requesting information of another AP of the AP MLD when the request frame is received from a STA of a non-AP MLD with which the AP MLD has performed ML setup?
  Y:
  N:
  A:

## Slide 17: Appendix

## Slide 18: References
[1]: 11-19-1526 Multi-link Power-save (Abhishek, Qualcomm)
[2]: 11-20/070 Multi-link power saving operation (Yonggang, ZTE)
[3]: 11-19/1988 Power Save for Multi-link (Ming, Huawei)
[4]: 11-20/370 Multi-link Power Save Discussion (Sharan, Samsung)
[5]: 11-20-0357 MLO: Container Structure for Capability Advertisement (Abhishek, Qualcomm)

## Slide 19: SP #2
Do you agree that a beacon transmitted by an AP of an AP MLD shall carry a change sequence counter (CSN) field whose value is associated with critical parameters for the AP’s BSS and the value is incremented by 1 each time there is an update to the critical parameters?
  Note 1: The name, size, and signaling of the sequence counter is TBD.
  Note 2: The sequence counter is initialized to 0 and the value is modulo of the maximum value carried in the field
  Note 3: The critical parameter are defined in 11.2.3.15
  Note 4: 802.11be amendment may make updates to the critical parameters list in 11.2.3.15
  Y:
  N:
  A:
Amend SP #77