## Slide 1: EHT-SIG Contents for SU transmission
Date: 2020-04-07
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Introduction and Recap
The following SP has been run and didn’t pass:
  [20/0524r2] Do you agree that EHT-SIG field included in EHT-PPDU sent to a single user is duplicated per 20MHz in BW?
    12Y/29N/17Abs
There was a comment that a higher efficient EHT-SIG is preferred when BW>20Mhz for SU transmission
In this contribution, several options regarding EHT-SIG contents for SU transmission are discussed.

## Slide 3: Introduction and Recap
In 11ax, an HE MU PPDU can be transmitted to a single user. When BW>20MHz (40MHz for example), the HE-SIG-B contents (compressed mode) are shown as below:
  Padding is a waste of resources, and can be further improved in 11be
Non-MU-MIMO user specific field + CRC + Tail
Padding
CC1
CC2

## Slide 4: EHT-SIG contents for SU transmission (20Mhz case)
When the BW is 20Mhz, there is only one content channel, there are two directions [20-402r0]:
  Opt1: Unified SU & MU structure: EHT-SIG includes U-SIG overflow info, preamble puncture indication (if exist, needed only if BW>=80MHz) + non-MU-MIMO user specific + CRC + Tail
    more than one symbol (or even two symbols) of EHT-SIG
  Opt2: Separate SU & MU structure: for SU, EHT-SIG includes part or all of non-MU-MIMO user specific + CRC + Tail
    One symbol of EHT-SIG

## Slide 5: EHT-SIG contents for SU transmission (20Mhz case)
The details contents (for example) are shown as below:
Bit | Field | Number
B0-B2 | Version Identifier | 3
B3 | DL/UL | 1
B4-B9 | BSS Color | 6
B10-B16 | TXOP | 7
B17-B22 | Bandwidth | 4~6 (set to 6 as example)
B23-B24 | PPDU Format | 2
B25 | STBC | 1
U-SIG1 (Opt 1 or 2)
Bit | Field | Number
B0 | Spatial Reuse | 2
B1 |  | 
B2 | GI+EHT-LTF | 2
B3 |  | 
B4 | LDPC Extra Symbol Segment | 1
B5 | PE Disambiguity | 1
B6 | Pre-FEC Padding Factor | 2
B7 |  | 
B8-B12 | Number of EHT-SIG Symbols or MU-MIMO users | 5
B13-B15 | EHT-SIG MCS and DCM | 3
B16-B19 | CRC | 4
B20-B25 | Tail | 6
U-SIG2 (Opt1)
Bit | Field | Number
B0 | Spatial Reuse | 2
B1 |  | 
B2 | GI+EHT-LTF | 2
B3 |  | 
B4 | LDPC Extra Symbol Segment | 1
B5 | PE Disambiguity | 1
B6 | Pre-FEC Padding Factor | 2
B7 |  | 
B8-B15 | AID-Part 1 (8 bit) | 8
B16-B19 | CRC | 4
B20-B25 | Tail | 6
U-SIG2 (Opt2)
 | Field | Number
B0 | Number of EHT-LTF Symbols And Midamble Periodicity+Doppler | 4
B1 |  | 
B2 |  | 
B3 |  | 
 | preamble puncture indication | X
 | AID | 34
 | … | 
 | Beamformed | 
EHT-SIG (Opt1)
 | Field | Number
B0-B2 | AID-Part 2 (3bit) | 3
B3-B7 | NSTS+Doppler | 5
B8-B11 | MCS | 4
B12 | DCM | 1
B13 | Beam change | 1
B14 | Coding | 1
B15 | Beamformed | 1
B16-B19 | CRC | 4
B20-B25 | Tail | 6
EHT-SIG (Opt2)
38+X bits for EHT-SIG
26 bits for EHT-SIG

## Slide 6: EHT-SIG contents for SU transmission (BW>20MHz, Opt1)
When BW>20Mhz, if assuming Opt1, then several options can be considered:
  Opt1a: duplication (across whole BW or within 80MHz)
    Take advantage of MRC to achieve higher MCS, and lower overhead
    38+X may lead to more than 2 EHT-SIG symbols with MCS0 when X>14 bits
  Opt1b: “load balance” version, split the info to 2 CCs to achieve lower overhead:
    Can be seen as a “40MHz CC”
U-SIG overflow info + preamble puncture indication + Non-MU-MIMO user specific field + CRC + Tail (38+X bits)
U-SIG overflow info + preamble puncture indication + Non-MU-MIMO user specific field + CRC + Tail (38+X bits)
CC1
CC2
U-SIG overflow info + preamble puncture indication + Part 1 of Non-MU-MIMO user specific field
Part 2 of Non-MU-MIMO user specific field + CRC + Tail
CC1
CC2

## Slide 7: EHT-SIG contents for SU transmission (BW>20MHz, Opt2)
When BW>20Mhz, if assuming Opt2, then two options can be considered:
  Opt2a: duplication (across whole BW or within 80MHz)
    Take advantage of MRC to achieve further robustness
    Fit perfectly into one EHT-SIG symbol, same as 20Mhz case
  Opt2b: further add preamble puncture info besides the 20Mhz case:
    Can be seen as a 40MHz CC
preamble puncture indication (if exist) + Part or all of Non-MU-MIMO user specific field + CRC + Tail
preamble puncture indication (if exist) + Part or all of Non-MU-MIMO user specific field + CRC + Tail
CC1
CC2
preamble puncture indication (if exist, only needed for BW>20/40MHz) + Part of Non-MU-MIMO user specific field
Part of Non-MU-MIMO user specific field + CRC + Tail
CC1
CC2

## Slide 8: Summary
The proposal discusses several options regarding EHT-SIG contents for SU transmission when BW>20MHz.
The discussion is kind of independent of Opt 1 and Opt2, and can be seen as:
  Opt a: duplication per 20MHz (across whole BW or within 80MHz)
  Opt b: load balance version (40MHz CC case)

## Slide 9: Straw Poll #1
Which option do you prefer regarding EHT-SIG contents for SU transmission when BW>20MHz.?
  Opt a: duplication per 20Mhz (across whole BW or within 80MHz)
  Opt b: load balance version (40MHz CC case)
  Neither
  Abstain

## Slide 10
[1] 11-20-0049-01-00be-ppdu-types-and-u-sig-content
[2] 11-20-0285-00-00be-su-ppdu-sig-contents-considerations
[3] 11-20-0031-02-00be-considerations-on-eht-ppdu-formats
[4] 11-20-0029-03-00be-preamble-structure-and-sig-contents
[5] 11-20-0019-01-00be-11be-ppdu-format
[6] 11-20-0087-00-00be-discussions-on-u-sig-content-and-eht-sig-format
References