## Slide 1: Further Discussions on Efficient EHT Preamble
Date: 2019-11-18
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek |  |  | jianhan.liu@mediatek.com

## Slide 2: Introduction
EHT WLAN enable 240MHz and 320MHz BW PPDU and multiple resource units aggregations .
  To enable such features, preamble design based on IEEE 802.11ax/ac is not efficient because the length of the preamble can be very long.
In [2], an efficient preamble design that allows different signaling information conveyed on different 80MHz segment has been proposed.
In this contribution, we further discuss the benefits of per-80MHz segment EHT-SIGs.

## Slide 3: Agreed format of EHT PPDU
The agreed format of an EHT PPDU is shown in the following figure.
  The detection of EHT PPDU based on The LENGTH field in L-SIG and RL-SIG to a value N such that mod(N, 3) = 0.
U-SIG:
  There shall be a 2 OFDM symbol long, jointly encoded U-SIG in the EHT preamble immediately after the RL-SIG.
    The U-SIG will contain version independent fields. The intent of the version independent content is to achieve better coexistence among future 802.11 generations.
    In addition, the U-SIG can have some version dependent fields.
EHT-SIG:
  A variable MCS and variable length EHT-SIG, immediately after the U-SIG, in an EHT PPDU.

## Slide 4: Per-80MHz U-SIG and EHT-SIG
The per-80MHz U-SIG has been accepted in 11be [1]:
  Do you agree with allowing information in U-SIG to vary from one 80MHz to the next in an EHT PPDU of bandwidth >80MHz?
    Notes
      Each STA still needs to decode only one 80MHz segment in U-SIG
      Within each 80MHz, U-SIG is still duplicated in every non-punctured 20MHz
      SST operation using TWT is one potential applicable scenario, other scenarios are TBD (Needs MAC discussion).
Without per-80MHz EHT-SIG, per-80MHz U-SIG becomes less useful.
  Most overheads come from EHT-SIG, not U-SIG.
  Per-80MHz U-SIG can enable per-80MHz EHT-SIG.

## Slide 5: Per-80MHz preamble signaling
EHT-SIG in one 80MHz segment can contain assigned RU larger than 80MHz and also can contain assigned RU in other 80MHz segment.
  For stations support 160/240and 320MHz BW.
For 80MHz only STA, EHT-SIG in the 80MHz segment can only contain assigned RU within this 80MHz segment.
Each STA knows at which 80MHz its content channels are located before receiving the EHT PPDU.
Stations operated on non-primary 80MHz channel can only receive DL PPDUs or be triggered for uplink transmission on this non-primary 80MHz channel.
  If stations operated on non-primary 80MHz channel wants to transmit by itself, these stations need to switch to primary channel and contend on primary channel.

## Slide 6: EHT-SIG Content Channels
EHT-SIG can carry different contents in each 80MHz
  Each station knows the position of its content channels before reception the 11be PPDU.
  RU allocation, modulation informations for target stations are carried in the content channels in EHT-SIGs.
    EHT-SIG for each 80MHz segment can have two content channels similar to 11ax HE-SIGB.
    EHT-SIG for each 80MHz segment can also have more than two content channels similar to 11ax HE-SIGB.
  EHT-SIG efficiency significantly can be significantly improved.
    For 320MHz, even each 80MHz only have two content channels, there are 2X4=8 content channels in total.

## Slide 7: Merits of Per-80MHz Signaling
Duplication EHT-SIGs over 320MHz is not efficient at all. We can enhance the EHT-preamble efficiency by increase the number of content channels.
  In [3], overhead reduction analysis shows for 320MHz, the efficiency of per-80MHZ EHT-SIG can be enhanced by 4 times compared to duplicated EHT-SIGs.
With per-80MHz varying U-SIG, per-80MHz EHT-SIG can be easily enabled.
  U-SIG can indicate the required information for decoding the followed EHT-SIG within the same 80MHz segment.

## Slide 8: Merits of Per-80MHz Signaling (cont.’s)
Most importantly, based on knowledge of VHT and HE, 320MHz non-AP STAs will appear much later than 320MHz AP. Without per-80MHz signaling, for 80MHz/160MHz non-AP stations, AP can only use 80/160MHz BW.
  All 80MHz/160MHz only STAs must operate on primary 80MHz/160MHz.
  Note 80MHz/160MHz only STAs can not switch to other 80/160MHz in the middle of an PPDU since STAs need to process preamble in the primary 80MHz and switch center frequency to other frequency.
  So without per-80MHz signaling, 320MHz AP can only operate with 160MHz BW when STAs are 80MHz or 160MHz only. 320MHz AP becomes useless and this is not good for 11be market taking off.

## Slide 9: Straw Poll #1
Do you agree that EHT-SIG may carry different content in each 80MHz?
  For PPDU BW larger than 80MHz.
  SST operation using TWT is one applicable scenario, other scenarios are TBD.

## Slide 10: References
[1] “U-SIG structure and Preamble Processing”, IEEE 802.11-20/0380r0, Sameer Vermani.
[2] “Efficient EHT Preamble Design”, IEEE 802.11-20/0439r0, Jianhan Liu.
[3] “Multi-segment EHT-SIG design discussion”, IEEE 802.11-20/0545r1, Ross Yu Jian.