## Slide 1: Further Discussion on Bandwidth and Puncturing Information
Date: 2020-04-28
Authors:

## Slide 2: Introduction (1/2)
During the 04/09/2020 PHY conference call, following SPs were run [1]
  Do you support that U-SIG in each 80MHz shall carry puncturing channel info for at-least the specific 80MHz where it is transmitted?
    Whether BW/Puncturing info can be different for different 80MHz is TBD
    Whether BW and puncturing info bits in U-SIG are carried as a combined or a separate field is TBD
    Y/N/A: 42/9/6
  Do you agree that a subfield for preamble puncturing pattern information separate from the BW field is included in U-SIG and/or EHT-SIG for the 11be PPDU transmitted to a single user?
    Y/N/A: 36/4/14
  Which option do you prefer to configure the preamble puncturing information for transmission to a single user?
    Approach. 1 : BW field includes some puncturing information
    Approach. 2 : BW field doesn’t include puncturing information. Puncturing information is a separate field.
    Approach. 1/Approach. 2/Abs: 17/30/10

## Slide 3: Introduction (2/2)
From those SPs, below seems got most support
  Separate BW and puncturing information
  Inform puncturing information of at-least the specific 80MHz where it is transmitted in the U-SIG
In this contribution, we listed potential options for bandwidth and puncturing information based on above assumptions
All options assume 3 bit BW field in U-SIG to inform BW only
  6 cases: 20 / 40 / 80 / 160 or 80+80 / 240 or 160+80 / 320 or 160+160 MHz
  2 cases are reserved for future extension
  Note: 320MHz is already quite wide. If it is wider, then we need to follow UWB regulation.

## Slide 4: Potential Options
Option 1: 3 bit Puncturing Information in U-SIG to inform puncturing pattern for the 80MHz
  Total 7 cases
  Further puncturing information in EHT-SIG is needed for full bandwidth single user or multi user transmission
  In case of OFDMA, resource allocation information should be enough (by not allocating resources in punctured subchannels)
Option2: 4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth
  Maximum 13 case
See appendix for detail information

## Slide 5: Option 1 Examples
Puncturing Pattern of [1 1 x x 1 1 1 1]
U-SIG to inform each
80MHz puncturing
information
EHT-SIG to further
inform other 80MHz
segments puncturing
information in case of
full bandwidth
transmission
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 1 1]
PuncInfo=[1 1 x x]
PuncInfo=[1 1 x x]
Further PuncInfo
=[1 1 1 1]
Further PuncInfo
=[1 1 1 1]
Further PuncInfo
=[1 1 x x]
Further PuncInfo
=[1 1 x x]
Further PuncInfo
=[1 1 x x]
Further PuncInfo
=[1 1 x x]
U-SIG
EHT-SIG
Punctured
subchannels
Upper 80MHz
Lower 80MHz

## Slide 6: Option 2 Examples
Puncturing Pattern of [1 1 x x 1 1 1 1]
U-SIG to inform entire
BW puncturing information,
e.g. first four is for current
80MHz, and remaining is for
other 80MHz
No further information in
EHT-SIG
PuncInfo=[1 1 1 1
1 1 x x]
U-SIG
Punctured
subchannels
Upper 80MHz
Lower 80MHz
PuncInfo=[1 1 1 1
1 1 x x]
PuncInfo=[1 1 1 1
1 1 x x]
PuncInfo=[1 1 1 1
1 1 x x]
PuncInfo=[1 1 x x
1 1 1 1]
PuncInfo=[1 1 x x
1 1 1 1]

## Slide 7: Updated Contents Based on Feedback (Rev2)
In updated slides, we address the following comments
  Where to put puncturing information; version-independent or version-dependent?
  Whether entire puncturing information creates confusion to non-intended STA

## Slide 8: Where to put puncturing information; version-independent or version-dependent?
BW information is part of version-independent bits
Should puncturing information in version-independent bits as well?
Non-associated STA needs to know the exact puncturing pattern, at least, to decode FILS/unsolicited Probe Response
But it is not clear whether legacy (in this case 11be) device to know the puncturing information of next-generation PPDU is useful or not

## Slide 9: Where to put puncturing information; version-independent or version-dependent?
Let’s consider following cases
  11be STA’s operating P20 is punctured in next-gen PPDU: not clear whether 11be STA will decode the next gen. PPDU which does not contain P20
  Other than 11be STA’s operating P20 is punctured in next-gen PPDU: not clear whether 11be STA can transmit using the punctured channel which does not contain P20
Unless there is a use case, we propose to put puncturing information in version-dependent bits
Proposal 1. 11be signaling allows decoding BW/puncturing information without knowing the primary channel
Proposal 2. Place puncturing information in version-dependent bits or EHT-SIG

## Slide 10: Whether entire puncturing information creates confusion to non-intended STA?
Even if puncturing bits carriers puncturing information for entire bandwidth, it can be designed to be decoded for the 80MHz without knowing BSS channelization
For example (see slide 6), puncturing pattern of [1 1 x x 1 1 1 1]
  In the lower 80MHz, puncturing information can be [1 1 x x 1 1 1 1]
  In the upper 80MHz, puncturing information can be [1 1 1 1 1 1 x x]

## Slide 11: Whether entire puncturing information creates confusion to non-intended STA?
By this way,
  if a STA knows exact BSS channelization, then it knows entire bandwidth puncturing information
  if a STA does not know exact BSS channelization, then it only knows the 80MHz puncturing information
Proposal 3. 11be signaling allows decoding BW/puncturing information of the specific 80MHz where it is transmitted without knowing exact BSS channelization

## Slide 12: Summary
We propose followings
  11be signaling allows decoding BW/puncturing information without knowing the primary channel
  Place puncturing information in version-dependent bits or EHT-SIG
  11be signaling allows decoding BW/puncturing information of the specific 80MHz where it is transmitted without knowing exact BSS channelization

## Slide 13: Straw Poll #1
Do you support 11be signaling allows decoding BW/puncturing information without knowing the primary channel?

## Slide 14: Straw Poll #2
Do you support 11be signaling allows decoding BW/puncturing information of the specific 80MHz where it is transmitted without knowing exact BSS channelization?

## Slide 15: Straw Poll #3
Do you support placing puncturing information in version-dependent bits or EHT-SIG?

## Slide 16: Straw Poll #4
Do you support 3 bit BW field which doesn’t include puncturing information and puncturing information is a separate field?

## Slide 17: Straw Poll #5
Which option do you prefer?
  Option 1: 3 bit Puncturing Information in U-SIG to inform puncturing pattern for the specific 80MHz where it is transmitted
  Option 2: 4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth

## Slide 18: Reference
[1] 11-20/0587r1, “Minutes 802.11 be PHY ad hoc Telephone Conferences, April 2020”
[2] 11-20/0285r5, “SU PPDU SIG Contents Considerations”

## Slide 19: Appendix
3 bit Puncturing Information in U-SIG to inform puncturing pattern for the 80MHz
  7 cases: [1 1 1 1], [x 1 1 1], [1 x 1 1], [1 1 x 1], [1 1 1 x], [x x 1 1], [1 1 x x]
4 bit Puncturing Information in U-SIG to inform puncturing pattern for the entire bandwidth
  80MHz 1: No puncturing, 2: Agg 60MHz [x 1 1 1], 3: Agg 60MHz [1 x 1 1], 4: Agg 60MHz [1 1 x 1], 5: Agg 60MHz [1 1 1 x],
  160MHz 1: No puncturing, 2: Agg 120MHz [x x 1 1 1 1 1 1], 3: Agg 120MHz [1 1 x x 1 1 1 1], 4: Agg 120MHz [1 1 1 1 x x 1 1], 5: Agg 120MHz [1 1 1 1 1 1 x x], 6: Agg 140MHz [x 1 1 1 1 1 1 1], 7: Agg 140MHz [1 x 1 1 1 1 1 1], 8: Agg 140MHz [1 1 x 1 1 1 1 1], 9: Agg 140MHz [1 1 1 x 1 1 1 1], 10: Agg 140MHz [1 1 1 1 x 1 1 1], 11: Agg 140MHz [1 1 1 1 1 x 1 1], 12: Agg 140MHz [1 1 1 1 1 1 x 1], 13: Agg 140MHz [1 1 1 1 1 1 1 x],
  240MHz 1: No puncturing, 2: Agg 160MHz [1 1 1 1 x x x x 1 1 1 1], 3: Agg 160MHz [1 1 1 1 1 1 1 1 x x x x], 4: Agg 200MHz [x x 1 1 1 1 1 1 1 1 1 1], 5: Agg 200MHz [1 1 x x 1 1 1 1 1 1 1 1], 6: Agg 200MHz [1 1 1 1 x x 1 1 1 1 1 1], 7: Agg 200MHz [1 1 1 1 1 1 x x 1 1 1 1], 8: Agg 200MHz [1 1 1 1 1 1 1 1 x x 1 1], 9: Agg 200MHz [1 1 1 1 1 1 1 1 1 1 x x],
  360MHz 1: No puncturing, 2: Agg 240MHz [1 1 1 1 x x x x 1 1 1 1 1 1 1 1], 3: Agg 240MHz [1 1 1 1 1 1 1 1 x x x x 1 1 1 1], 4: Agg 240MHz [1 1 1 1 1 1 1 1 1 1 1 1 x x x x], 5: Agg 280MHz [x x 1 1 1 1 1 1 1 1 1 1 1 1 1 1], 6: Agg 280MHz [1 1 x x 1 1 1 1 1 1 1 1 1 1 1 1], 7: Agg 280MHz [1 1 1 1 x x 1 1 1 1 1 1 1 1 1 1], 8: Agg 280MHz [1 1 1 1 1 1 x x 1 1 1 1 1 1 1 1], 9: Agg 280MHz [1 1 1 1 1 1 1 1 x x 1 1 1 1 1 1], 10: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 x x 1 1 1 1], 11: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 1 1 x x 1 1], 12: Agg 280MHz [1 1 1 1 1 1 1 1 1 1 1 1 1 1 x x]