## Slide 1: Further discussion on RU allocation subfield in EHT-SIG
Date: 2020-04-16
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 
Oded Redlich | Huawei |  |  | 
Shimi Shilo | Huawei |  |  | 
Genadiy Tsodik | Huawei |  |  | 

## Slide 2: Introduction and recap
Several contributions have talked about MRU indication using RU allocation subfield in EHT-SIG:
  https://mentor.ieee.org/802.11/dcn/20/11-20-0578-00-00be-on-ru-allocation-singling-in-eht-sig.pptx (Jianhan Liu, Mediatek)
  https://mentor.ieee.org/802.11/dcn/20/11-20-0373-01-00be-ru-allocation-subfield-design-for-multi-ru-support.pptx (Myeongjin Kim, Samsung)
  https://mentor.ieee.org/802.11/dcn/20/11-20-0403-00-00be-signaling-of-multiple-ru-aggregation-in-ofdma.pptx (Dongguk Lim, LGE)
  https://mentor.ieee.org/802.11/dcn/20/11-20-0400-00-00be-multi-ru-combination-and-signaling-for-ofdma-transmission.pptx (Mengshi Hu, Huawei)
The contributions have merged a solution to use an enhanced table for RU allocation for both single RU and multi-RU.
This contribution further discusses several aspects regarding the detailed signaling, and talks about the pro and con.

## Slide 3: Recap of 11ax RU allocation subfield
The RU allocation subfield in 11ax spec is an 8-bit look-up table. Whilst it can also be indicated through Hierarchical Indication RU allocation signaling without referring to a 8-bit look-up table (15-1335r2)
52 reserved entries so far

## Slide 4: Feasibility of an 8-bit table for 11be
There was concern about an even bigger RU allocation table for 11be. This proposal wants to discuss the feasibility of an 8-bit table also for 11be.
Several aspects are considered:
  MU-MIMO support for small and big single RU/MRU respectively
  Number of entries needed if MU-MIMO is supported for MRU
  An high efficient way to support MU-MIMO for big MRU

## Slide 5: MU-MIMO support for single RU
For single RU, the number of entries needed for different size are shown below:
Considering the applicable scenario, the entries overhead and the benefits, it is proposed to keep 106-tone RU with up to 8 entries.
Single RU size | Number of entries needed |  | 
 | MU-MIMO with 8 entries | MU-MIMO with 16 entries | Gap
106 | 10*8 | 10*16 | 80
106+26+106 | 64 | 256 | 192
242, 484, 996, | 3*8 | 3*16 | 24
2*996 | 8 | 16 | 8
106 - 106 | Support up to 4 users per 106 so far to reduce number of entries, not considered to expand so far |  | 

## Slide 6: MU-MIMO support for single RU
For large RUs that are larger than 242-tone RU, two ways can be used for supporting up to 16 MU-MIMO users
  Opt1: 8 entries per RU allocation subfield: as 11ax, the number of MU-MIMO users is the sum of the user fields indicated in two RU allocation subfields within two CCs, for example:
    RU allocation subfield 1 indicates 484 (6) in CC1 and RU allocation subfield 2 indicates 484 (7) in CC2. The number of MU-MIMO users is 13 in the 484-tone RU.
    Pro: fewer number of entries needed
    Con: cannot support more than 8 MU-MIMO users for 242-tone RU; cannot support full flexibility regarding EHT-SIG CC load balance.
  Opt2: 16 entries per RU allocation subfield
    Pro: can support more than 8 MU-MIMO users for 242-tone RU, full flexibility regarding EHT-SIG CC load balance
    Con: larger number of entries needed
Considering the applicable scenario, the entries overhead and the benefits, it is preferred to have 8 entries (up to 16 users) for RUs that are larger than 242-tone RU. 242-tone RU case is open for discussion.

## Slide 7: MU-MIMO support for small MRU
For small MRUs, the number of entries needed for MRU are shown as follows:
MRU size | Number of entries needed |  | 
 | without MU-MIMO in both single RU and MRU | MU-MIMO with 8 entries | MU-MIMO with 16 entries
52+26 | 8 | 8 | 8
52+26 and 52+26 | 1 | 1 | 1
52+26 and 106 | 2 | 16 | 32
52+26 and 106+26 | 2 | 16 | 32
106+26 | 8 | 64 | 128
106+26 and 106 | 2 | 128 | 512
Total | 23 | 233 | 713

## Slide 8: MU-MIMO support for small MRU
Small MRU is an optional feature
ODFMA + MU-MIMO is an optional feature and seldom implemented.
OFDMA + MU-MIMO in 106-tone RU is even less attracting compared with OFDMA + MU-MIMO in large RU.
So supporting MU-MIMO for small MRU is trying to support an optional feature on top of another optional and seldom implemented feature.
  Can be simply replaced by doing MU-MIMO in 106-tone RU or 242-tone RU
Considering the applicable scenario, the entries overhead and the benefits, it is preferred to not support MU-MIMO for small RU when small MRU exists within one 242-tone RU.

## Slide 9: RU allocation subfield Entries for Small MRU
RU Allocation subfield ( B7 B6 B5 B4 B3 B2 B1 B0) | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
232 | 26 | 26 | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | 1
233 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 26 | 26 | 1
234 | 26 | 26+52 multi-RU |  |  | 26 | 26 | 26 | 52 |  | 1
235 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 26 | 26 | 1
236 | 26 | 26 | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | 1
237 | 26 | 26+52 multi-RU |  |  | 26 | 52+26 multi-RU |  |  | 26 | 1
238 | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
239 | 26 | 26+52 multi-RU |  |  | 26 | 52 |  | 52 |  | 1
240 | 52 |  | 26 | 26 | 26 | 52+26 multi-RU |  |  | 26 | 1
241 | 52 |  | 52 |  | 26 | 52+26 multi-RU |  |  | 26 | 1
242 | 26 | 26 | 26 | 26 | 26+106 multi-RU |  |  |  |  | 1
243 | 26 | 26+52 multi-RU |  |  | 26 | 106 |  |  |  | 1
244 | 26 | 26 | 52 |  | 26+106 multi-RU |  |  |  |  | 1
245 | 26 | 26+52 multi-RU |  |  | 26+106 multi-RU |  |  |  |  | 1
246 | 52 |  | 26 | 26 | 26 | 106 |  |  |  | 1
247 | 52 |  | 26 | 26 | 26+106 multi-RU |  |  |  |  | 1
248 | 52 |  | 52 |  | 26+106 multi-RU |  |  |  |  | 1
249 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 26 | 26 | 1
250 | 106+26 multi-RU |  |  |  |  | 26 | 26 | 52 |  | 1
251 | 106+26 multi-RU |  |  |  |  | 52 |  | 26 | 26 | 1
252 | 106 |  |  |  | 26 | 26+52 multi-RU |  |  | 26 | 1
253 | 106+26 multi-RU |  |  |  |  | 26+52 multi-RU |  |  | 26 | 1
254 | 106+26 multi-RU |  |  |  |  | 52 |  | 52 |  | 1
23 entries in total

## Slide 10: MU-MIMO support for large MRU
For large MRUs, the number of entries needed for MRU are shown as follows if assuming the exact MRU combinations can be indicated through a single RU allocation subfield:
MU-MIMO support can be more useful for large MRU compared with small MRU. It is preferred to support MU-MIMO for large MRU. Whilst the overhead is pretty big, which would lead to a larger table.
MRU size (OFDMA case) | Number of entries needed |  | 
 | without MU-MIMO in both single RU and MRU | MU-MIMO with 9 entries (including zero user fields) | MU-MIMO with 17 entries (including zero user fields)
242+484 | 4 | 36 | 68
484+996 | 4 | 36 | 68
3*996 | 4 | 36 | 68
Total | 12 | 108 | 204

## Slide 11: Large MRU indication with 9 entries
108 or 204 entries are consumed by large RU combinations shown in the previous slide assuming one RU allocation subfield itself is enough for the exact location of MRU.
An alternative way for large MRU indication was introduced in 400r0, which needs only 9 or 17 entries, only 1/12 overhead of the above cases.
192-199 | 242 | 8
200-207 | 484 | 8
208-215 | 996 | 8
216-223 | 2*996 | 8
224-231 | Belongs to an MRU; contributes 1~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 8
113 | 242-tone RU empty (with zero users) | 1
114 | 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
115 | 996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
116 | 2*996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
117 | Belongs to an MRU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
9 new entries for single RU 2*996
9 new entries for MRU

## Slide 12: Large MRU indication with 9 entries
The RU allocation subfields fall within any MRU combinations in an OFDMA transmission shall be set to one of the 9 values.
The Rx knows the location and size of the MRU by counting all the RU allocation subfields with the 9 values.
192-199 | 242 | 8
200-207 | 484 | 8
208-215 | 996 | 8
216-223 | 2*996 | 8
224-231 | Belongs to an MRU; contributes 1~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 8
113 | 242-tone RU empty (with zero users) | 1
114 | 484-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
115 | 996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
116 | 2*996-tone RU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
117 | Belongs to an MRU; contributes zero User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield | 1
11 reserved entries left: 118-119, 120-127, 255

## Slide 13: Some Examples
CC1 | else | N(1) | N(0) | N(0) | else | N(0) | else | else
CC2 | else | N(1) | N(0) | N(0) | N(1) | N(0) | else | else
  N(x) to indicate the newly added entries with x user fields. Different colors mean different combinations for large RU.
  After Reading all the RU allocation subfields of the same color, the STA knows the RUs of the same color are assigned
    484+996 has to be within one 160Mhz boundary
    242+484 has to be within one 80MHz boundary
Example A
Enhanced RU
allocation subfields
Example B
CC1 | else | N(1) | N(0) | N(0) | N(1) | N(0) | N(0) | N(0)
CC2 | else | N(1) | N(0) | N(0) | else | N(0) | N(1) | else
2 MU-MIMO users
1 user
2 MU-MIMO users
1 user
1 user

## Slide 14: Overhead Comparison and Analysis
  In 20-578r0, 20-715r0, 11ax style RU allocation has shown up to 50% efficiency gain regarding the number of EHT-SIG symbols.
  In 11be, the data rate can be 46.8 Gbps per link as shown in 19-754r0. The duration of the data part can be relatively short considering the latency requirement and traffic pattern. Correspondly, it is important to ensure a smaller number of EHT-SIG symbols.
  In 20-575r0, it has been shown the overhead for 11ax style RU allocation is larger when number of users in the PPDU is small mainly due to the overhead of the common field. Whilst several members show interests to further reduce the overhead of the common field.
  Regarding implementation complexity of 11ax style RU allocation, since 11ax has already implemented it, it is straightforward for 11be to further implement it.

## Slide 15
Feasibility of an 8-bit table for 11be is proved in this proposal.
  52 reserved entries in 11ax. Among them, 23 are used for small MRU, 9 for 2*996 single RU, 9 for large MRU. 11 reserved entries are for other purposes.
The proposal analyzes the tradeoff between supporting MU-MIMO for different RU sizes. The proposed method enables MU-MIMO for MRU with only 9 few entries.
Summary

## Slide 16: Straw Poll #1
Do you agree to add the following to the 11be SFD:
  An RU Allocation subfield that is present in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users, indicates RU assignment, including the size of the RU(s) and their placement in the frequency domain, to be used in the EHT modulated fields of the PPDU in the frequency domain.
    Compressed modes are TBD.
  Yes/No/Abstain

## Slide 17: Discussion regarding SP1
Note in 11ax specs, we have the following description:
  Each RU Allocation subfield in an HE-SIG-B content channel corresponding to a 20 MHz frequency segment indicates the RU assignment, including the size of the RU(s) and their placement in the frequency domain, to be used in the HE modulated fields of the HE MU PPDU in the frequency domain, also indicates information needed to compute the number of users allocated to each RU, where the subcarrier indices of the RU(s) meet the conditions in Table 27-25 (RUs associated with each RU Allocation subfield for each HESIGB content channel and PPDU bandwidth).
We also have the following passed motion in 11be:
  An RU Allocation subfield is present in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users.
    Compressed modes are TBD.
    Contents of the RU Allocation subfield are TBD.
  [Motion 57, [9] and [25]]

## Slide 18: SP2
Do you agree that the mapping from the TBD-bit RU Allocation subfield to the RU assignment, contains the following entries:
  The RUs highlighted in orange means combination.
Table XX - RU Allocation subfield
order | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
TBD | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
TBD | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
TBD | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 26 | 26 | 26 | 52 |  | 52 |  | 1
TBD | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
TBD | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
TBD | 52 |  | 26 | 26 | 26 | 26 | 26 | 26 | 26 | 1
TBD | 52 |  | 26 | 26 | 26 | 26 | 26 | 52 |  | 1
TBD | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
TBD | 52 |  | 26 | 26 | 26 | 52 |  | 52 |  | 1
TBD | 52 |  | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
TBD | 52 |  | 52 |  | 26 | 26 | 26 | 52 |  | 1
TBD | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
TBD | 52 |  | 52 |  | 26 | 52 |  | 52 |  | 1
TBD | 52 |  | 52 |  | -- | 106 |  |  |  | TBD
TBD | 106 |  |  |  | -- | 52 |  | 52 |  | TBD
TBD | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | TBD
TBD | 26 | 26 | 52 |  | 26 | 106 |  |  |  | TBD
TBD | 52 |  | 26 | 26 | 26 | 106 |  |  |  | TBD
TBD | 52 |  | 52 |  | 26 | 106 |  |  |  | TBD
TBD | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | TBD
TBD | 106 |  |  |  | 26 | 26 | 26 | 52 |  | TBD
TBD | 106 |  |  |  | 26 | 52 |  | 26 | 26 | TBD
TBD | 106 |  |  |  | 26 | 52 |  | 52 |  | TBD
TBD | 106 |  |  |  | -- | 106 |  |  |  | TBD
TBD | 52 |  | 52 |  | -- | 52 |  | 52 |  | 1
TBD | 242-tone RU empty (with zero users) |  |  |  |  |  |  |  |  | 1
TBD | 106 |  |  |  | 26 | 106 |  |  |  | TBD
TBD | 242 |  |  |  |  |  |  |  |  | TBD
TBD | 484 |  |  |  |  |  |  |  |  | TBD
TBD | 996 |  |  |  |  |  |  |  |  | TBD
TBD | 2*996 |  |  |  |  |  |  |  |  | TBD
order | #1 | #2 | #3 | #4 | #5 | #6 | #7 | #8 | #9 | Number of entries
TBD | 26 | 26 | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 26 | 26 | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 26 | 26 | 52 |  | 1
TBD | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 52 |  | 26 | 52 |  | 52 |  | 1
TBD | 52 |  | 26 | 26 | 26 | 52 |  | 26 | 26 | 1
TBD | 52 |  | 52 |  | 26 | 52 |  | 26 | 26 | 1
TBD | 26 | 26 | 26 | 26 | 26 | 106 |  |  |  | TBD
TBD | 26 | 26 | 52 |  | 26 | 106 |  |  |  | 1
TBD | 26 | 26 | 52 |  | 26 | 106 |  |  |  | TBD
TBD | 26 | 26 | 52 |  | 26 | 106 |  |  |  | TBD
TBD | 52 |  | 26 | 26 | 26 | 106 |  |  |  | TBD
TBD | 52 |  | 52 |  | 26 | 106 |  |  |  | TBD
TBD | 106 |  |  |  | 26 | 26 | 26 | 26 | 26 | TBD
TBD | 106 |  |  |  | 26 | 26 | 26 | 52 |  | TBD
TBD | 106 |  |  |  | 26 | 52 |  | 26 | 26 | TBD
TBD | 106 |  |  |  | 26 | 52 |  | 26 | 26 | 1
TBD | 106 |  |  |  | 26 | 52 |  | 26 | 26 | TBD
TBD | 106 |  |  |  | 26 | 52 |  | 52 |  | TBD
TBD | 106 |  |  |  | 26 | 106 |  |  |  | TBD
TBD | 106 |  |  |  | 26 | 106 |  |  |  | TBD
Cont’d

## Slide 19: Discussion regarding SP2
Discussion:
  Now there is argument regarding MU-MIMO support for 106-tone RU, 132-tone RU, number of entries for MU-MIMO support (8 or 16), large MRU indication method. The entries in the table now try to avoid those controversial parts.

## Slide 20: Straw Poll #3
Do you agree that when MRU exists within a 242-tone RU range, MU-MIMO shall not be supported within the 242-tone RU range?

## Slide 21: Straw Poll #4
Do you agree that when no MRU exists within a 242-tone RU range, if there exists one or two 106-tone RU within the 242-tone RU range, up to 8 MU-MIMO users is supported within one 106-tone RU?
  Yes/No/Abstain

## Slide 22: Straw Poll #5
Do you agree that for RU484 or RU996, in the RU allocation table, 9 entries per RU size will be used to indicate: contributes 0~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield?
  Yes/No/Abstain

## Slide 23: Straw Poll #6
Do you agree that for RU 2*996, in the RU allocation table, 9 entries per RU size will be used to indicate: contributes 0~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield?
  Yes/No/Abstain

## Slide 24: Straw Poll #7
Do you agree that for RU242, in the RU allocation table, 9 entries per RU size will be used to indicate: contributes 0~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield?
  Yes/No/Abstain

## Slide 25: Straw Poll #8
Do you agree that for large multi-RU, 9 entries will be used to indicate: belongs to an MRU, contributes 0~8 User fields to the User Specific field in the same EHT-SIG content channel as this RU Allocation subfield?
  Yes/No/Abstain

## Slide 26: Straw Poll #9
Do you agree that one RU allocation subfield is 8 bit in the common field of an EHT-SIG for single RU and multi-RU indication in a DL OFDMA transmission?
  Yes/No/Abstain

## Slide 27
https://mentor.ieee.org/802.11/dcn/20/11-20-0578-00-00be-on-ru-allocation-singling-in-eht-sig.pptx (Jianhan Liu, Mediatek)
https://mentor.ieee.org/802.11/dcn/20/11-20-0373-01-00be-ru-allocation-subfield-design-for-multi-ru-support.pptx (Myeongjin Kim, Samsung)
https://mentor.ieee.org/802.11/dcn/20/11-20-0403-00-00be-signaling-of-multiple-ru-aggregation-in-ofdma.pptx (Dongguk Lim, LGE)
https://mentor.ieee.org/802.11/dcn/20/11-20-0400-00-00be-multi-ru-combination-and-signaling-for-ofdma-transmission.pptx (Mengshi Hu, Huawei)
https://mentor.ieee.org/802.11/dcn/15/11-15-1335-02-00ax-he-sig-b-contents.pptx (Le Liu, Huawei)
https://mentor.ieee.org/802.11/dcn/20/11-20-0715-00-00be-overhead-comparisons-of-eht-sig.pptx (Myeongjin Kim, Samsung)
References