## Slide 1: AP assisted Non-STR behavior
Date: 2020-04-01
Authors:

## Slide 2: Background
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can only do Tx/Tx or Rx/Rx on all links)
Problem statement
  When the Non-STR STA MLD finishes its transmission on the first link, what should a STA belong to the same MLD do on the second link given that this STA has been deaf on that second link?
  This problem is similar to what a STA changing from doze state to awake state meets.
STA 1
STA 2
Non-STR MLD
Packet
CCA busy
Deaf period
???
Link 1
Link 2

## Slide 3: Background
In 802.11-2016 Spec, a STA shall follow the rule below:
  A STA that is changing from doze to awake state in order to transmit shall perform CCA until a frame is detected by which it can set its NAV, or until a period of time indicated by the NAVSyncDelay from the MLME-JOIN.request primitive has transpired.
The above rule is to first have the STA synchronized to the medium and then access the channel in order to prevent potential collisions with transmissions from hidden nodes
STA1 hidden from STA2
Data
Ack
STA1
AP
STA2
STA2:Doze to Awake
NAVSyncDelay = Max PPDU+SIFS+BA (or ACK)
STA2 detects transmission in the channel
(synched with the activities in the channel)
Data
Ack
STA2 cannot hear STA1’s transmission
AP
STA 2
STA 1

## Slide 4: NAVSyncDelay
NAVSyncDelay is proposed to address hidden node problem, and also could be applied for the STA in a Non-STR MLD
  Because of the same application scenario-missing channel state info
  However, AP MLD could assist the STA in Non-STR MLD to access the channel quickly as mentioned in reference [1]
  Assume that AP MLD is STR , and all the APs in the AP MLD could the sense the channel simultaneously
  The AP MLD could exactly know when the STA in Non-STR MLD intends to access the channel, which is different from the existing power save scenario
Ack
Other STA
AP
STA2 in non-STR MLD
STA2 Intends to tx packet
NAVSyncDealy
STA2 detects transmission
(synch with the activities in the channel)
STA2 cannot hear other STA’s transmission
Case 1 for link 2
Data
Data
Case 2 for link 2
Backoff is pending although the channel is idle.
Other STA
AP
NAVSyncDealy
STA2 stays awake
STA2 Intends to tx packet
STA2 in non-STR MLD
Data

## Slide 5: Recap
In reference [1], it provides 3 options to address it
Opt 1: use countdown_prohibit timer like NAVSync Delay what we have for the STA in power save mode
  Fixed time will waste spectrum resource when the second link is idle
Opt 2: Lower ED level (-82dBm)
  Can not address the issue-miss NAV info in the second link
  False alarm issue
Opt 3: Cross-Link NAV sent by AP MLD in one link for another link
  A fancy design, need to change the change existing frame format, such as BA
  Asymmetric NAV info between AP and STA, it could be ignored because it is not typical case

## Slide 6: AP assisted Non-STR behavior
We propose that AP MLD assists the STA in a Non-STR MLD to access the channel when the channel is idle
  AP 2 sends a short frame to the STA 2 in the Non-STR MLD when it receives the request from STA 1
  TBD for short frame
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Short frame
Data
Change to link 2
BA
BA
Data
Other STA
AP2
Link 2
No transmission

## Slide 7: AP assisted Non-STR behavior
We propose that AP MLD does nothing when the channel is busy as long as busy time beyond the NAVSyncDelay
  The STA 2 in a non-STR MLD reuses NAVSyncDelay to access the channel
  Or the frame sent in the link 2 sets STA 2’s NAV
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Data
Change to link 2
BA
BA
Data
Other STA
AP2
Link 2
Data
BA
NAVSyncDelay or NAV

## Slide 8: Summary
We propose that the AP in MLD assists the STA in Non-STR MLD to access the channel
  The AP in MLD sends a short frame to the STA in the Non-STR MLD when the channel is idle
  The STA in a non-STR MLD reuses NAVSyncDelay to access the channel when the channel is busy

## Slide 9: References
[1] IEEE 802.11-20/0444r1 MLA non-STR STA EDCA rules after self interference

## Slide 10: SP 1
Do you support that if during a PPDU transmission of a STA (STA 1) of a non-STR non-AP MLD to an AP (AP 1) of the AP MLD, another STA (STA 2) of the same non-AP MLD cannot detect its medium state when required and starts a NAVSyncDelay timer count down at the end of the PPDU transmission, another AP (AP 2) of the same AP MLD shall send a short frame to the STA-2 if the channel is idle, NAVSyncDelay timer is not 0 and the PPDU carries a signal which indicates the STA2 intends to send the uplink frame(s).