## Slide 1: AP assisted Non-STR behavior
Date: 2020-04-01
Authors:

## Slide 2: Background
Non-STR
  An MLD that is not capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can only do Tx/Tx or Rx/Rx on all links)
Problem statement
  When the Non-STR STA MLD finishes its transmission on the first link, what should a STA belong to the same MLD do on the second link given that this STA has been deaf on that second link?
  This problem is similar to what a STA changing from doze state to awake state meets.
STA 1
STA 2
Non-STR MLD
Packet
CCA busy
Deaf period
???
Link 1
Link 2

## Slide 3: Background
In 802.11-2016 Spec, a STA shall follow the rule below:
  A STA that is changing from doze to awake state in order to transmit shall perform CCA until a frame is detected by which it can set its NAV, or until a period of time indicated by the NAVSyncDelay from the MLME-JOIN.request primitive has transpired.
The above rule is to first have the STA synchronized to the medium and then access the channel in order to prevent potential collisions with transmissions from hidden nodes
STA1 hidden from STA2
Data
Ack
STA1
AP
STA2
STA2:Doze to Awake
NAVSyncDelay = Max PPDU+SIFS+BA (or ACK)
STA2 detects transmission in the channel
(synched with the activities in the channel)
Data
Ack
STA2 cannot hear STA1’s transmission
AP
STA 2
STA 1

## Slide 4: NAVSyncDelay
NAVSyncDelay is proposed to address hidden node problem, and also could be applied for the STA in a Non-STR MLD
  Because of the same application scenario-missing channel state info
  However, AP MLD could assist the STA in Non-STR MLD to access the channel quickly as mentioned in reference [1]
  Assume that AP MLD is STR , and all the APs in the AP MLD could the sense the channel simultaneously
  The AP MLD could exactly know when the STA in Non-STR MLD intends to access the channel, which is different from the existing power save scenario
Ack
Other STA
AP
STA2 in non-STR MLD
STA2 Intends to tx packet
NAVSyncDealy
STA2 detects transmission
(synch with the activities in the channel)
STA2 cannot hear other STA’s transmission
Case 1 for link 2
Data
Data
Case 2 for link 2
Backoff is pending although the channel is idle.
Other STA
AP
NAVSyncDealy
STA2 stays awake
STA2 Intends to tx packet
STA2 in non-STR MLD
Data

## Slide 5: Recap
In reference [1], it provides 3 options to address it
Opt 1: use countdown_prohibit timer like NAVSync Delay what we have for the STA in power save mode
  Fixed time will waste spectrum resource when the second link is idle
Opt 2: Lower ED level (-82dBm)
  Can not address the issue-miss NAV info in the second link
  False alarm issue
Opt 3: Cross-Link NAV sent by AP MLD in one link for another link
  A fancy design, need to change the change existing frame format, such as BA
  Asymmetric NAV info between AP and STA, it could be ignored because it is not typical case

## Slide 6: AP assisted Non-STR behavior
We propose that AP MLD assists the STA in a Non-STR MLD to access the channel when the channel is idle
  AP 2 sends a short frame to the STA 2 in the Non-STR MLD when it receives the request from STA 1
  TBD for short frame
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Short frame
Data
Change to link 2
BA
BA
Data
Other STA
AP2
Link 2
No transmission

## Slide 7: AP assisted Non-STR behavior
We propose that AP MLD does nothing when the channel is busy as long as busy time beyond the NAVSyncDelay
  The STA 2 in a non-STR MLD reuses NAVSyncDelay to access the channel
  Or the frame sent in the link 2 sets STA 2’s NAV
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Data
Change to link 2
BA
BA
Data
Other STA
AP2
Link 2
Data
BA
NAVSyncDelay or NAV

## Slide 8: Summary
We propose that the AP in MLD assists the STA in Non-STR MLD to access the channel
  The AP in MLD sends a short frame to the STA in the Non-STR MLD when the channel is idle
  The STA in a non-STR MLD reuses NAVSyncDelay to access the channel when the channel is busy

## Slide 9: References
[1] IEEE 802.11-20/0444r1 MLA non-STR STA EDCA rules after self interference
[2]11-20-1009-09-00be-multi-link-hidden-terminal-followup

## Slide 10: SP 1
Do you agree to add to 11be SFD in R1: If a STA (STA-2) of a non-STR non-AP MLD experiences a loss of medium synchronization due to transmission by another STA (STA-1) within the same MLD) and starts a MediumSyncDelay timer, then while the MediumSyncDelay timer of STA-2 is running:
  The STA may attempt to initiate up to MSD_TXOP_MAX TxOPs using EDCA. The STA is only allowed to attempt to initiate up to number of TxOPs assigned by the AP (at least 1) and shall attempt to initiate that TxOP with the transmission of an RTS frame using regular EDCA backoff and baseline CCA but a TBD ED threshold value
    The value of MSD_TXOP_MAX is assigned by the AP and shall be at least 1.
    TXOP attempts shall begin with an RTS frame
    If the channel was busy immediately after the blind period, additional TBD rules to transmit the RTS may apply.
  A special ED threshold shall be used by the STA. The value of this ED threshold is TBD
    The TBD ED threshold value has a default value specified in the spec (e.g., -62dBm) but can also be assigned by the AP MLD within a limited range such as between -82dBm and -62dBm
  If the PPDU transmitted by STA 1 carries a signal (Signaling is TBD) which indicates that STA 2 intends to send UL frame after transmission from STA-1 then another AP (AP 2) of the same AP MLD should send a Trigger frame to STA-2 soliciting UL PPDU if the channel is idle and the AP2 does not have frame exchange already scheduled with another STA
Note:
  If either the intra-BSS NAV or the inter-BSS NAV is non-zero in STA-2 at the end of transmission of STA-1, STA-2 does not transmit any PPDU using EDCA until the NAV expires.
  If either the intra-BSS NAV or the inter-BSS NAV is non-zero in STA-2 at the end of transmission of STA-1, there could be further TBD conditions and requirements to expire the MediumSyncDelay timer.

## Slide 11: SP 1A
Do you agree to add to 11be SFD R1: if during a transmission of a STA (STA-1) of a non-STR non-AP MLD, another STA (STA-2) of the same MLD cannot detect its medium state when required (due to STA-1’s UL transmission interference), STA-2 shall start a MediumSyncDelay timer at the end of STA-1’s transmission, unless the STA-2 ended a transmission at the same time. While the MediumSyncDelay timer is running,
  The STA is only allowed to attempt to initiate up to number of TxOPs assigned by the AP (at least 1) and shall attempt to initiate that TxOP with the transmission of an RTS frame using regular EDCA backoff and baseline CCA but a TBD ED threshold value
    The TBD ED threshold value has a default value specified in the spec (e.g., -62dBm) but can also be assigned by the AP MLD within a limited range such as between -82dBm and -62dBm
    If the channel was busy immediately after the blind period, additional TBD rules to use RTS may apply.
    It is optional for the STA to initiate a TXOP while the timer is running
  If the PPDU transmitted by STA 1 carries a signal (Signaling is TBD) which indicates that STA 2 intends to send UL frame after transmission from STA-1 then another AP (AP 2) of the same AP MLD should send a Trigger frame to STA-2 soliciting UL PPDU if the channel is idle, MediumSyncDelay timer is not 0 and if the AP2 does not have frame exchange already scheduled with another STA
Note:
  If either the intra-BSS NAV or the inter-BSS NAV is non-zero in STA-2 at the end of transmission of STA-1, STA-2 does not transmit any PPDU using EDCA until the NAV expires.
  If either the intra-BSS NAV or the inter-BSS NAV is non-zero in STA-2 at the end of transmission of STA-1, there could be further TBD conditions and requirements to expire the MediumSyncDelay timer.

## Slide 12: Blindness topic analysis

## Slide 13: Blindness
Problem statement
  During the first transmission on link 1 from STA 1 in the Non-STR non-AP MLD, the channel status is unknown by the STA2 in the same non-AP MLD. It is deaf period
  This problem is similar to what a STA changing from doze state to awake state meets.
STA 1
STA 2
Non-STR MLD
Packet
CCA busy
Deaf period
???
Link 1
Link 2
AP 1
AP 2
AP MLD
STA1
AP1
STA2
AP2

## Slide 14: Two cases
Case 1: During the NAVSync period, there is a frame from other STA on link 2, i.e., at the beginning
  In this case, this frame could set the NAV for STA2
  Both STA adhoc and AP assistance are not needed
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Data frame
Data
Change to link 2
BA
BA
Data
Other STA
AP2
Link 2
NAVSyncDelay

## Slide 15: Two cases
Case 2: During the NAVSync delay period, there is no frame from other STA which could be detected by STA 2
  There are two possibilities: 1. no frame on link 2; 2. a frame sent by the other STA which is hidden from STA 2. However, this two possibilities can not be distinguished by STA2, so STA 2 has to keep silence during NAVSync delay (baseline)
  However, STA adhoc channel access [2] during NAVsync delay period may cause collision with its hidden node (no matter what ED level it uses because it can not be aware that frame)
  On the other hand, AP assistance (in this contribution) can address this issue since that other STA is not hidden from AP
  If there is frame sent by the other STA which is hidden from STA 2, AP will not send the short frame
  If there is no frame sent by the other STA which is hidden from STA 2, AP will send the short frame such that to make full use of the idle time during the NAVSync Delay period
AP 1
STA 1
AP 2
STA 2
AP MLD
Non-AP MLD
Link 1
STA1
AP1
STA2
AP2
Link 2
Data frame
Data
Change to link 2
BA
BA
Data
2: Other STA，hidden from STA 2
AP2
Link 2
NAVSyncDelay
1: No frame
Link 2
AP2

## Slide 16: Backup
Do you support that in R1:
  a PPDU transmission of a STA (STA 1) of a non-STR non-AP MLD to an AP (AP 1) of the AP MLD carries a signal which indicates that another STA (STA 2) of the same non-AP MLD, that cannot detect its medium state when required, intends to send uplink frame after transmission from STA-1
    Signal is TBD.
  another AP (AP 2) of the same AP MLD should send a short Trigger frame to the STA-2 soliciting UL PPDU if the channel is idle, MediumSyncDelay timer is not 0 and if the AP2 does not have frame exchange already scheduled with another STA