## Slide 1: Multi-AP Operation - Basic Definition
Date: 2020-04-16
Authors:
Name | Affiliations | Address | Email
Oren Kedem | Huawei | Israel | oren.kedem@huawei.com
Boyce Bo Yang |  | Nanjing, China | yangbo59@huawei.com
Lily Yunping Lyu |  | Nanjing, China | lvyunping@huawei.com
Notes: September 2012

## Slide 2: Introduction
Multi-AP operation is one of the EHT key features and has been discussed in many contributions
Most of the Multi-AP contributions pointed on several similar roles and groups that are required for Multi-AP Operation.
Nevertheless, SFD is still missing several basic definitions with respect to Multi-AP feature.
This contribution consolidates the common basic definitions that are involved in Multi-AP operation and set a unified terminology.

## Slide 3: Multi-AP Operation Groups
[2] [3] [9] discussed the need for “Multi-AP Set”, “Candidate Set” and “Multi-AP Group formation”.
[6] Explained the need for Static and Dynamic Multi-AP Group
Definition of two groups is required:
  Multi-AP Candidate Set
  Multi-AP Operation Set

## Slide 4: Multi-AP Candidate Set (M-AP-CS)
Multi-AP Candidate Set (M-AP-CS) is established by a Coordinator AP and contain the following participants:
  The Coordinator AP
  One or more Coordinated AP(s) that has a reliable link with the Coordinator AP
  Coordinator AP and Coordinated AP(s) associated STA’s who are targeted to participate in Multi-AP Operation procedures.
  Note: Reliable link definition is TBD
M-AP-CS information is maintained by the Coordinator AP.
Coordinator AP may trigger the establishment of the M-AP-CS by the following means:
  Broadcast Announcement that contains the Coordinator AP capabilities and a request to form M-AP-CS group.
  Unicast requests sent to Coordinated AP’s
M-AP-CS includes all AP & STA that can coordinate with Coordinator AP

## Slide 5: Multi-AP Operation Set (M-AP-OS)
Multi-AP Operation Set (M-AP-OS) is a dynamic sub group of M-AP-CS and include the following participants:
  The Sharing AP who obtained TXOP to be utilized for Multi-AP Transmission
  Shared AP(s) and STA(s) that participate in the upcoming Multi-AP Transmission.
NOTE: M-AP-CS and M-AP-OS does not preclude joint transmissions by multiple AP(s) in the group and enable JT/CBF/OFDMA/TDMA or any other Multi-AP operation method discussed in the group
M-AP-OS includes all AP & STA that participate in the upcoming coordinated transmission shared by Sharing AP

## Slide 6: Roles definitions in Coordinated Multi-AP Operation
Coordinator AP
  An EHT AP that supports Multi-AP Operation capability and established Multi-AP Candidate Set is defined as Coordinator AP for that M-AP-CS.
  Note: AP may act as a Coordinator AP in one M-AP-CS group.
Coordinated AP
  An EHT AP that that supports Multi-AP Operation capability and has joined a M-AP-CS is defined as Coordinated AP in that M-AP-CS.
  Note: AP may act as a Coordinated AP in several M-AP-CS groups
Sharing AP (already in SFD)
  An EHT AP which obtains a TXOP and initiates the Multi-AP coordination.
  An EHT AP in which the frequency and time synchronization during Multi-AP coordinated transmission is synchronized to.
Shared AP (already in SFD)
  An EHT AP which is coordinated for the Multi-AP transmission by the Sharing AP
  An EHT AP that synchronizes to the frequency and time of the Sharing AP during Multi-AP coordinated transmission.
Note: If Sharing AP is coordinator AP or could be any AP in M-AP-CS is TBD

## Slide 7: Multi-AP Operation Procedure
[7] [10] [1] Discussed the Multi-AP Coordination Procedure and Multi-AP Coordinated Transmission.
[4] Introduced the setup procedure intended to form Multi-AP Coordination group
General definition of the Multi-AP Operation Procedure is required.

## Slide 8: Multi-AP Operation Procedures
Multi-AP Operation Procedures is composed of three stages:
Multi-AP Setup - Initiated by the Coordinator AP to establish Multi-AP Candidate Set with nearby Coordinated AP. Multi-AP Setup may includes the exchange of AP capabilities, participating STA, resource sharing etc.
Multi-AP Coordination – Initiated by the Sharing AP and Shared AP to form a Multi-AP Operation Set and involves with exchange of the upcoming Multi-AP Transmission characteristics.
Multi-AP Transmission - A coordinated transmission within the TXOP was obtained by the Sharing AP with the Shared AP(s) to a group of STA(s).

## Slide 9: Multi-AP Operation Procedure
Given as an example of functions may be used in a coordinated scheme when required (e.g. JT or CBF)

## Slide 10: Examples for M-AP-CS and M-AP-OS
AP1 forms M-AP-CS with AP2 and AP3
M-AP-CS [A]= [AP1(Ctor), AP2(Cnted), AP3(Cnted)]
M-AP-OS groups that can be formed during operations are:
  M-AP-OS [A]= [AP1(Sharing), AP2(Shared), AP3(Shared)]
  M-AP-OS [B]= [AP1(Sharing), AP2(Shared)]
  M-AP-OS [C]= [AP1(Sharing), AP3(Shared)]
AP2 forms M-AP-CS with AP1
M-AP-CS [B]= [AP2(Ctor), AP1(Cnted)]
M-AP-OS group can be formed during operations is:
  M-AP-OS [B]= [AP2(Sharing), AP1(Shared)]
AP3 forms M-AP-CS with AP1
M-AP-CS [C]= [AP3(Ctor), AP1(Cnted)]
M-AP-OS group can be formed during operations is:
  M-AP-OS [C]= [AP3(Sharing), AP1(Shared)]
An example of Multi-AP Setup stage
AP1 sends request to AP2/AP3 for joint coordination agreement:
AP1 adds AP2 and AP3 to M-AP-CS [A]= [AP1(Ctor), AP2(Cnted), AP3(Cnted)]
In return, AP2 adds AP1 to M-AP-CS [B]= [AP2(Ctor), AP1(Cnted)]
In return, AP3 adds AP1 to M-AP-CS [C]= [AP3(Ctor), AP1(Cnted)]

## Slide 11: Straw Poll 1
Which of the options do you prefer with regards to Multi-AP set definition?
  Option 1 – One Static group “Multi-AP Candidate Set”
  Option 2 – Two groups, one static “Multi-AP Candidate Set” and one Dynamic group “Multi-AP Operation/Active Set”
 | Option 1 | Option 2 | 
 | Cheng (DCN596) | Oren (DCN617) | Yonggang (DCN1961)
Static Group |  |  | 
Name | Coordinated AP Set | AP Candidate Set | AP Candidate Set
Definition | Trusted boundary of coordinated AP operations in the management domain | AP’s within the Sharing AP coverage area and can coordinate | A set of APs are formed statically within a coverage area, and can discover each other, establish a connection and share the frequency and time resources
Method of Establishment | External Coordinator or user configuration setting | Group is formed Per-AP and by the AP via negotiations with other APs | The AP candidate set is static and established by the configuration from the management entity
Dependencies | None | Reliable link between APs in the set | Wired or Wireless link between the APs in the set
Dynamic Group |  |  | 
Name | None | AP Operation Set | Multi-AP Active Set
Definition | N/A | Subset of the AP Candidate set and includes all AP & STA that participate in the upcoming coordinated transmission shared by Sharing AP | A subset of the multi-AP candidate set, formed dynamically to communicate to a STA or a group of STAs within a TXOP.
Method of Establishment |  | Established by the Sharing AP based on its associated STA's feedback about the neighbor APs in the coverage area | Established by the AP based on its associated STA's feedback about the neighbor APs in the coverage area

## Slide 12: Straw Poll 2
Do you agree that SFD will include the following Multi-AP definitions as defined in this contribution:
Option A: All definitions (roles, groups and procedures)
Option B: Only Multi-AP roles and groups definitions
  Coordinator AP, Coordinated AP
  Multi-AP Candidate Set (M-AP-CS)
  Multi-AP Operation Set (M-AP-OS)
Option C: None
Option D: Abstain

## Slide 13: Straw Poll 3
Do you agree that SFD will include the definition of Coordinator/Coordinated AP and modifications of Sharing/Shared AP as follow:
Coordinator AP
  An EHT AP that supports Multi-AP Operation capability and established Multi-AP Candidate Set (M-AP-CS) is defined as Coordinator AP for that M-AP-CS.
  Note: AP may act as a Coordinator AP in one M-AP-CS group.
Coordinated AP
  An EHT AP that that supports Multi-AP Operation capability and has joined a M-AP-CS is defined as Coordinated AP in that M-AP-CS.
  Note: AP may act as a Coordinated AP in several M-AP-CS groups
Sharing AP
  An EHT AP which obtains a TXOP and initiates the Multi-AP coordination.
  An EHT AP in which the frequency and time synchronization during Multi-AP coordinated transmission is synchronized to.
Shared AP
  An EHT AP which is coordinated for the Multi-AP transmission by the Sharing AP
  An EHT AP that synchronizes to the frequency and time of the Sharing AP during Multi-AP coordinated transmission.

## Slide 14: Straw Poll 4
Do you agree that SFD will include the definitions of Multi-AP Candidate Set (M-AP-CS) and Multi-AP Operation Set (M-AP-OS) as follow:
Multi-AP Candidate Set (M-AP-CS) is established by a Coordinator AP and contains the following participants:
  The Coordinator AP
  One or more Coordinated AP(s) that has a reliable link with the Coordinator AP
  Coordinator AP and Coordinated AP(s) associated STA’s who are targeted to participate in Multi-AP Operation procedures.
  Note: Reliable link definition is TBD.
Multi-AP Operation Set (M-AP-OS) is a dynamic sub group of M-AP-CS and include the following participants:
  The Sharing AP who obtained TXOP to be utilized for Multi-AP Transmission
  Shared AP(s) and STA(s) that participate in the upcoming Multi-AP Transmission.

## Slide 15: Straw Poll 5
Do you agree that SFD will include the definition of Multi-AP Operation Procedure stages which includes Multi-AP Setup, Multi-AP Coordination and Multi-AP Transmission as follow:
Multi-AP Operation Procedures is composed of three stages:
Multi-AP Setup - Initiated by the Coordinator AP to establish Multi-AP Candidate Set with nearby Coordinated AP. Multi-AP Setup may includes the exchange of AP capabilities, participating STA, resource sharing etc.
Multi-AP Coordination – Initiated by the Sharing AP and Shared AP to form a Multi-AP Operation Set and to exchange the characteristics of upcoming Multi-AP Transmission.
Multi-AP Transmission - A coordinated transmission within the TXOP was obtained by the Sharing AP with the Shared AP(s) to a group of STA(s).

## Slide 16: References
[1] 11-19-1102-00-00be-a-unified-transmission-procedure-for-multi-ap-coordination
[2] 11-19-1931-02-00be-multi-ap-group-formation-follow-up
[3] 11-19-1616-01-00be-multi-ap-group-formation
[4] 11-19-1895-01-00be-setup-for-multi-ap-coordination
[5] 11-19-1129-01-00be-consideration-on-multi-ap-coordination
[6] 11-19-1961-02-00be-multi-ap-group-establishment
[7] 11-19-1582-02-00be-c-ap-time-and-frequency-sharing-in-a-transmit-opportunity-in-11be
[8] 11-20-0107-00-00be-multi-ap-coordination-for-spatial-reuse
[9] 11-20-0277-00-00be-coordinated-ofdma-protocol
[10] 11-20-0064-01-00be-overview-of-multi-ap-operation-in-11be

## Slide 17: Backup

## Slide 18: M-AP-CS and Anchor Coordinator
M-AP-CS definition is aligned with the existence of Anchor Coordinator
M-AP-CS could be also configured by Anchor Coordinator that acquire a full view of the network
  Anchor Coordinator collects network and channel status information from all nearby AP(s)
  Anchor Coordinator configure each of the AP with M-AP-CS
AP1
AP2
Channel
Measurements
Anchor Coordinator
Channel
Measurements
AP3
Channel
Measurements
AP1
AP2
M-AP-CS Configuration
Anchor Coordinator
AP3
M-AP-CS Configuration
M-AP-CS Configuration
Step 1
Step 2

## Slide 19: Considerations to include STA(s) in the M-AP-CS?
Coordinator AP may need to know the actual CSI of the participating STAs In case of “Multi-AP Joint Transmission” or “Interference Nulling” coordinated procedures
In some implementations, Coordinator AP may run adaptive radio or AI processing to initiate the next Multi-AP Coordination hence may benefit the information of participating STAs and their radio characteristics (e.g. M-AP TX success/failure statistics, path-loss, STA location, buffer status etc)