## Slide 1: Further Thoughts on EHT-LTF PAPR in 802.11be
Date: 13-04-2020
Authors:

## Slide 2: Introduction
The PAPR topic was discussed in several 11be contributions, some of which were focused on puncturing cases and solutions for the entire BW [1], [2]
In [3] we examined the PAPR aspect of EHT-LTF field in cases of an MRU and compared between several solutions that minimize the PAPR
Following the discussions that took place during the presentation of [3] we would like to provide clarifications and also to extend the discussion on PAPR aspects for additional scenarios (not only Multi-RU)
We recap here the main technical details that were discussed in [3] and also add a more extended view of the PAPR problem
In this contribution we suggest a solution that may be applied on top of EHT-LTF sequence to minimize PAPR in specific scenarios (the results are based on EHT-LTF produced by reusing HE-LTF for BW ≤ 160MHz)

## Slide 3: Recap – Main Issues
In [3] we studied MRU scenarios, where the transmitted signal contains multiple frequency segments, and showed that there is an impact on the PAPR of EHT-LTF in some cases
We also compared between PAPR of EHT-LTF field and data portion and showed that the gap between data portion and EHT-LTF field is smaller than it is in 11ax cases
We showed that such smaller gap may cause PER degradation (we applied the RAPP model for PA nonlinearity)
During the review of potential solutions, we highlighted the issue that a single (or small number of) EHT-LTF sequence cannot yield minimization of PAPR in all MRU cases due to an abundance of scenarios and combinations
We suggested to apply a linear phase with constant phase offset where the phase values are selected per scenario (e.g. MRU combination)
Time

## Slide 4: Recap - Impact on PAPR
We showed that there is an impact on PAPR of EHT-LTF up to 2.5-3dB in most of the scenarios
This increase can be explained by a superposition of multiple waveforms which increase the probability of higher peaks to be created

## Slide 5: Recap – Impact of PAPR on Performance
We also showed the impact on data portion PAPR (less than 0.5dB) is smaller than on EHT-LTF field, thus back-off may be mandated by EHT-LTF
We further explained that the higher PAPR associated with the EHT-LTF sequences of an MRU impacts the channel estimation and hence the demodulation performance
Hence, we showed the impact of higher MRU EHT-LTF PAPR on the PER by simulating the same scenarios with random sequences with different PAPR based on RAPP model of PA nonlinearity
~2dB
~0.3dB

## Slide 6: Recap – Solutions Survey
We examined several solution for PAPR reduction, including new EHT-LTF sequence design, extension of 11ax phase rotation and the proposed new method of linear phase with phase offset
The results revealed that new sequences (designed per MRU) and the proposed method of linear phase with phase offset may minimize PAPR for most of the examined scenarios
242+484 Comb | 2/2 | 1/2 | 4/1 | 3/1
Single RU484 | 5.86 | 5.86 | 5.86 | 5.86
MRU PAPR | 7.03 | 7.93 | 7.65 | 7.8
New Sequence | 6.29 | 6.68 | 6.68 | 6.28
Constant Phase | 6.96 | 7.42 | 7.65 | 7.23
Linear Phase | 6.95 | 6.95 | 6.87 | 7.16
Linear Phase + Offset | 6.71 | 6.85 | 6.82 | 6.9

## Slide 7: Recap – Summary
Finally we summarized the reviewed solutions and compared them in terms of PAPR reduction and also design and implementation aspects
The main conclusion was that finding a single/unified solution that can minimize all the combinations is not practical, whereas the proposed method of linear phase with phase offset may resolve the trade-off between design complexity and PAPR minimization
Solution | PAPR Reduction | Design/Spec Complexity | Implementation Complexity | Backward Compatibility
New Sequnce Design | High | High - A lot of sequences to define | High - large memory required | None
Reuse 11ax Phase Rotation | Very low | None | None | Full
Constant Phase Rotation | Low | Medium | Low | Full (by setting phase to zero)
Linear Phase | Medium | Meidum | Low | Full (by setting phase to zero)
Linear Phase with Phase Offset | High | Medium | Low | Full (by setting phase to zero)

## Slide 8: Extension for Phase Continuity
As raised during the presentation of [3], we would like to ensure phase continuity over the allocated tones in relevant MRU combinations
Thus we rechecked the case of 52+26 MRU where the two aggregated RUs are contiguous in frequency
We added a restriction on Linear Phase to be continuous on the edges of the two RUs (we actually restricted our solution to zero phase at the intersection)
We can see in the figure on the right that in all the simulated MRU combinations the gap between general linear phase and linear phase with phase continuity restriction is negligible
26RU
52RU
Frequency
Linear Phase

## Slide 9: Extension of the Topic to More Scenarios
During the discussions of [3], it was mentioned that the high PAPR issue is not unique for MRU scenarios but can be relevant for additional scenarios supported in 11be (e.g. preamble puncturing)
As this is indeed true, we extend the relevant scenarios for high EHT-LTF PAPR to include the following:
  Punctured non-OFDMA transmission (in both DL & UL)
  Multi-RU OFDMA transmission in the UL
  Punctured NDP transmission
The main metrics for PAPR minimization in a specific scenario is the difference between PAPR on data portion and PAPR on EHT-LTF, and PER degradation

## Slide 10: Detailed Analysis
In order to decide which combinations are relevant and require PAPR minimization we examined the impact of PAPR on PER in different scenarios for BW ≤ 80MHz
The example on the right shows that in specific case of 242+484 we can improve PER by reducing PAPR from 7.9dB to 6.8dB
According to our simulations ~25% of total combinations may require PAPR reduction
BW(MHz) | # of Problematic Combinations (Total) | Combinations
20 | 1 (4) | 52(2)+26(2)
40 | 1 (8) | 52(6)+26(11)
80 (small RUs) | 2(4) | 52(6)+26(11)
 |  | 52(7)+26(17)
80 (Large RUs) | 2(4) | 242(1)+484(2)
 |  | 242(4)+484(1)
> 80 | TBD | 

## Slide 11: General Solution for PAPR Issue
Following the two previous slides we can say that the majority of the MRU combinations (BW≤80MHz) have small or negligible PER degradation with reused HE-LTF sequences, however few MRUs do need to be handled
Hence we propose the following approach for PAPR reduction of EHT-LTF:
  Apply on top of EHT-LTF sequence a PAPR reduction solution for specific scenarios
  We the suggested in [3] a linear phase with phase offset as a solution for additional PAPR reduction
In this case the implementation may include an additional block that can be applied only for specific scenarios of high PAPR
802.11be
EHT-LTF Sequence(s)
Transmission Parameters
Linear Phase + Phase Offset
X
EHT-LTF Freq Domain
Phases Sequence
(may be ‘1’ if no apply )
Lower PAPR
EHT-LTF
Sequence

## Slide 12: Conclusion
PAPR is increased in multiple scenarios adopted by 802.11be and needs to be reduced in order to minimize the impact on channel estimation and PER
We simulated a design that consists of EHT-LTF sequence (reused HE-LTF for BW≤80MHz) and marked a specific cases where PAPR reduction is required
We suggested to add a PAPR reduction solution on top of EHT-LTF sequence in marked cases
We proposed solution of linear phase with phase offset which implies low implementation complexity and can be easily applied for these specific cases
A proposed solution of linear phase and phase offset can be considered for PAPR minimization of EHT-STF field as well

## Slide 13: References
[1] 11-19-1925-02-00be-consideration-of-eht-ltf
[2] 11-20-0117-01-00be-eht-ltfs-design-for-wideband
[3] 11-20-0473-01-00be-impact-of-multiple-ru-allocation-on-papr

## Slide 14: SP1
Do you support that 802.11be will define a solution which minimizes PAPR of EHT-LTF field in following scenarios?
  For BW ≤ 80MHz cases mentioned on slide 10
  For BW > 80MHz TBD

## Slide 15: SP2
Do you support that 11be will define a solution, based on linear phase and phase offset, as a solution for minimizing PAPR of EHT-LTF in specific cases?
  For BW ≤ 80MHz cases mentioned on slide 10
  For BW > 80MHz TBD