## Slide 1: Group addressed frames delivery for MLO
Date: 2020-04-20
Authors:

## Slide 2: Background
In the SFD, we agreed that
  A non-AP MLD monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s).
  As per reference [1] [2], it is straight forward to just have one link to monitor the traffic notification
  Today, DL traffic includes DL individual addressed BUs and group addressed BUs
  DL traffic notification is carried in Beacon frame
  In this contribution, we focus on group addressed BUs delivery
  These group addressed BUs do not require acknowledgement, like GCR group address frames
  Try to reuse the existing group addressed BUs delivery mechanism for multi-link

## Slide 3: Group addressed BUs
From frame type perspective, group addressed BUs contain the following two types
  Group addressed management frames
  Group addressed data frames
  From transmission scheme perspective, group addressed BUs can also be classified as
  Broadcast BUs
  Multicast BUs
  In the existing spec, group addressed BUs (if any) are immediately delivered after DTIM beacon
  Whether there are group addressed BUs is indicated by the first bit of Bitmap Control field in the TIM element
  No further finer mechanisms for different types of group addressed BUs

## Slide 4: Group addressed BUs delivery
There may exist two schemes to delivery group addressed BUs
  Opt 1： Deliver all the group addressed BUs of all the links to the STA MLD on a configured link
  It may be applied to multicast addressed data frames
  But it can not be applied to either group addressed management frames or broadcast addressed data frames because of coexistence of legacy STAs
  Broadcast addressed data frames shall be sent on all the links of the AP MLD
  Group addressed management frames shall be sent on its related link, otherwise it would bloat the group addressed BUs transmission time on a configured link and waste the power of the legacy STA and single link STA
  In this option, it is likely to have duplicated group addressed BU on every link if each STA MLD has a different configured link
AP 1
AP 2
Link 1
STA1
AP1
STA2
AP2
Link 2
DTIM B
Group BU 1
AP 3
DTIM B
Group BU 2
STA 3
AP3
Link 3
DTIM B
Group BU 1+2+3
STA 1
STA 2
STA 3
Configured link
Legacy STA

## Slide 5: Group addressed BUs delivery
Opt 2: Deliver the group addressed BUs on a corresoding link immediately after DTIM beacon
  Follow the existing group addressed BUs delivery mechanisms, no need to have separate schemes for different group BU types
  Group addressed management frames are sent on its corresponding link
  Broadcast addressed data frames are sent on all the links of the AP MLD
  Multicast addressed data frames are sent in some link(s) as per AP MLD’s implementation algorithm
  Multicast addressed data frames are sent to a specific group of STAs, not to all the STAs
  However, each STA MLD in this specific group may configure a different link to monitor traffic indication.
  Maybe AP could choose some implementation algorithm to deliver them separately on one or more links as AP know this specific group , not duplicate them of all the links and send them on a configured link
AP 1
AP 2
Link 1
STA1
AP1
STA2
AP2
Link 2
DTIM B
Group BU 1
AP 3
DTIM B
Group BU 2
STA 3
AP3
Link 3
DTIM B
Group BU 3
STA 1
STA 2
STA 3
Configured link
Legacy STA

## Slide 6: Group addressed BUs delivery with configured link
For option 1, it requires a configured link to receive traffic for a STA MLD, otherwise the AP MLD does not know how to deliver them (lazy scheme-do duplication)
  Actually if there is a configured link but different configured link for each STA MLD，it still needs duplication
Example without configured link
  No need group BUs duplication of all the links in option 2
Example with configured link
AP 1
Link 1
STA1
AP1
DTIM B
Group BU 1
AP 2
STA 2
AP2
Link 2
DTIM B
Group BU 2
STA 1
STA 2
Configured link
AP 1
Link 1
STA1
AP1
DTIM B
Group BU 1+2
AP 2
STA 2
AP2
Link 2
DTIM B
Group BU 1+2
STA 1
STA 2

## Slide 7: Group addressed BUs delivery with configured link
In option 1, a STA MLD uses a configured link to receive group addressed BUs
However in option 2, a STA MLD could use one or more links to monitor the group addressed BUs notification and then to receive its group addressed BUs on the corresponding link
  The same design philosophy as the existing group BU delivery mechanism
  The same way as Wake up Radio where it uses group BUs notification to tell the STA whether there are group BUs after DTIM beacon for primary connective radio
  No burden to separate different group addressed BUs
  Note that option 2 can still work without obvious overhead increment if there is no configured link for the non-AP MLD
AP 1
Link 1
STA1
AP1
DTIM B
Group BU 1
AP 2
STA 2
AP2
Link 2
DTIM B
STA 1
STA 2
STA MLD has group BU on link 1
Configured link
Reception

## Slide 8: Summary
We propose that the group addressed BUs delivery immediately after DTIM beacon is link specific
  Follow the existing group addressed BUs delivery mechanisms, no need to have separate schemes for different types

## Slide 9: References
[1] IEEE 802.11-19/1988r0 Power save for Multi-link
[2] IEEE 802.11-19/1526r3 Multi-link operation: anchor channel
[3] IEEE 802.11-20/0488r0 Multi-link Group Addressed Data Delivery

## Slide 10: SP 1
Do you agree that group addressed BUs transmission immediately after DTIM beacon is link specific for an AP MLD