## Slide 1: 320 MHz BSS Configuration Follow Up
Date: 2020-04-18
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Robert Stacey |  |  |  | 
Xiaogang Chen |  |  |  | 
Danny Alexander |  |  |  | 
Arik Klein |  |  |  | 
Daniel F Bravo |  |  |  | 
Notes: September 2012

## Slide 2: Background
We discuss 320 MHz BSS configuration in the past[1]
The latest development in 6 GHz regulatory suggests that there may be SP AFC AP, and certain 20 MHz maybe restricted for usage (disallowed or power limit)
We expect that the most common operation is LPI mode due to uncertainty of AFC management
  There is no need for static puncturing in LPI mode
Nevertheless, we discuss how we can manage 320 MHz BSS advertisement for legacy and EHT STA for SP AFC AP.
  For example, advertise 20 for legacy due to 20 MHz restriction and 40/80/160 or 80+80/320 or 160+160 for EHT STA
  Note that this proposal is only needed in 6 GHz

## Slide 3: General Design Principle
In EHT operation element
  Have Channel Width to indicate 20/40/80/160 or 80+80/320 or 160+160
  Have EHT CCFS0 with same indication principle of CCFS0 in HE operation element
  Have EHT CCFS1 with same indication principle of CCFS1 in HE operation element
  Have EHT CCFS to indicate center of 320 or center of secondary 160
If the EHT BSS configuration is larger than the BSS configuration for legacy STA
  Simply looking at the EHT operation element as one place for all the indication
  Avoid complicated linking with the legacy indication in 6 GHz for whatever scenario

## Slide 4: Advertisement in 6 GHz
Legacy BSS Configuration | Setting | EHT BSS Configuration | Setting
20 | Channel Width: 20 CCFS0: center of 20 CCFS1: 0 | 20 | Channel width: 20 EHT CCFS0: center of 20 EHT CCFS1: 0 EHT CCFS: 0
20 | Channel Width: 20 CCFS0: center of 20 CCFS1: 0 | 40 | Channel width: 40 EHT CCFS0: center of 40 EHT CCFS1: 0 EHT CCFS: 0
20 | Channel Width: 20 CCFS0: center of 20 CCFS1: 0 | 80 | Channel width: 80 EHT CCFS0: center of 80 EHT CCFS1: 0 EHT CCFS: 0
20 | Channel Width: 20 CCFS0: center of 20 CCFS1: 0 | 160/80+80 | Channel width: 160/80+80 EHT CCFS0: center of primary 80 EHT CCFS1: center of 160 or secondary 80 EHT CCFS: 0
20 | Channel Width: 20 CCFS0: center of 20 CCFS1: 0 | 320/160+160 | Channel width: 320/160+160 EHT CCFS0: center of primary 80 EHT CCFS1: center of primary 160 EHT CCFS: center of 320 or secondary 160

## Slide 5: Advertisement in 6 GHz
Legacy BSS Configuration | Setting | EHT BSS Configuration | Setting
40 | Channel Width: 40 CCFS0: center of 40 CCFS1: 0 | 40 | Channel width: 40 EHT CCFS0: center of 40 EHT CCFS1: 0 EHT CCFS: 0
40 | Channel Width: 40 CCFS0: center of 40 CCFS1: 0 | 80 | Channel width: 80 EHT CCFS0: center of 80 EHT CCFS1: 0 EHT CCFS: 0
40 | Channel Width: 40 CCFS0: center of 40 CCFS1: 0 | 160/80+80 | Channel width: 160/80+80 EHT CCFS0: center of primary 80 EHT CCFS1: center of 160 or secondary 80 EHT CCFS: 0
40 | Channel Width: 40 CCFS0: center of 40 CCFS1: 0 | 320/160+160 | Channel width: 320/160+160 EHT CCFS0: center of primary 80 EHT CCFS1: center of primary 160 EHT CCFS: center of 320 or secondary 160

## Slide 6: Advertisement in 6 GHz
Legacy BSS Configuration | Setting | EHT BSS Configuration | Setting
80 | Channel Width: 80 CCFS0: center of 80 CCFS1: 0 | 80 | Channel width: 80 EHT CCFS0: center of 80 EHT CCFS1: 0 EHT CCFS: 0
80 | Channel Width: 80 CCFS0: center of 80 CCFS1: 0 | 160/80+80 | Channel width: 160 EHT CCFS0: center of primary 80 EHT CCFS1: center of 160 or secondary 80 EHT CCFS: 0
80 | Channel Width: 80 CCFS0: center of 80 CCFS1: 0 | 320/160+160 | Channel width: 320/160+160 EHT CCFS0: center of primary 80 EHT CCFS1: center of primary 160 EHT CCFS: center of 320 or secondary 160

## Slide 7: Advertisement in 6 GHz
Legacy BSS Configuration | Setting | EHT BSS Configuration | Setting
160/80+80 | Channel Width: 160/80+80 CCFS0: center of primary 80 CCFS1: center of 160 or secondary 80 | 160/80+80 | Channel width: no indication EHT CCFS0: center of primary 80 EHT CCFS1: center of 160 or secondary 80 EHT CCFS: 0
160 | Channel Width: 160 CCFS0: center of primary 80 CCFS1: center of 160 | 320/160+160 | Channel width: 320/160+160 EHT CCFS0: center of primary 80 EHT CCFS1: center of primary 160 EHT CCFS: center of 320 or secondary 160

## Slide 8: 2.4/5 GHz band
Expect that we do not have SP AFC AP in 2.4/5 GHz
  Only need Channel Width indication and EHT CCFS for 320 MHz or 160+160
If we need indication of difference BSS bandwidth in 5 for legacy and EHT, then the solution is to add EHT CCFS2 to EHT operation element when we need to differentiate w/o Extended NSS channel width for VHT.

## Slide 9: Signaling for Channel Width indication in EHT operation element
3 bits Channel Width field in EHT operation element to indicate the following
  0: 20
  1: 40
  2: 80
  3: 160/80+80
  4: 320/160+160
  5: reserved
  6: reserved
  7: reserved
The above indication aligns nicely with the indication about 6 GHz BSS configuration in HE operation element

## Slide 10: Conclusion
To resolve the need of advertising all possibilities of BSS configuration to EHT STA and smaller BSS configuration to legacy HE STA, we propose to
  Have EHT CCFS0 and EHT CCFS1 in EHT operation element
  Have Channel Width field of EHT operation element indicate 20/40/80/160 or 80+80/320 or 160+160

## Slide 11: Straw Poll
Do you support to have at least the following indication in the Channel Width field of the EHT operation element?
  20
  40
  80
  160/80+80
  320/160+160
  Note – Channel Width field of the EHT operation element is expected to be set inline with the channel with field of HT/VHT/HE operation element unless explicitly stated otherwise

## Slide 12: Straw Poll
Do you support to include EHT CCFS0 and EHT CCFS1 in EHT operation element?
  The indication of EHT CCFS0 and EHT CCFS1 when Channel Width field of the EHT operation element indicates 20, 40, 80, 160/80+80 are the same as the indication defined in 11ax for CCFS0 and CCFS1 in HE operation element when Channel Width field of the HE operation element is equal to 20, 40, 80, 160/80+80, respectively.

## Slide 13: Straw Poll
Do you support the following indication for CCFS field in EHT operation element?
  320 MHz: indicates the channel center frequency index of the 320 MHz channel
  160+160 MHz: indicates the channel center frequency index of the secondary 160 MHz channel
  0 otherwise
Do you support 3 bits of Channel Width field in EHT operation element?

## Slide 14: Reference
11-20-384r1 320 MHz BSS Configuration