## Slide 1: Multi-link Individual Addressed Data Delivery without BA
Date: 2020-05-04
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Dan Bravo |  |  |  | 
Danny Alexander |  |  |  | 
Arik Klein |  |  |  | 
Ofer Schreiber |  |  |  | 
Notes: September 2012

## Slide 2: Background
Multi-link framework has been proposed below. We discuss how to transmit individual addressed traffic without BA across links.
AP1
AP2
AP3
STA1
STA2
STA3
AP MLLE
Non-AP MLLE

## Slide 3: Motivation
For single link operation, after association and RSNA, STA can transmit QoS data without BA agreement.
  Follow similar line of thought, after multi-link setup and security negotiation, MLD can transmit QoS data without BA agreement subject to TID mapping constraints.
Why transmitting data without BA?
  When BA is negotiated across links, it is possible that we may have transient period of deleting BA and renegotiating BA. In the transient period, we may want to continue to transmit individual addressed traffic across links like today
  When there are not a lot of traffic to send or low MCS is used, BA may not be needed, and transmission across links is still needed when switching link used for frame exchange

## Slide 4: General Consideration on the Scenario
Example: Data continuity
Example: Add Reliability
AP
1
AP
2
AP MLD
Non
-
AP MLD
Non
-
AP
1
Non
-
AP
2
Individual
addressed
frame
1
Individual
addressed
frame
2
Radio
1
on
-
link
1
Radio
2
off
-
link
2
Radio
2
on
-
link
2
Radio
1
off
-
link
1
AP
1
AP
2
AP MLD
Non
-
AP MLD
Non
-
AP
1
Non
-
AP
2
Individual
addressed
frame
1
Individual
addressed
frame
1
Radio
1
on
-
link
1
Radio
2
off
-
link
2
Radio
2
on
-
link
2
Radio
1
off
-
link
1

## Slide 5: Recap of delivering individual addressed traffic without BA in one link
Transmitter:
  Can not transmit other QoS Data frame from the same TID until the current frame finish transmission or dropped
  Continue to transmit the failed QoS Data frame until retry counter is met
Receiver:
  Maintain at least the most recent record of <Address 2, TID, sequence number>.
  Drop the frame with retry bit set and record match

## Slide 6: Extension to Multi-link
Transmitter:
  Expand Table 10-5—Transmitter sequence number spaces to have a new entry Indexed by <destined MLD Address, TID>
  Continue to transmit the failed QoS Data frame until retry counter is met
  Can not transmit other QoS Data frame from the same TID in any link until the current frame finish transmission or dropped
Receiver:
  Maintain at least the most recent record of <peer MLD address, TID, sequence number>.
  Drop the frame with retry bit set and record match

## Slide 7: Conclusion
We discuss how to transmit individual addressed data in multi-link without BA negotiation
We propose to enable this feature for multi-link as a extension from baseline

## Slide 8: Straw Poll
After multi-link setup, do you support the following to enable delivery of individual addressed QoS traffic of a TID without BA negotiation across links, where the TID is mapped, in R1?
  For Transmitter:
    Expand Table 10-5—Transmitter sequence number spaces to have a new entry Indexed by <destined MLD Address, TID>
    Continue to transmit the failed QoS Data frame until retry counter is met
    Cannot transmit other QoS Data frame from the same TID in any link until the current frame finish transmission or dropped
  For Receiver:
    Maintain at least the most recent record of <peer MLD address, TID, sequence number>.
    Drop the frame with retry bit set and record match