## Slide 1: Fragmentation in EHT
Date: 2020-02-06
Authors:
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
George Cherian | Qualcomm Inc. |  |  | 

## Slide 2: Introduction
EHT is significantly increasing the achievable throughput due to
  Increase of BW to 320 MHz, SSs to 16, QAM constellation to 4K,
  Introduction of multi-link operation, etc.
In this contribution we discuss fragmentation, its variants and the impact on the design of EHT STAs

## Slide 3: Baseline Fragmentation
Static frag. splits an MSDU into multiple fragments, with each fragment
  Having equal length, except for the last one that can be smaller.
  Soliciting an immediate Ack frame
This type of fragmentation
  Is used at low data rates regimes and in bad channel conditions
  Requires high overhead compared to useful information delivered
    Each fragment has its own MAC header, SIFS, Ack frame, etc.
    Leading to increased airtime and latency, and reduced efficiency
EHT STAs target extremely high throughputs, among other things
  Targets which can be impacted by static fragmentation
Propose to disallow static frag. or make it optional (RX)
  At least consider disallowing for EHT STAs that are MLO STAs since it adds complexity with no benefits

## Slide 4: Dynamic fragmentation
Dynamic fragmentation splits an (A)MSDU into multiple fragments, wherein each fragment
  Has a length different from that of other fragments of same (A-)MSDU
  Solicits an Ack, (M-)BlockAck, depending on the level of fragmentation
This type of fragmentation is used for high efficiency (HE)
  Replaces padding that is otherwise needed in HE MU/TB PPDUs
  Can be used for low data rates and/or extended range scenarios (on a single link)
This type of functionality is beneficial for EHT STAs
  Helps to improve efficiency, and reduce overhead, wherever necessary
    Similar to the HE use cases (e.g., low data rate / extended range over a single link)
Propose to preserve the optionality of this feature for EHT
  Additional details in following slides

## Slide 5: Dynamic Fragmentation (Cont.)
Currently a STA declares its support for dynamic fragmentation along with a variety of parameters via HE Capabilities IE that it transmits
  E.g., number of fragments, level of fragmentation, etc.
  Proposal: For multi-link these parameters are at the MLD level
During BA setup, the MLDs can negotiate different levels of dynamic fragmentation on a per-TID basis
  In ADDBA Extension IE included in ADDBA Request/ADDBA Response frame (i.e., reuse existing 11ax framework)

## Slide 6: Dynamic Fragmentation (Cont.)
Handling in a multi-link setting will require some considerations
If link-level fragmentation is used, there is a high risk that a fragment can get stuck on a congested link which would prevent the BA window from advancing further
  Thus bringing down the overall thruput and going against the charter of EHT.
MLO provides link diversity which means if conditions deteriorate on a link, a fragment can be attempted on another link
Therefore we propose that dynamic fragmentation must be performed at the MLD level

## Slide 7: Dynamic Fragmentation (Cont.)
A STA transmits fragment(s) and reports to MLD the portion of MSDU which did not make it through
  i.e., transmitting STA uses explicit acknowledgment functionalities (defined in 11ax) to ensure the successful delivery of a portion of the MSDU
Receive status of MSDUs that are fragmented is maintained at the MLD
Fragment can be sent on any link as long as the fragment size and contents remain unchanged
  An MLD may attempt to retransmit a failed fragment on any link
An MLD may not be capable of receiving fragments of an MSDU
  Define a bit to indicate if the MLD supports receiving fragment from a peer MLD.
  Originator may perform fragmentation and transmit frames of an MSDU only if the receiving MLD has indicated support (i.e., bit set to 1)

## Slide 8: Disallow Fragmentation for R1
In order to keep things simple and meet the R1 timeframe, we propose disallowing fragmentation in R1
Then in R2, we can discussion and provide details in the spec on fragmentation for MLO (i.e., the proposal in previous the slides)

## Slide 9: Summary
We discuss fragmentation for EHT STAs and propose to
  Disallow or make optional static fragmentation for EHT
Propose to have a receiver capability to indicate if the recipient can receive fragments of the same MSDU on more than one link
Propose to move fragmentation under MLO to R2 to keep things simple for R1
For R2, negotiate dynamic fragmentation at the MLD level which allows, a fragment may be retransmitted on any link of the MLD

## Slide 10: Additional discussion
Disallow static fragmentation in MLO
  Static fragmentation: used in low data rate regimes and highly inefficient
    Will have adverse impact on performance of an EHT STA
  An MLD can always pick a different/better link when the conditions on a certain link deteriorate
There are different opinions about dynamic fragmentation (link vs MLD level).
  In our view, dynamic fragmentation at MLD level will provide the most benefit.
  STAs of an MLD share the same sequence number space along with a common BA scoreboard therefore fragmentation at MLD level naturally fits in the design
  If fragmentation is performed at link-level, there is a high risk that a fragment can get stuck on a congested link which would prevent the BA window from advancing further.
  MLO provides link diversity which means, a fragment can be retried on any link
With respect to dynamic fragmentation in R1/R2: propose disabling in R1
  This gives the TGbe group more time to have a healthy discussion on the topic, e.g.,
    Whether dynamic fragmentation should be performed at link-level or MLD-level,
    Whether fragmentation is possible if encryption is handled at higher layer, etc.
      cases brought up in 11-20/1545 (MLD Security Considerations – Gaurav, HPE)
  There are views that dynamic fragmentation in R1 will be useful to replace padding to align Sync PPDUs
    However, transmission of sync PPDUs is optional and padding is conditional to sync PPDU
    Therefore, replacing padding with fragments is a second order optimization  not a strong motive for having it in R1

## Slide 11: SP 1
Do you support that the 802.11be amendment shall disallow static fragmentation in MLO?
  Y:
  N:
  A:

## Slide 12: SP 2
Do you support that dynamic fragmentation between two MLDs is not supported in R1?
  Y:
  N:
  A:

## Slide 13: SP 3
Do you support that dynamic fragmentation between two MLDs is optional for R2?
  Dynamic fragmentation operation between two MLDs is TBD
  Y:
  N:
  A:

## Slide 14: SP 4
Do you support to have a capability bit “MLD Fragmentation” in TBD element?
  If the bit is set to 0 by a STA affiliated with an MLD, the MLD does not support reception of a fragment from a peer MLD
  An MLD shall not fragment frames and send fragment to another MLD that has set this bit to 0.
  Note: The bit is set to 0 for R1
  Y:
  N:
  A:

## Slide 15: Appendix

## Slide 16: Fragmentation in EHT
Dynamic Frag. Support* (HE Caps) | MLD Fragmentation (EHT Caps/ML IE) | Description
0 | 0 | No support for dynamic fragmentation at any level (EHT STA or MLD DEV). No support for static fragmentation at any level (EHT STA or MLD DEV. R1 text: STA of an MLD shall not fragment frames sent to another STA of MLD that has set these bits set to these values. No R2 text.
0 | 1 | No support for dynamic fragmentation at MLD level. Not applicable to EHT STA without MLD setup (sets new cap bit to 0). Maybe support for static fragmentation at MLD level?** No R1 text. R2 text to be dealt with later.
> 0 | 0 | Yes support for dynamic fragmentation at EHT STA (baseline). No support for dynamic fragmentation at MLD level. No support for static fragmentation at any level. No R1 text. No R2 text.
> 0 | 1 | Yes support for dynamic fragmentation at MLD level. Not applicable to EHT STA without MLD setup (sets new cap bit to 0). No support for static fragmentation at MLD level** No R1 text. R2 text to be dealt with later.
*Each STA (of an MLD eventually) indicates its support in HE Caps. IE as per baseline. ** Static fragmentation can be disabled altogether. |  |