## Slide 1: Multi Link Group Addressed Frame delivery for non-STR MLD
Date: 2020-04-23
Authors:
Name | Affiliations | Address | Phone | email
Jason Yuchen Guo | Huawei Technologies |  |  | guoyuchen@huawei.com
Yunbo Li |  |  |  | 
Guogang Huang |  |  |  | 
Ming Gan |  |  |  | 
Yifan Zhou |  |  |  | 
Yiqing Li |  |  |  | 

## Slide 2: Introduction
Multi-link operation is a key feature in TGbe
Non-AP MLD may be non-STR on two links: not capable of transmitting on one link while receiving on the other link
On each link, the non-AP MLD always has DL frames to receive if it’s not in PS mode
  Beacon frame
  Group addressed frames
    Broadcast frames
    Multicast frames
When a non-STR non-AP MLD is receiving DL frames on a link, there should be some restrictions on the other link, e.g., The non-STR non-AP MLD should not transmit on the other link
In this contribution, we propose a scheme on group addressed frame delivery to alleviate the above restrictions

## Slide 3: Motivation
As show in the following figure, when link 1 is used for transmitting Beacon and group addressed frames, there are some restrictions on link 2, and vice versa.
  Restriction 1: The AP-MLD should not transmit a frame to the non-STR non-AP MLD on Link 2 which solicits response
  Restriction 2: The non-STR non-AP MLD should not contend channel on Link 2 to transmit frames
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
DTIM Beacon
DTIM Beacon
Group addressed frame
Group addressed frame
Restriction 1
Restriction 2
Restriction 1
Restriction 2

## Slide 4: Proposal 1.1 - Beacon alignment
Regarding Beacon frame reception, there will be no restriction since all links are used for Beacon transmission at the same time, non-STR non-AP MLD is receiving Beacon frames on all links, simultaneous TX and RX will not happen
Regarding Group addressed frames, if there are group addressed frames on all links, then there will be no restriction; if there is no group addressed frame on a certain link, then restriction only happens on this certain link
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
DTIM Beacon
DTIM Beacon
Group addressed frame
DTIM Beacon
Group addressed frame
DTIM Beacon
Group addressed frame
Restriction 1
Restriction 2
Group addressed traffic indicator = 0
Proposal: if there exist at least one non-STR non-AP MLD whose STAs are associated with the APs that belong to the same AP MLD, then the target Beacon Transmission Time (TBTT) of the APs should be the same.

## Slide 5: Proposal 1.1 - Beacon alignment
Sometimes, the Beacon frames on different links may not be entirely aligned due to channel busy, but it doesn’t matter if the channel busy is caused by STR MLD or single link STAs
We only need to make sure that the non-STR MLD shall not cause channel busy at the TBTT
Proposed rule: if a non-STR MLD successfully contends the channel before the TBTT, then it should end its TXOP before the TBTT
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
DTIM Beacon
Group addressed frame
DTIM Beacon
Group addressed frame
TXOP
backoff
TXOP
backoff

## Slide 6: Proposal 1.2 – Dedicated service period for group addressed frames on all links
An alternative is: setup a dedicated service period for group addressed frames on all links
  This service period is only for non-STR non-AP MLD
  Legacy STAs and STR non-AP MLD can behave like before
Restriction only happens on the link where group addressed frames are not present
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
Beacon
Group addressed frame
Group addressed frame
Service period for group addressed frames on all links
Group addressed frame
Service period for group addressed frames on all links
Restriction 1
Restriction 2

## Slide 7: Proposal 2 – Multicast Traffic indication Map
The group addressed frames include broadcast frames and multicast frames
If a STA (STA1) only has broadcast frame to receive, then the other STA (STA2) in the MLD can start contending channel after STA1 finishes reception of the broadcast frame
If STA1 has both broadcast and multicast frames to receive, then STA2 can only start contending channel after STA1 finishes reception of both the broadcast frames and the multicast frames
Hence, it would be beneficial to tell a STA whether it has multicast frame to receive or not.
MLD1 - AP1
Link 1
Link 2
MLD2 - STA1
MLD1 – AP2
MLD2 – STA2
DTIM Beacon
Broadcast Frame
DTIM Beacon
Multicast Frame
Restriction 1
Restriction 2
STA1 may or may not be the receiver of the multicast frame
Restriction or not?

## Slide 8: Proposal 2 – Multicast Traffic indication Map
In the current SPEC, the Traffic Indicator bit in the TIM element indicates whether the AP has group addressed frames to transmit, but it doesn’t distinguish broadcast frame and multicast frames
In this case, the STA may need to wait for a long time to know whether it has pending multicast traffic to receive or not
In order to solve this problem, we propose to include a multicast traffic indication map (MTIM) element in the DTIM Beacon frame to tell each STA whether it has pending multicast traffic to receive
Element ID
Length
Element ID Extension
Bitmap Control
Partial Virtual Bitmap for Multicast Traffic
Broadcast Indicator
Bitmap Offset

## Slide 9: Conclusion
  We propose a scheme on group addressed frame delivery
  We suggest define the following operations in TGbe
    Beacon frame alignment when non-STR MLD exist
    TXOP early termination of non-STR MLD to make sure the Beacon frames can be received on other links
    Dedicated service period for group addressed frames on all links for non-STR non-AP MLD
    Multicast Traffic indication Map carried in the DTIM Beacon frame

## Slide 10: Straw Poll 1
  Do you agree with the following rule?
    If there exist at least one non-STR non-AP MLD whose STAs are associated with the APs that belong to the same AP MLD, then the target Beacon Transmission Time (TBTT) of the APs should be the same

## Slide 11: Straw Poll 2
  Do you support the following rule?
    When a non-STR MLD intends to receive Beacon frames on more than one link, if it successfully contends the channel on one link before the TBTT of the other link, then it should end its TXOP before the TBTT of the other link

## Slide 12: Straw Poll 3
  Do you support to define a dedicated service period for group addressed frames on all links?

## Slide 13: Straw Poll 4
  Do you support to include a multicast traffic indication map (MTIM) element in the DTIM Beacon frame to indicate each STA whether it has pending multicast traffic to receive?

## Slide 14: References
  [1]