## Slide 1: On Number of Users in MU-MIMO
Date: 2020-05-13
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Proposal
Discussion:
  While the number of streams supported in MU-MIMO has increased to 16 in 11be, for the typical 75% loading used in MU-MIMO we only need 6STA, each with Nss=2 (typical STA configuration has 2 antenna)  8 STA for MU-MIMO seems sufficient
  In addition, from STA point of view prefer not to receive Nss=1 and decode 12-16 LTF in a scenario that sends 12 streams to 12 STA.
  We have also looked at typical scenarios in the home and enterprise and don’t see a case where there is a need for more than 8 heavy traffic users that could be candidates for MU-MIMO
  The spec will also support groups of MU-MIMO on partial BW, can envision at least 32 MU-MIMO users in four groups without the need for more than 8 STA in a group.
Hence, propose to keep the maximum number of users in MU-MIMO to 8 as in 11ax.

## Slide 3: Straw Poll 1
Do you support that no more than 8 users can be scheduled in MU-MIMO?
Yes
No
Abs