## Slide 1: Multi-link Element format
Date: 2020-05-11
Authors:
Name | Company | Address | Phone | Email
Rojan Chitrakar | Panasonic Corporation | 202 Bedok South Avenue 1, #02-11 Singapore 469332 |  | rojan.chitrakar@sg.panasonic.com
Lei Huang |  |  |  | 
Yanyi Ding |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Introduction
Many variants of Multi-link elements have been proposed in .11be. Defining multiple elements will cause the Element ID Extension space to run out faster. As of REVmd_D3.3, only 162 IDs are available.

## Slide 3
Multi-link elements - 1
Multi-link TIM element [2]
Multi-link element for Discovery & Multi-link Setup [1]
1
Element ID
Octets:
Length
1
Element ID
Extension
0 or 1
Link ID
TBD
Per-link TIM Information
TBD
For link “x”
Link ID
TBD
Per-link TIM Information
TBD
For link “y”

## Slide 4
Multi-link elements - 2
Multi-link IE for BSS Parameter update [3]
Element ID | Length | Element ID Extension | Link ID | Optional Subelements
1 octet | 1 octet | 1 octet | 1 octet | variable
<Multi-link IE>
Multiple Link Attribute (MLA) element for ML Discovery [4]
 | Element ID | Length | Element ID Extension | Common Control | MLD Address | MLD SSID | Authentication Algorithm | … | Optional Sub-elements
Octets: | 1 | 1 | 1 | x | 0 or 6 | 0 or 32 | 0 or 2 | … | variable
Common/MLD Capabilities
Set of elements organized as a profile for every other STA of the MLD
Strcuture of Multiple Link Attribute element
MLD Addr Present
MLD SSID Present
Auth Algo Present

## Slide 5
Multi-link elements: Others?
New elements may be needed for other Multi-link operations, e.g. TID-to-link mapping, per-link Medium State Information etc.
It may be possible to design a unified format for some usage e.g. Multi-link Discovery and Multi-link Setup, but a common design that cater to all use cases may be more complicated and may lead to unnecessary overhead.

## Slide 6
Proposal: A common Multi-link element
A common Multi-link element that carries a Type field to differentiate the various usages, each of which could be of different format:
Type field Values | 
Value | Meaning
0 | Multi-link Discovery
1 | Multi-link Setup
2 | Multi-link BSS Parameter update
3 | TID-to-link Mapping
4 | Multi-link TIM
5 ~ 255 | Reserved
Type field Values | 
Value | Meaning
0 | Capabilities
1 | Operation Parameters
2 | BSS Parameter update
3 | TID-to-link Mapping
4 | TIM
5 ~ 255 | Reserved
Option 1: Based on Usage:
Option 2: Based on content:

## Slide 7: Reference
[1] 20/28r1 - Indication of Multi-link Information (Insun Jang)
[2] 20/84r0 - Multi-link TIM design (Alexander Min)
[3] 20/337r1 - Multi-link BSS Parameter Update (Yongho Seok)
[4] 20/357r0 - Container for advertising ML Information (Abhishek Patil)

## Slide 8
Straw Poll 1
Do you support that:
  A common element is defined to carry the information for various Multi-link operations, the element carrying a Type field right after the Element ID Extension field to differentiate the various usage of the element.
    The format of the element may differ based on the value of the Type field.
  Y/N/A
  Note: This is not for SFD.

## Slide 9
Straw Poll 2
Which option do you prefer for the Type field:
  Option 1: Based on Usage
  Option 2: Based on Content
  Opt1/Opt2/Others/Abstain
  Note: This is not for SFD.