## Slide 1: Mandatory Larger BW Support
Date: 2020-06-04
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Proposal
In 11be the top BW increases to 320MHz
It is likely that some AP will be communicating with devices not supporting their BSS BW (e.g. 160 device in a 320MHz BSS).
In 11ax it is allowed for devices to reject packets with BW higher than their supported BW even though they could still participate in a DL OFDMA frame.
  In order to improve operation in these cases, propose that in 11be, 80MHz and 160MHz operating STA shall be able to participate in a higher BW OFDMA PPDU

## Slide 3: Straw Poll 1
Do you support that in 11be, 80MHz and 160MHz operating STA shall be able to participate in a higher BW DL and UL OFDMA transmission?
  STA shall be able to decode the preamble and its assigned RU (some restrictions TBD)
  No capability bit as in 11ax