## Slide 1: Triggered P2P transmissions follow up
Date: 2020-05-07
Authors:

## Slide 2: Outline
Proposal for Triggered P2P Transmissions for R1
Advantages

## Slide 3: Principle 1/2
Allow only time sharing for R1
  Reduced feature capabilities
Reuse as much as possible 11ax feature and signaling
  Based on 11ax cascading scheme
  Requires only one bit of signaling to indicate P2P RUs
Prepare frequency sharing for R2.
  Signaling based on TF/RU signaling.

## Slide 4: Principle 2/2
AP
STA1
STA2
STA3
STA4
HE MU PPDU / TRS or TF
ACK 21
HE MU PPDU /TRS or TF
HE TB PPDU
HE TB PPDU
Multi STA Block Ack
SIFS
SIFS
SIFS
SIFS
SIFS
TXOP
MU cascading sequence
TB Length
P2P PPDU
UL Length
SU PPDU
(N x 20MHz)

## Slide 5: Triggered P2P Transmissions follow up
No Change in the direct link setup/teardown procedure.
Triggered P2P feature should be controlled by a capability (both at AP or STA level).
A non-AP STA can signal the need for P2P transmission thanks to Tspec or BSR (exact signaling is TBD).
P2P traffic is triggered by the AP for a “Single-User style” PPDU :
  AP can share a part of the TXOP to the P2P traffic, based on 11ax cascading mechanism.
    The AP provides resource to the source P2P station that is associated with it.
  P2P traffic uses a “P2P RU” = n x 20MHZ covering all the operating band for that period of time.
  Simple signaling (typically 1 bit) to signal “P2P RU”.
  P2P traffic uses its own preamble on its distinct channel :
    AP does not need to provide all trigger transmission parameters (e.g. MCS)
    No synchronization requirement (even for Ack part)
  PPDU format is TBD (e.g. SU or MU PPDU format can be envisaged)

## Slide 6: Advantages
Take combined benefits of MU and SU operations :
  Enhance global cell’s efficiency
    More efficient compared to SU medium-access schemes (former EDCA Direct-Link protocols, RDP protocol, etc.)
  AP can still share Uplink/Downlink RUs from other STAs.
  P2P stations communicate alone in their allocated RU channel (operating band)
  AP does not need to be aware of P2P transmission characteristics (so does not provide all trigger parameters, e.g. MCS)
  Acknowledgement can be performed without interference issue (no parallel transmission)
  Receiving peer station can be outside of the AP’s BSS.
MU
SU

## Slide 7: Summary
Trigger Frame is the natural tools for scheduling non-AP stations, including P2P STAs.
Reusing cascading mechanism allows a time sharing for P2P with limited modifications
Triggered P2P operation is simple :
  P2P stations are triggered over the operating band.
  P2P stations use their own PPDU format for the shared period of time (including Ack).

## Slide 8
Straw Poll #1
Do you support that 11be defines a procedure for an AP to share a part of the obtained TXOP for peer-to-peer (STA-to-STA) frame exchanges using cascading mechanism as defined in slide 4?
Results: Y/N/A

## Slide 9: Reference
[1]. 11-18-1481-01: Technology for EHT
[2]. 11-19-1117-00: Coordinated OFDMA Operation
[3]. 11-20-0095-02: Triggered P2P transmissions