## Slide 1: Trigger Frame for Frequency-domain A-PPDU Support
Date: 2020-05-20
Authors:

## Slide 2: Background
Frequency-domain (FD) A-PPDU will be supported in 11be
We need a MAC protocol to support it
  Announcement/Trigger frame
DCN 0674r3 [2] contribution provides MAC requirements to support A-PPDU
  [Downlink] enhanced downlink (DL) announcement frame
  [Uplink] enhanced uplink (UL) trigger frame
In this contribution, we propose several design options for trigger frame to support FD A-PPDU

## Slide 3: Expected UL Operation
Trigger frame allocates the 80MHz segment(s) to be used for UL
  HE STA will be assigned to use P80 or P160 (backward compatibility)
  EHT and EHT+* STA will be assigned to use secondary segments
* EHT+: the amendments after EHT

## Slide 4: Design Principles for Trigger Frame
MAC requirements
  New design should support any combination of HE, EHT and EHT+ PPDUs to support UL FD A-PPDUs
  New design should incorporate “EHT and EHT+ specific” fields
    E.g., UL BW extension, RU allocation, etc.
Backward compatibility
  HE STA shall not be affected by the new design
Forward compatibility
  New design should be easily extendable for EHT+

## Slide 5: Design Options for Trigger Frame
[Option1] Aggregated-MPDU design
  Define EHT/EHT+ variant of the trigger frame
  To trigger HE, EHT and EHT+ STAs with one PPDU, AP should use the A-MPDU
    E.g., Trigger frame (for HE STA) and trigger frame variant(s) (for EHT and EHT+ STA) are aggregated
[Option2] Single-MPDU design
  [Option 2a] Extend common/user info of the trigger frame by using reserved AID
    Assign specific AID(s) to indicate the common/user info fields for EHT and EHT+ STAs
  [Option 2b] Extend common/user info of the trigger frame by setting AID subfield to 4095
    Use AID 4095 (Start of padding field) for HE STA(s) not to decode EHT/EHT+ information

## Slide 6: Option 1: Aggregated-MPDU Design
Operation example

## Slide 7: Option 1: Aggregated-MPDU Design
Trigger type subfield encoding
  Trigger type subfield is 4-bit in the trigger frame
  MSB of trigger type subfield is currently reserved
  Candidate options for indicating EHT and EHT+ variant
    [1-bit] Use MSB 1-bit as a EHT/EHT+ indication e.g., 0000: HE Basic, 1000: EHT/EHT+ Basic
    [1-subtype] Assign one subfield value. e.g., 8: EHT, 9:EHT+, 10-15: Reserved

## Slide 8: Option 1: Aggregated-MPDU Design
Common info field of EHT variant TF
  If trigger type is EHT Basic Trigger (subtype 8), then the rest of common info field can be re-defined to support EHT information
    E.g., UL BW field can be extended to support 320MHz
  We may include “protocol subfield” to indicate exact amendment instead of assigning separate trigger type value for each amendment after HE
    E.g., 00: EHT, 01:EHT+, …

## Slide 9: Option 1: Aggregated-MPDU Design
User info field of EHT variant TF
  If trigger type is EHT Basic Trigger (subtype 8), then User info field can also be re-defined to support EHT user-specific information
    E.g., RU allocation can be extended to support multi-RU
  We may include “protocol subfield” to indicate exact amendment instead of assigning separate trigger type value for each amendment after HE
    E.g., 00: EHT, 01:EHT+, …

## Slide 10: Option 2a: Single-MPDU Design w/ Reserved AID
Operation example

## Slide 11: Option 2a: Single-MPDU Design w/ Reserved AID
Common/user info field
  stays the same
EHT or EHT+ STAs can obtain the common info field and additionally obtain EHT or EHT+ specific common info
EHT or EHT+ specific common info
  Assign one of the reserved AID (2008-2044, 2047-4094) to indicate EHT or EHT+ common info
  Example of EHT common info field
    EHT STAs obtain EHT-specific common information from the user info field with AID 2008 while HE STAs ignore it
    Length of EHT common info should be the same with that of the user info field since this field reuses the existing user info field format (5-bytes)
  Instead of assigning separate AID for EHT and EHT+ common info, EHT common info field may include protocol subfield to indicate amendment
AID (2008) | EHT UL BW | Other EHT-specific parameters

## Slide 12: Option 2a: Single-MPDU Design w/ Reserved AID
EHT or EHT+ specific user info
  Assign one of the reserved AID (2008-2044, 2047-4094) to EHT or EHT+ user info
  Example of EHT user info field
    EHT STAs obtain EHT-specific user information from the user info field with AID 2010 while HE STAs ignore it
    Additional (EHT) AID field is required to specify EHT STA
    Length of EHT user info should be the same with that of the user info field since this field reuses the existing user info field format (5-bytes)
  Only 2-bytes are free to use per-user info field
  We may need to integrate multiple user info fields for the same (EHT) AID
  Instead of assigning separate AID for EHT and EHT+ user info, EHT user info field may include protocol subfield to indicate amendment
AID (2010) | (EHT) AID | RU allocation | Other EHT user-specific parameters
12-bit
12-bit
16-bit

## Slide 13: Option 2b: Single-MPDU Design w/ AID 4095
Operation example
Notes: byte alignment

## Slide 14: Option 2b: Single-MPDU Design w/ AID 4095
Common/user info field
  stays the same
The user info field with AID 4095 (Start of padding field) in 11ax
  Padding is optionally present to give the recipient STAs enough time to prepare a response
[Proposal] EHT/EHT+ specific common info and user info will be followed by the user info field with AID 4095
  HE STAs believe there are no meaningful information after AID 4095
  EHT STAs will decode after the user info field with AID 4095, since all EHT or EHT+ specific information will be followed
  EHT or EHT+ specific common info and user info format can be re-designed with full flexibility
  The padding AID for EHT/EHT+ STAs should be additionally assigned

## Slide 15: Pros and Cons of Candidates
Summary table
Candidates | Pros | Cons
[Option 1] Aggregate-MPDU | Simple – just adding new trigger variants | Cannot use non-HT duplicate format
[Option 2a] Single-PPDU with the reserved AID | Can use non-HT duplicate format | Overhead of indicating EHT user info
[Option 2b] Single-PPDU with the AID 4095 | Can use non-HT duplicate format High design flexibility (no format limitation of EHT common/user info) | New padding AID required for EHT and EHT+ STA(s)

## Slide 16: Summary
New trigger frame design options to support UL FD A-PPDU
  Aggregate-PPDU approach
  Single-PPDU approach
    Using the user info field with reserved AIDs
    Using the user info field with AID 4095 (Preferred)
We investigate pros and cons of each option

## Slide 17: Straw Poll
Do you support in 11be using user info field with AID 4095 to add EHT/EHT+ common/user info field after the user info field with AID 4095 to trigger A-PPDU comprised of HE and EHT/EHT+ PPDUs?
  EHT+: the amendments after EHT
  The padding AID for EHT/EHT+ STA(s) shall be additionally assigned
  Format of EHT/EHT+ common/user info fields is TBD