## Slide 1: Sounding Request in Sequential Sounding
Date: 2020-06-22
Name | Affiliation | Address | Phone | Email
Ross Jian Yu | Huawei Technologies | F3-6A, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Jason Yuchen Guo |  |  |  | 
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 

## Slide 2: Introduction
In [1], the group has the following motion and passed SP regarding sequential sounding scheme:
  802.11be shall provide a joint NDP sounding scheme as optional mode for multiple-AP systems.
    Sequential sounding scheme that each AP transmits NDP independently and sequentially without overlapped sounding period of each AP can also be used in multi-AP systems.
  [Motion 14, [3] and [57]]
  Do you support that multiple APs can sequentially use an 11ax-like sounding sequence to collect CSI from the in-BSS STAs and OBSS STAs?
    Each AP’s sounding sequence is similar to the 11ax sounding protocol with multiple STAs (NDPA + NDP + BFRP TF + CSI report).
  [20/0123r0 (Channel Sounding for Multi-AP CBF, Feng Jiang, Intel), SP#1, Y/N/A/No answer: 81/4/43/30] [#SP18]

## Slide 3: Sounding Sequence for CBF [2]
For CBF-only multi-AP scenario, an example sounding sequence with two APs is:
  Reuse 11ax sounding sequence
  STA11 to STA1N associate with AP1, STA21 to STA2N associate with AP2
  NDPA1 and NDPA2 includes ID info of STAs in both AP1’s and AP2’s BSS
  In AP1’s sounding sequence, CSI report includes CSI info for NDP1
  In AP2’s sounding sequence, CSI report includes CSI info for NDP2
CSI
report
SIFS
NDP1
Master: AP1
Slave: AP2
STA11
STA1N
SIFS
NDPA2
NDP2
STA21
STA2N
BFRP
Trigger
SIFS
CSI
report
CSI
report
BFRP
Trigger
SIFS
SIFS
…
…
CSI
report
NDPA1
SIFS

## Slide 4: Problem Statement
It is not clear when the slave AP(s) begin its sounding procedure. It is better that the two or more sounding procedures finish within the coherence time. A sounding request frame is needed to notify the slave AP(s) to begin its sounding procedure sequentially.
The two or more sounding procedures are suggested to signal same parameters (e.g., BW, partial BW info parameters, Ng, feedback type etc.), and contain the same targeted STAs, to assist multi-AP/AP coordination transmission.
When the slave AP(s) finish sounding, it is better for them to notify the master AP so that the master AP can initiate the multi-AP/AP coordination transmission.

## Slide 5: Sounding request procedure
The sounding request frame may be transmitted from the master AP to the slave AP(s).
The slave AP(s) then begin to contend the channel, and transmit NDPA frame.
  An alternative special case would be transmit NDPA within the same TXOP, which is less likely
CSI
report
SIFS
NDP1
Master: AP1
Slave: AP2
STA11
STA1N
SIFS
NDPA2
NDP2
STA21
STA2N
BFRP
Trigger
SIFS
CSI
report
CSI
report
BFRP
Trigger
SIFS
SIFS
…
…
CSI
report
NDPA1
SIFS
Sounding
Request
ACK/response
…
CSMA/CA

## Slide 6: Sounding request frame
The sounding request frame may contain the following information:
  Suggested BW, partial BW Info, Ng, feedback type etc.
  Slave AP information (through RA, or AP ID etc.)
  Targeted STAs (in-BSS and OBSS)
The exact details of the contents can be further discussed.
CSI
report
SIFS
NDP1
Master: AP1
Slave: AP2
STA11
STA1N
SIFS
NDPA2
NDP2
STA21
STA2N
BFRP
Trigger
SIFS
CSI
report
CSI
report
BFRP
Trigger
SIFS
SIFS
…
…
CSI
report
NDPA1
SIFS
Sounding
Request
ACK/response
…
CSMA/CA

## Slide 7: Sounding end frame
After one salve AP finishes its sounding procedure. It can transmit a sounding end frame to notify it has finished the sounding procedure with CSI report ready. So that the master AP can initiate the multi-AP/AP coordination transmission.
CSI
report
Master: AP1
Slave: AP2
STA11
STA1N
SIFS
NDPA2
NDP2
STA21
STA2N
BFRP
Trigger
SIFS
CSI
report
SIFS
…
…
ACK/
response
Sounding End
…

## Slide 8: Conclusion
A sounding request frame is introduced and may be transmitted from the master AP to the slave AP(s) to notify the slave AP(s) to do 11ax-like sounding procedure.
The sounding request frame may contain necessary sounding parameters to assist multi-AP/AP coordination transmission.
The sounding end frame may also be transmitted from the slave AP to the master AP to tell the readiness of multi-AP/AP coordination transmission.
The sounding request/end frame is optional.
  May also be transmitted through wired line and is out of the scope of 11be spec.
Regarding sounding, the naming of the master AP or slave APs need further discussion.
  Master AP = sharing AP? Slave AP = shared AP?

## Slide 9: Reference
IEEE 802.11-20/0566r20 Compendium of straw polls and potential changes to the Specification Framework Document
IEEE 802.11-20/0123r1 Channel Sounding for Multi-AP CBF

## Slide 10: SP#1
Do you support that a sounding request frame may be transmitted from one AP to other AP(s) to notify the other AP(s) to do 11ax-like sounding procedure.
  Support of this sounding request frame is optional.
  Detailed contents of the sounding request frame is TBD.
  The naming of the AP(s) is TBD

## Slide 11: SP#2
Do you support that a sounding end frame may be transmitted to notify that the 11ax-like sounding procedure is finished.
  Support of this sounding end frame is optional.
  Detailed contents of the sounding end frame is TBD.