## Slide 1: Triggered P2P for 11be Release 1
Date: 2019-08-23
Authors:

## Slide 2: Abstract
Propose a simple/low-complexity Triggered P2P scheme to be used for 11be R1.

## Slide 3: Introduction
Direct Link transmission => A Direct Link Scheduled (“DLS”) STA communicates directly with another Direct Link Peer STA (“DLP”).
Benefits of Direct Link (“DiL”) transmission [1] :
  high throughput because lower number of transmissions
  low latency due to one hop communication.
Use-case of interest:
  Miracast streaming from laptop to monitor.
  VR applications
  Wireless file transfer from phone to printer.
Slide 3
AP
DiL-A
DLS STA
DLP STA
SIFS
Data
SIFS
Ack
TXOP

## Slide 4: Trigger based DiL sequence benefits
A DiL transmission sequence initiated by a TF transmission has following benefits.
  Increases the chances of either AP or the DiL STA wins a TXOP for DiL transmissions when both contend simultaneously.
  Better medium management at AP as it can serve more than just one DiL STA in a TXOP.
Submission 1117r1 (appendix) mentions some inefficiency of QTP to support Direct link:
  Legacy STA not prevented from channel access.
  AP is not aware of actual resource requests at STA during the QTP period. The initial configuration of schedules may be stale => medium inefficiency.

## Slide 5: Possible Topologies
ESS
Both STAs associated
to same AP.
Only one STA associated
to the Triggering AP.
: Non-AP STA
: AP
Case 1
Case 2
DLS
STA (laptop)
DLP
STA
(wireless monitor)
AP in the ceiling
of an office
DLS
STA (laptop)
DLP
STA
(wireless monitor)
AP in the ceiling
of an office
[Optional]
Another AP in the ESS
Notes: Case 3 is same as general Multi-AP.

## Slide 6: Basic Triggered P2P sequence
AP transmits a TF allocating remaining portion of TXOP to STA.
  Special signaling needed; may be a bit.
Peer STA responds with TBD frame (in TB PPDU) acknowledging the allocation if it wants to use the allocation.
Peer STA uses the allocation for any purpose including peer-to-peer communication.
TF from AP for P2P (Allocate T1)
TBD response frame from peer STA
Data from peer STA to other peer
Ack to peer STA from other peer
T1
TXOP owned by AP

## Slide 7: Summary
Discussed challenges with Triggered P2P operation.

## Slide 8: References
11-18-1481-01-0eht-technology-for-EHT
11-18-2009-06-0rta-rta-report-draft

## Slide 9: Backup slides

## Slide 10: 1117r1: Direct Link issues with 11ax amendments
Direct link provides high “interferences” to the AP
  Direct link traffic carries large amount of data
    Large video transmission for VR, or video streaming.
  Direct link traffic often requires low latency thus frequently accesses the medium.
    Interactive applications (VR, visio conferences, etc.)
Direct link cannot be efficiently scheduled by an AP today
  AP cannot trigger the sending of direct link data, so fine scheduling is not possible.
    Direct link only relies on EDCA.
    Multi User OFDMA doesn’t support Direct link traffic.
  Quiet time period mechanism is not incentive enough
    Every station with direct link traffic will contend on the same period. Even if this period has been negotiated by a STA, the quiet time period is open for all direct link stations
    Other stations with uplink data may also contend during this period (Quiet time period is just intended to give a better priority of medium access for direct link traffic).
    No specific protection against legacy stations.

## Slide 11: Motivation
P2P communication can significantly reduce the load on the BSS and simultaneously the latency by a one-hop communication.
About 70% reduction in
latency/airtime possible in
the two floor home scenario
by using P2P communication among users in the same room.