## Slide 1: 320 MHz/16 SS OM Operation
Date: 2020-06-09
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Danny Alexander |  |  |  | 
Danny Ben-ari |  |  |  | 
Daniel F Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Notes: September 2012

## Slide 2: Background
320 MHz has been agreed to be one of the R1 features [1]
We discuss the required MAC support for 320 MHz/16 SS OM operation
  OM Control in A-Control
  OMN

## Slide 3: Current OM Control
The current Channel Width field only indicates 20/40/80/160 or 80+80
  There is a need to expand the size for Channel Width for one bit
There is also a need to expand the size for Rx NSS/Tx NSTS for at least one bit each
  although 16 SS is in R2, we prefer to have one OM for R1 and R2
There may be a need to include other things in R1
There may be a need to have enough reserved bits to add other things in R2
Having enough bits help us to avoid another design later due to fixed length control information design of A-Control

## Slide 4: Proposal of New OM Control
One entry in Control ID for this new OM Control
Option 1:
  4 bits for Rx NSS
  3 bits for Channel Width
  4 bits for Tx NSTS
  Have Reserved field for the rest
  Remaining fields are the same as the current OM Control
Option 2:
  Just have additional bits to combine with HE OM
Do not reuse existing control ID to avoid complicate hardware implementation
 | Rx NSS | Channel Width | UL MU Disable | Tx NSTS | ER SU Disable | DL MU-MIMO Resound Recommendation | UL MU Data Disable | Reserved
Bits: | 4 | 3 | 1 | 4 | 1 | 1 | 1 | TBD
 | Rx NSS | Channel Width | Tx NSTS | Reserved
Bits: | 1 | 1 | 1 | TBD

## Slide 5: Consideration for two options:
Option 1 stays with the current design principle of A-Control to see everything within one Control Information
Option 2 requires searching for potential EHT OM after seeing HE OM
  The search can be avoided by mandating EHT OM always follows by HE OM
  Receiver can always remove the fixed size including Control ID for HE OM and HE OM Control info
  The proposal is then in principle the same as Option 1 with additional 4 bits of Control ID for HE OM
Either option requires a new control ID for EHT OM
Control ID for EHT OM
EHT OM Control Info
Control ID for HE OM
HE OM Control Info

## Slide 6: OMN element
There is a need to expand the size for Channel Width
Setting for Channel Width and 160 should not be changed when indicating 320 MHz for legacy compatibility if OMN is broadcasted
Similar consideration for Rx NSS
Proposal:
  have additional Channel Width Extension field
  have additional Rx NSS Extension field
  AP can decide to have the extension or not

## Slide 7: Conclusion
To support 320 MHz and 16 SS OM operation, we propose to
  Define new EHT OM Control
  Extend OMN to have Channel Width Extension field and Rx NSS Extension field

## Slide 8: Straw Poll
Do you support to define a new Control ID in A-Control for EHT Operating mode (OM) that enables indication of 320 MHz, Tx NSTS larger than 8, and Rx NSS larger than 8?
  Signaling TBD