## Slide 1: Preamble Puncturing Support for EHT Wide Bandwidth Transmission
Date: 2020-05
Authors:

## Slide 2: Introduction
The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to one or more STAs.
Based on knowledge of VHT and HE, 320MHz non-AP STAs will appear much later than 320MHz AP.
  In order to support small bandwidth devices in a wide bandwidth system, some devices may need to park on non-primary channels to have frame exchanges
It was agreed to allow the punctured channel information carried in U-SIG to vary across different 80MHz channels, i.e. puncturing information in an 80MHz is specific to only that 80MHz. [1]

## Slide 3: Issues
When preamble is allowed to be punctured on any non-primary channels, eg. preamble puncturing is allowed in any one or two 20MHz channels of a non-primary 80MHz segment
  A non-AP STA parking on this segment should be capable of monitoring multiple 20MHz channels for preamble detection, which is much power consuming
  In order to save power, saying a non-AP STA only monitor one 20MHz channel for preamble detection, the allocated resources might be wasted if the 20MHz channel that the non-AP STA monitoring is punctured

## Slide 4: Motivation
  This contribution discusses how to efficiently utilize the allocated resources among multiple users while supporting flexible preamble puncturing for OFDMA transmission.

## Slide 5: Preamble Puncturing Support in EHT BSS
An AP can indicate the channels within its operating bandwidth as disallowed or allowed channels, in which the allowed channels are the candidate preamble detection (PD) channels
  Eg. Disallowed channels are channels that are locally unauthorized for unlicensed use by the AFC at 6 GHz
The position of each candidate PD channel in an 80MHz segment can be indicated eg. using candidate PD channel bitmap
  Each “1” in the bitmap represents one PD channel/allowed channel.
  Each “0” in the bitmap can represent the disallowed channel

## Slide 6: Preamble Puncturing Support in EHT BSS
The following figure shows the examples of candidate PD channels for a non-primary 80MHz segment
  Bitmap pattern “1111”: all four 20MHz channels in the 80MHz segment can be used for preamble detection
  Bitmap pattern “1100”: the 20MHz channels corresponding to “1” in the 80MHz segment can be used for preamble detection
Primary 80MHz
Segment
Non-Primary 80MHz
Segment
Four 20MHz channels
are PD channels
in the non-primary
80MHz segment
Primary 80MHz
Segment
Non-Primary 80MHz
Segment
PD Channels in the non-primary
80MHz segment
Pattern “1111”
Pattern “1100”

## Slide 7: Preamble Puncturing Support in EHT BSS
The candidate PD channels are used to select or to allocate a PD channel for preamble detection for EHT STAs parking in a specific non-primary 80MHz segment
The PD channels for multiple non-AP STAs parking in the same non-primary 80MHz segment could spread over the candidate PD channels in the non-primary 80MHz segment
Primary 20MHz
Non-Primary
80MHz Segment
Primary 80MHz
Segment
STA1’s PD channel
STA2’s PD channel
STA3’s PD channel
STA4’s PD channel
Pattern “1111”
Primary 20MHz
Non-Primary
80MHz Segment
Primary 80MHz
Segment
STA1 and STA3’s PD channel
STA2 and STA4’s PD channel
Pattern “1100”

## Slide 8: Preamble Puncturing Support in EHT BSS
The AP shall follow the rules below when transmitting to STAs parking in non-primary 80MHz segment:
  It shall not transmit on a non-primary 80MHz segment, if all candidate PD channels for the non-primary segment are CCA busy.
  It may transmit on a non-primary 80MHz segment if at least one candidate PD channel for the non-primary 80MHz segment is CCA idle.
  It shall not transmit downlink frame or triggers uplink transmission for a non-AP STA whose allocated/selected PD channel is punctured
  It may transmit downlink frame or triggers uplink transmission for a non-AP STA whose PD channel is not punctured
punctured 20MHz
160MHz BSS
Primary 20MHz
STA1’s PD channel
Punctured TXOP
Non-Primary
80MHz Segment
Primary 80MHz
Segment
STA2’s PD channel
STA3’s PD channel
STA4’s PD channel
RU allocations for
STAs except for STA3

## Slide 9: CCA Reset on PD channel
Since a non-AP STA parking on a non-primary 80MHz segment will not contend the medium, when it detected preambles on its PD channel and the detected preamble is an OBSS PPDU, the STA’s MAC sublayer may issue a PHY-CCARESET.request primitive
  If the OBSS PPDU with RSSI less than ED threshold
  If a PHY-RXEND.indication(CarrierLost) primitive is generated
  If a PHY-RXEND.indication(FormatViolation) primitive is generated
After the MAC issuing the PHY-CCARESET.request primitive to reset the PHY entity to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle. Then STA is able to detect new preamble on its PD channel to receive the PPDU sent by its associated AP

## Slide 10: Conclusion
We believe dynamic puncturing for OFDMA transmission is useful to support non-AP STAs parking in the non-primary 80MHz segment
Preamble detection channel selection or allocation scheme for non-AP STAs parking in the non-primary 80MHz segment is discussed.

## Slide 11: SP1
Do you support that more than one candidate PD channels in each 80MHz segment should be allowed for OFDMA transmission ?

## Slide 12: SP2
Do you support that a non-AP EHT STA parking in a non-primary 80MHz segment can be assigned or select a PD channel from the candidate PD channels?

## Slide 13: SP3
Do you support that when a non-AP EHT STA parking in a non-primary 80MHz segment detected a preamble and determined an OBSS PPDU with RSSI less than ED threshold, its MAC entity may issue a PHY-CCARESET.request primitive to reset the PHY entity to the state appropriate for the end of a received frame and to initiate a new CCA evaluation cycle?

## Slide 14: Reference
[1] 11-20-0566-34-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document