## Slide 1: Multi-link Group Addressed Data Frame Delivery Follow up
Date: 2020-05-28
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Daniel Bravo |  |  |  | 
Laurent Cariou |  |  |  | 
Notes: September 2012

## Slide 2: Background
We have discussed the “miss” and “duplicate” group addressed data frame problem when switching the selected link to receive group addressed data frame in the past
  Note that there are strong opinions that this has to be achieved without the need of non-AP MLD to indicate the selected link to receive group addressed data frame to AP MLD
We provide a follow up in attempt to close the topic

## Slide 3: Basic non-AP MLD behavior for receiving group addressed frame
Non-AP MLD can choose not to receive group addressed data frame
  This is an extension from the existing spec that ReceiveDTIM can be false
If non-AP MLD chooses to receive group addressed data frame, then
  A non-AP MLD shall follow the baseline rules to receive the group addressed data frames on one link selected by the non-AP MLD
  The non-AP MLD may change the selected link at any time except during an ongoing group addressed delivery period
  AP MLD duplicates a group addressed data frame that is expected to be received by the non-AP MLD and schedules for transmission in all the setup links with the non-AP MLD
TBD for the proposal that a non-AP MLD indicates the selected link to the AP MLD

## Slide 4: Condition to Avoid “Miss” Group addressed data frame
Under the condition that AP MLD will duplicate group addressed data frame if non-AP MLD does not indicate the selected link to receive group addressed data frame
Based on this condition, non-AP MLD can avoid missing group addressed data frame if non-AP MLD switching the link right after seeing AP of the selected link indicates there is no buffered group addressed data
  The indication is provided by AID 0 in TIM or corresponding group addressed bit under multiple BSSID
  The indication is also provided by more data bit in group addressed data frame
Proposal:
  Non-AP MLD should switch the selected link to receive group addressed data frame right after seeing the corresponding AP of the link indicates there is no buffered group addressed BUs to avoid missing reception of group addressed data frame

## Slide 5: Example
TIM bit 0 =0
Change link to receive group addressed data frame and there will be no miss
DTIM
DTIM

## Slide 6: Condition to avoid duplicate Group addressed data frame
There are opinions that avoiding group addressed data frame cannot be ignored
Under the condition that we follow the baseline and switch after the end of group addressed data delivery period, duplicate in a different link only happens if there are duplicate group addressed data (if any) to be transmitted at that point in the different link
Proposal: each AP affiliated with an AP MLD indicates if other APs affiliated with the same AP MLD has buffered group addressed data frames that are duplicated across links
  If a non-AP MLD wants to switch the selected link to receive group addressed data frame, the non-AP MLD should switch the selected link if the AP corresponding to another link does not have buffered group addressed data that are duplicate across links to avoid duplicate reception of group addressed data frame

## Slide 7: Example
Indicate another link does not have buffered group addressed data that are duplicate across links
Change link to receive group addressed data frame and there will be no duplicate
DTIM
DTIM

## Slide 8: Conclusion
We discuss the basic operation of non-AP MLD to receive group addressed data frame
We discuss the miss and duplicate solution for receiving group addressed data frame
We propose that a non-AP MLD switches the link to receive group addressed data frame right after seeing the indication of no buffered group addressed BUs to avoid missing group addressed data frame
We propose that an AP indicates if other APs in the same AP MLD has buffered duplicate group addressed data frame to be delivered, and a non-AP MLD switches the link to receive group addressed data frame right after seeing another link without buffered duplicate group addressed data frame to avoid duplicate group addressed data frame

## Slide 9: SP #1
Do you support that in R1 if non-AP MLD chooses to receive group addressed data frame?
  A non-AP MLD shall follow the baseline rules to receive the group addressed data frames on one link selected by the non-AP MLD
  The non-AP MLD may change the selected link at any time except during an ongoing group addressed delivery period
  AP MLD duplicates a group addressed data frame that is expected to be received by the non-AP MLD and schedules for transmission in all the setup links with the non-AP MLD

## Slide 10: SP #2
Do you support that in R1 if a non-AP MLD wants to switch the selected link to receive group addressed data frame, the non-AP MLD should switch the selected link right after seeing the corresponding AP of the selected link indicates there is no buffered group addressed BUs to avoid missing reception of group addressed data frame?

## Slide 11: SP #3
Do you support that in R1, each AP affiliated with an AP MLD indicates if other APs affiliated with the same AP MLD has buffered group addressed data frames that are duplicated across links?
  If a non-AP MLD wants to switch the selected link to receive group addressed data frame, the non-AP MLD should switch the selected link if the AP corresponding to another link does not have buffered group addressed data that are duplicate across links to avoid duplicate reception of group addressed data frame?