## Slide 1: Enhanced Non-STR MLD operation
Date: 2020-06-10
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Insun Jang | LG Electronics |  | insun.jang@lge.com
Taewon Song | LG Electronics |  | taewon.song@lge.com
Namyeong Kim | LG Electronics |  | namyeong.kim@lge.com
Jinsoo Choi | LG Electronics |  | js.choi@lge.com

## Slide 2: Recap: Non-STR MLD operations (1/2)
We agreed with the concept of non-STR non-AP MLD in SFD[1]
Regarding a pair of links with non-STR, when a STA of a non-AP MLD receives a DL frame for the STA on one link, if other STA of the same MLD transmits an UL frame on the other link, the DL frame reception may be failed due to the UL TX interference
To avoid that interference, it’s recommended that a STA of an non-STR non-AP MLD should not transmit an UL frame on one link while the other STA of the same MLD receives a DL frame for the STA
AP 1
STA 1
AP 2
STA 2
DL frame (AP1 -> STA1)
STR AP MLD
: AP 1, AP2
Non-STR non-AP MLD
: STA 1, STA 2
UL frame (STA2 -> AP2)
Interference

## Slide 3: Recap: Non-STR MLD operations (2/2)
For the same purpose, basically, an AP MLD will also not trigger a STA in non-STR non-AP MLD while the AP MLD transmits a DL frame to the other STA of the same non-AP MLD
Then non-STR operations will have lower performance than STR operations
Based on the operating maximum bandwidth and maximum power, the only fixed STR/Non-STR indication could make lower performance
  Fixed STR/non-STR indication means that STA MLD just inform AP MLD of which link sets are STR or non-STR
    E.g.,) Non-STR for a pair of link 1 and 2, non-STR for a pair of link 2 and 3, STR for a pair of link 1 and 3, etc.
  Because in this case STA MLD should perform non-STR operation even in dynamic STR/non-STR cases (see next slides)
We propose the method for improving the performance of non-AP MLD with non-STR links

## Slide 4: Dynamic STR/non-STR case (1/2)
According to bandwidths or center frequency offsets, a pair of links can be either STR or non-STR
Example
BWs of two links (160, 160)
160 MHz
160 MHz
Link1
Link2
Non-STR
160 MHz
80 MHz
Non-STR
160 MHz
80 MHz
Non-STR
BWs of two links (160, 80)
BWs of two links (80, 160)
80 MHz
STR
BWs of two links (80, 80)
80 MHz

## Slide 5: Dynamic STR/non-STR case (2/2)
STA’s TX power can be considered for selection of STR or non-STR
Different power info can be used according to different BWs
BWs of two links (160, 160)
160 MHz
Link1
Link2
Non-STR in maximum TX power (X dBm)
160 MHz
80 MHz
BWs of two links (160, 80)
BWs of two links (160, 80)
160 MHz
80 MHz
160 MHz
Recommended TX power for STR
(X – 30) dBm
(X – 20) dBm
(X – 10) dBm
Link1
Link2
Non-STR in maximum TX power (X)
TX power (x)
 Non-STR
TX power (x-y)
 STR
Non-STR area
STR area
x
y
x-y
TX power

## Slide 6: Enhanced non-STR MLD operation (1/7)
Non-AP MLD can inform its AP MLD of STR/non-STR capability for each pair of links
  STR/non-STR capability : information for indicating whether a pair of links is STR capable or not (i.e., non-STR) based on the maximum operating bandwidth and the maximum STA’s TX power
The Non-AP MLD can inform AP MLD of the following information to enable STR operation for the link set indicated as non-STR
  Bandwidth combinations for two links according to corresponding STA’s TX power
link1 & link2 | link2 & link3 | …
Non-STR | STR | STR
For link1 & link2 |  | 
TX power info (dBm) | BWs for two links | Descriptions (link 1, 2) for BWs
Full TX power (X) | <= (40MHz, 40MHz) | (20, 20), (20, 40), (40, 20), (40, 40)
X- 10 | <= (80MHz, 80MHz) | <(40,40) + (20, 80), (40, 80) , (80, 20), (80, 40), (80, 80)
X- 20 | < =(160, 160) | <(80,80) + (20, 160), (40, 160) , (80, 160), (160, 20), (160, 40), (160, 80), (160, 160)
… | … | ….

## Slide 7: Enhanced non-STR MLD operation (2/7)
Example
Non-AP MLD can decide the number of non-STR link sets and the number of the combinations of TW Power info and the corresponding BW info per each link set
If the two links are very close each other, two links will always be non-STR regardless of STA’s TX power and BW combinations information and in this case, non-AP MLD will not inform AP of any information for the link set
Non-AP MLD
AP MLD
Multi-link Setup Request
(…, STR possible info (TX PWs & BWs) for 1st non-STR link set, …)
Multi-link Setup Response
MLO discovery

## Slide 8: Enhanced non-STR MLD operation (3/7)
In 11ax, when an AP triggers TB PPDU, AP can control the TX power of the scheduled STA(s) (i.e., STA can reduce its power) using the UL Target RSSI subfield of User Info field
The AP MLD can trigger a STA in an MLD using the received TX power and BWs Info while the AP MLD transmits DL frame to the other STA in the same STA MLD
  If the received STA’s TX power info is higher than or equal to the STA’s power value expected by the AP (i.e., UL Target RSSI for the STA), the AP will trigger the STA using the expected TX power value(i.e., UL Target RSSI) and allocate UL RU within bandwidth information (see the next slide)
  Otherwise, the AP will not trigger the STA for TB PPDU transmission because if AP reduces the STA’s TX power to the lower value than the expected value, then AP will fail to decode the UL frame

## Slide 9: Enhanced non-STR MLD operation (4/7)
Example (1/3)
  Based on the information, AP decides UL RU size of the STA and controls the STA’s Power in the Trigger frame
AP 1
STA 1
AP 2
STA 2
DL frame (AP1 -> STA1, 40MHz BW)
STR AP MLD
: AP 1, AP2
Non-STR non-AP MLD
: STA 1, STA 2
TB PPDU (STA2 -> AP2)
(TX power setting based on Z)
No Interference
TF
TX Power of STA 2 <= y (e.g., Z) dBm,
RU of the STA is allocated in the 40MHz
ML Setup REQ
(TX power = y dBm, BWs= (40MHz,40MHz) )
ML Setup RSP

## Slide 10: Enhanced non-STR MLD operation (5/7)
Example (2/3)
  Based on the information, an AP MLD decides the bandwidth of DL PPDU on link1 while the AP MLD receives UL PPDU on link 2
AP 1
STA 1
AP 2
STA 2
DL frame (AP1 -> STA1, 20MHz BW)
STR AP MLD
: AP 1, AP2
Non-STR non-AP MLD
: STA 1, STA 2
UL frame (STA2 -> AP2, 20MHz BW)
No Interference
ML Setup REQ
(TX power = X dBm, BWs= (20MHz, 20MHz) )
X= max TX Power
ML Setup RSP

## Slide 11: Enhanced non-STR MLD operation (6/7)
Example (3/3)
  STA can include the reduced TX power in UL frame
  Based on the information, an AP MLD decides the bandwidth of DL PPDU on link1 while the AP MLD receives UL PPDU on link 2
AP 1
STA 1
AP 2
STA 2
DL frame (AP1 -> STA1, 20MHz BW)
STR AP MLD
: AP 1, AP2
Non-STR non-AP MLD
: STA 1, STA 2
UL frame (TX PW= YdBm,
STA2 -> AP2, 20MHz BW)
No Interference
Y dBm= X – 20dBm
X= max TX Power
ML Setup REQ
(TX power = X dBm, BWs= (20MHz, 20MHz) )
ML Setup RSP

## Slide 12: Enhanced non-STR MLD operation (7/7)
If the STA does not inform AP of the recommended power information, the AP can not know whether TB PPDU can interfere with the DL TX sent on other link or not
So, AP will not trigger the STA for UL TB PPDU simply  Same as basic non-STR operation
That is, if the non-STR STA MLD wants to have more UL TX opportunities, the STA MLD will inform AP MLD of the STA’s TX power info and BW combination info for STR
AP MLD can send DL frame to non-STR non-AP MLD on one link while the AP MLD receives UL frame from the non-AP MLD on the other link
The more DL/UL TX opportunities of non-STR non-AP STA, the better latency as well as better throughput of non-STR STA MLD

## Slide 13: Conclusion
Generally non-STR operation has lower performance than STR operation
We can improve the performance of non-STR operation through the following simple mechanism
  Non-STR STA MLD informs AP MLD of the recommended STA’s TX power info and BWs combination info(of two links) for STR operation
  Based on the received information for the STR operation,
    AP MLD can trigger a STA of non-STR non-AP MLD while the AP transmits DL frame to another STA of the STA MLD
    AP MLD can send DL frame to non-STR non-AP MLD on one link while the AP MLD receives UL frame from the non-AP MLD on the other link
By this operation, non-STR STA MLDs have more UL TX opportunities so that the latency and throughput of the MLDs will be enhanced

## Slide 14: Straw Poll 1
Do you agree the following?
  Non-AP MLD can inform its AP MLD of STR/non-STR capability for each pair of links
    STR/non-STR capability: information for indicating whether a pair of links is STR capable or not (i.e., non-STR) based on the maximum operating bandwidth and the maximum STA’s TX power

## Slide 15: Straw Poll 2
Do you agree the following?
  Non-STR non-AP MLD can transmit to AP MLD the information for enabling the STR operation of the non-AP MLD during the multi-link setup

## Slide 16: Straw Poll 3
Do you agree the following?
  Non-STR non-AP MLD can provide AP MLD with the STA’s TX power and the corresponding bandwidth combinations information for STR operation

## Slide 17: Straw Poll 4
Do you agree the following?
  Upon receiving the STA’s TX power and BWs Info for STR operation from a non-STR non-AP MLD, the AP MLD can trigger a STA of the non-AP MLD while the AP MLD transmits DL frame to the other STA of the non-AP MLD

## Slide 18: Straw Poll 5
Do you agree the following?
  When a non-STR non-AP MLD transmits an UL frame on a link, the MLD may reduce the TX power for the UL frame and may include the reduced TX power info in the UL frame