## Slide 1: Discussion about STR Capabilities Indication
Date: 2020-06-20
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yuchen Guo |  |  |  | 
Yifan Zhou |  |  |  | 
Guogang Huang |  |  |  | 
Yiqing Li |  |  |  | 
Ming Gan |  |  |  | 
Meihong Zhang |  |  |  | 
Notes: September 2012

## Slide 2: Background
There is a STR capability indication related Motion passed
  A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
    NOTE 1 – The 2 links are on different channels.
    NOTE 2 – Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.
    [Motion 38, [3] and [38]]
Base on the Motion text and discussion, some people may treat it as a simple indication. I.e. a pair of link for between two MLD is either STR or non-STR;
But actually STR/non-STR depends on many issues, we will discuss some of them in this presentation.
Presentation [1], [2] and [3] discussing the similar issue.

## Slide 3: Directionality of STR Capabilities
Depends on different parameter setting, the transmission on link1 may interfere the reception on link2, while the transmission on link2 not interfere the reception of link1;
Example 1: link 1 with 80MHz BSS bandwidth and link2 with 20MHz BSS bandwidth.
  Very different spectrum mask for different bandwidth
Example 2: link 1 with high transmit power, while link2 with lower transmit power.
  Because of regulation or other reasons.
80MHz
20MHz

## Slide 4: Directionality of STR Capabilities
There may have two types of potential solutions;
Opt 1: indicate STR capability for both directions
  Indicate STR capabilities for link1 TX to link2 RX (link1link2), and for link2 TX to link1 RX (link2link1), respectively for each link pair
Opt 2: if non-STR on at least one direction, this link pair is non-STR
  Indicate non-STR for a link pair when (link1link2) is non-STR, or (link2link1) is non-STR, or both direction are non-STR
We prefer Opt 2 for below reasons
  Opt 1 has larger signaling overhead
  Most of the transmission has a response frame (Data/Ack, RTS/CTS,…), once any direction is non-STR, PPDU end sync is required. So it doesn’t need to distinguish which direction is non-STR.

## Slide 5: Discussion of STR
When the frequency gap is smaller than Δf1, PPDU1 transmission on link1 will block reception of PPDU2 (whatever parameters are used) in link2, it can clearly be called non-STR;
When the frequency gap is larger than Δf2, PPDU1 transmission on link1 has negligible interference to the reception of PPDU2 in link2, it can clearly be called STR;
When the frequency gap is between Δf1 and Δf2, PPDU2 can be correctly received for some parameter setting, but will be failed for other parameter setting. How to defined STR capability for this case?
  E.g. successful for MCS0 while failed for MCS 9
  E.g. successful for PPDU BW= 20MHz, while failed for PPDU BW = 160MHz
Frequency gap between two links
Non-STR
STR
STR or non-STR?
Δf1
Δf2

## Slide 6: Discussion of STR
Since it can not clearly indicate STR or non-STR, in order to solve this problem, it may needs to introduce a parameter to indicate the Cross Link Interference (CLI) level;
Below is an example Cross Link Interference subfield.
Cross link interference subfield | Meaning
0 | <-82dBm
1 | [-82, -79)dBm
2 | [-79, -76)dBm
3 | [-76, -73)dBm
… | …
… | …
14 | [-43, -40)dBm
15 | >=-40dBm

## Slide 7: How to Measure CLI
The CLI will affected by the TX power in link1, Bandwidth in link1 and Bandwidth in link2;
TX power may changes per PPDU, and most frames don’t carry a TX power indication, so it is better only consider max (or fixed) TX power when measure CLI;
Bandwidth is a factor that could be considered when measure CLI
  In 11be, Bandwidth can changes between 20MHz and 320MHz, it will greatly changes the frequency gap between two links, as well as the power spectral density. So it will greatly affect the CLI measurement;
  The STA may changes it bandwidth during operation, e.g. through OMI;

## Slide 8: How to Measure CLI
Opt 1: CLI measured for [operating bandwidth in link1, operating bandwidth in link2];
  Pros: Single CLI value, overhead is low
  Cons: Need to update once operating channel changes in either of the two links
Opt 2: multiple CLI measured for each combination of [bandwidth in link1, bandwidth in link2]
  Pros: Doesn’t need to update when operating channel changes
  Cons: larger overhead compare to Opt1
The CLI could report during the association phase, since it may just report one time, the signaling overhead is not a big burden.

## Slide 9: Relationship between CLI and STR
Opt 1: replace STR indication
  May need AP to broadcast a CLI threshold (or defined the threshold in spec) to determine STR or non-STR
Opt 2: CLI + STR
  A non-AP MLD determines it is STR or non-STR by itself
  Suggest to indicate as non-STR when PPDU reception will be blocked under at lease some parameter setting
  CLI information can help AP MLD to make the scheduling or channel access more flexible

## Slide 10: An Example of how to use CLI
In below example, the non-AP MLD reports CLIs for each combination of bandwidth in two links;
Base on the CLI values, if AP MLD constrain the bandwidth of one link not larger than 20MH, it will be STR for the two links for this non-AP MLD;
  AP MLD can treat this non-AP MLD as STR MLD, once it use an bandwidth or RU that is equal or less than 20MHz.
  When AP MLD choose the bandwidth in link2 according the PPDU bandwidth in link1, it can get more extra flexibility. E.G. if 40MHz is used in link1, AP MLD can treat non-AP MLD as STR MLD if it constrain the bandwidth (or RU) within 40MHz in link2.
 | 20MHz | 40MHz | 80MHz | 160MHz
20MHz | <-82dBm | <-82dBm | <-82dBm | <-82dBm
40MHz | <-82dBm | <-82dBm | -72dBm | -52dBm
80MHz | <-82dBm | -72dBm | -62dBm | -42dBm
160MHz | <-82dBm | -52dBm | -42dBm | >=-42dBm
BW in Link 2
BW in Link 1
Note: The CLI values are not from real measurement, just an example

## Slide 11: Summary
Some issues that will affect the STR capability of a MLD are discussed;
STR capability has directionality. Suggest that if at least one direction is non-STR, this MLD will be treat as a non-STR MLD;
STR capability can not clearly indicated in some case. Propose to introduce an indication of cross link interference;
Operating bandwidth will significantly affect the STR capability, so suggest to consider bandwidth when report STR capabilities.

## Slide 12: Reference
[1] 11-20/809r0 STR capability report
[2] 11-20/ 527r0 Multi-link Constraint Signaling
[3] 11-20/ 909r0 Enhanced Non-STR MLD Operation

## Slide 13: Straw Poll 1
Do you agree that if a MLD can support transmission on link 1 concurrent with reception on link2, but can not support transmit on link2 concurrent with reception on link1, this pair of links will be non-STR?
Y/N/A: 36/10/27

## Slide 14: Straw Poll 2
Do you support that a MLD indicates the STR capability of each link pair as below?
  Mandatory to use 1 bit to indicate the link pair is STR or non-STR
  If non-STR, optional to indicate other TBD parameters that describe the non-STR constraints.
  Y/N/A:

## Slide 15: Straw Poll 3
Do you support the other parameters to include cross link interference level?
  The name and format of cross link interference level can be further discussed.
Y/N/A: