## Slide 1: Channel Access for Constrained MLD
Date: 2020-06-20
Authors:
Name | Affiliations | Address | Phone | Email
Yiqing Li | Huawei | Shenzhen, China |  | liyiqing3@Huawei.com
Yunbo Li |  |  |  | 
Ming Gan |  |  |  | 
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yifan Zhou |  |  |  | 
Meihong Zhang |  |  |  | 

## Slide 2: Introduction
Terminology
  STR (simultaneous transmit and receive)
    An MLD that supports transmission on one link concurrent with reception on the other link for each pair of links
  non-STR
    An MLD that does not support transmission on one link concurrent with reception on the other link for each pair of links
Different channel access mechanisms were proposed to synchronize PPDUs for non-STR MLD
  Fully synchronization transmission
    Opt 1: single primary link EDCA + other secondary links do PIFS access
    Opt 2: multiple primary links EDCA + primary links can also do PIFS access
      This option has fairness issues (detail explanation is in the next page)
      Opt 2.1: multiple primary link + PIFS access + fairness compensation
  End time aligned transmission
    Opt 3: Independent Access on each link
In this contribution, we discuss the channel access mechanisms for non-STR MLD in order to guarantee the fairness.

## Slide 3: Recap: Fairness Issues for Fully Synchronized Transmission
Fairness Issues: for fully synchronized transmission, allowing full backoff on one link and PIFS access on another link provides more channel access opportunities for MLD than that for legacy devices.
Different Synchronized Transmission Channel Access methods regarding fairness have been proposed.
  Opt.1: Remain backoff counter threshold for limiting PIFS access along with PD/NAV check [1]
  Opt.2: Toggle full backoff link [2]
  Opt.3: Store the remain backoff counter for PIFS access. The suspended backoff counter value is added in the next EDCA transmission [2][3].
Fairness issues are not the first time to be discussed in IEEE 802.11 spec.

## Slide 4: Recap: MU EDCA for fairness issues in 802.11ax
Fairness Issues in 802.11ax: HE STAs have more channel access opportunities due to the trigger based channel access methods besides EDCA than legacy STAs.
  Similar with what we have for fully sync. transmission as MLDs acquiring more channel access chances than legacy devices due to PIFS access besides EDCA.
Solutions already in 802.11ax: To define MU EDCA parameters for non-AP HE STA that receives a Basic Trigger frame that contains a User Info field addressed to the STA. (See Section 26.2.7 in Draft P802.11ax_D6.0)
  The HE STA shall update its CWmin[AC], CWmax[AC], AIFSN[AC] and MUEDCATimer[AC] state variables.
For now, we can follow the direction of MU EDCA channel access mechanisms to propose the fairness compensation methods for PIFS access.

## Slide 5: Proposal 1: Fairness Compensation Methods for PIFS access - non-STR EDCA Parameters set
Based on what we have in 802.11ax as MU EDCA channel access mechanism, we propose to define a new EDCA parameters set and a new timer which can be named as non-STR EDCA Parameters set and PIFSAccessTimer[AC].
Each link performs Independent EDCA. If backoff on one link completes for sync. transmission and PIFS check passes on other links, all these links change the EDCA parameters set to non-STR EDCA parameters set for the next transmission during PIFSAccessTimer[AC].
  PIFSAccessTimer[AC] as the time of applying non-STR EDCA parameters set
  E.g., Once the AP 1 has full backoff and AP 2 has used the PIFS access, during the PIFSAccessTimer[AC], non-STR EDCA parameters set is applied for both AP 1 and AP 2 for the next transmission.

## Slide 6: Proposal 1: Fairness Compensation Methods for PIFS access - non-STR EDCA Parameters set (Cont.)
Discussion about PIFSAccessTimer[AC]
  Each link has its own PIFSAccessTimer[AC] value?
    PIFSAccessTimer[AC] is link based (Preferred).
    PIFSAccessTimer[AC] is MLD based.
  About the decreasing rule
    The timer decreases by time regardless of the channel state, aligned with MUEDCATimer[AC] (Preferred).
    The timer decreases when the channel is idle, same as the backoff counter.
  If one link is still in back off when its PIFSAccessTimer[AC] reaches 0, the device can change back to EDCA parameters set while remaining the ongoing backoff counter value.
  If one link applies PIFS access during PIFSAccessTimer[AC], its PIFSAccessTimer[AC] will be refreshed.
    The link which completes backoff procedure resulting in other links PIFS accessing should set up PIFSAccessTimer[AC] or refresh it if the timer is non-zero.
  AP can broadcast its non-STR EDCA Parameters set and PIFSAccessTimer[AC] in beacon frames or in probe response/request
    Both non-STR EDCA Parameters set and PIFSAccessTimer[AC] can have default values.

## Slide 7: Proposal 2: Fairness Compensation Methods for PIFS access – DisallowTimer
In order to limit the PIFS access behaviors, we propose to define a new timer which can be named as DisallowTimer[AC].
  Simpler and cleaner than proposal 1.
Each link performs Independent EDCA. If one link is PIFS access for the last sync. transmission, set a DisallowTimer[AC] during which PIFS access in not allowed on this link.
  DisallowTimer[AC] can have default values. Additionally, it can be set and broadcasted by AP in beacons or Probe response/request.
  The timer decreases by time regardless of the channel state or decreases when the channel is idle
The link can do PIFS access when DisallowTimer[AC] value reaches 0.

## Slide 8: Summary
For 802.11ax, MU EDCA parameters are defined to solve the fairness issues that HE STAs acquiring more channel access opportunities than legacy STAs.
Following this direction, to deal with similar fairness issues in fully synchronized transmission for constrained MLD, we propose to define a non-STR EDCA parameters set and a PIFSAccessTimer[AC].
  If backoff on one link completes for sync. transmission and PIFS check passes on other links, all these links change to non-STR EDCA parameters set for the next transmission during PIFSAccessTimer[AC].
As another simpler and cleaner option, we propose to define a DisallowTimer to limit the PIFS access behaviors during which PIFS access is not allowed on that link.

## Slide 9: Reference
[1] IEEE802.11-20/26r6, “MLO: Sync PPDUs”
[2] IEEE802.11-20/487r5, “Multiple Link Operation Follow Up”
[3] IEEE802.11-20/638r0, “STR AP Sync. PPDU Transmission”