## Slide 1: Consideration on User-specific field in EHT-SIG
Date: 2020-06-23
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
June 2020

## Slide 2: Introduction
Based on the 11be SFD, we have achieved the following agreements.
  “802.11be supports a maximum of 16 spatial streams (total across all the scheduled STAs) for MU-MIMO.”
  “802.11be defines a maximum of 16 spatial streams for SU-MIMO.”
  “The following subfields exist in U-SIG and/or EHT-SIG of an EHT PPDU sent to single user:
    MCS, NSTS, GI+EHT-LTF Size, Coding
In addition, during the previous conference call, the following was agreed.
  “For an EHT MU-MIMO transmission, the maximum number of Spatial Streams allocated to each MU-MIMO scheduled non-AP STA is 4.”
In this contribution, we investigate the signaling regarding the number of spatial streams when MU PPDU is used by considering the above agreements. Also, we deal with the configuration of the user-specific field in EHT-SIG field.

## Slide 3: 11be MU PPDU
Regarding the MU-PPDU , the followings have agreed.
  “A PPDU that is sent to multiple user is configured as follows:
    L-STF, L-LTF, L-SIG, RL-SIG, U-SIG, EHT-SIG, EHT-SIG, EHT-STF, EHT-LTF, DATA
    Additional fields are TBD”
  “The EHT-SIG (immediately after the U-SIG) in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s).
    Special case compressed modes (e.g., full BW MU-MIMO) are TBD.”

## Slide 4: Configuration of User-specific field(1/2)
According to passed motion, the EHT-SIG consists of the common field and the user-specific field in MU-PPDU.
  And, the user-specific field includes the information for multiple users.
  In 11ax, the user-specific field consists of user block fields that contain information for STAs that is used to decode their payloads.
    The user block field is made up of 2 user fields.
Since we consider the signaling way that is similar to 11ax in MU transmission, we can consider applying the same design way into the user-specific field of EHT-SIG.

## Slide 5: Configuration of User-specific field(2/2)
The common field includes tail bits enabling the receiver to immediately decode this field.
The user-specific field is consists of 2-user block fields, where each block field contains a CRC.
  Each block field includes tail bits that enable the receiver to decode that block field without waiting until the end of EHT-SIG.
  The performance of the user block field consists of 2-user fields has been verified in 11ax TG[2].
EHT-SIG content channel
Common field
User-specific field
2 users + CRC + Tail
…
2 users + CRC + Tail
1/2 users + CRC + Tail
Common bits (+ CRC) +Tail
1 BCC Block
1 BCC Block
User block field
1 BCC Block
1 BCC Block

## Slide 6: Signaling of spatial stream
In 11ax MU PPDU, the number of spatial streams are indicated from HE-SIGB.
  In MU transmission, a field of user field in HE-SIGB is used and this field is defined differently according to MU-MIMO allocation.
    a non-MU-MIMO allocation
    a MU-MIMO allocation
Similar to 11ax, the information for the number of spatial streams are indicated by using a subfield of user field in user-specific field of EHT-SIG field in MU-PPDU.

## Slide 7: Spatial stream configuration field
For MU-MIMO allocation, the number of spatial streams allocated to STA can be indicated by the spatial stream configuration field in the user field.
  The spatial stream configuration field can be configured by considering the following included in passed motions.
    Total number of spatial streams : 16
    Maximum number of users for MU-MIMO : 8
    The maximum number of Spatial Streams allocated to each MU-MIMO scheduled STA : 4
  As shown in the appendix, taking account of all cases(i.e., all combinations of the number of users and the number of spatial streams), it can be indicated by using the 6bits information.
    The required maximum number of indications is 54 when N_user is 6.
  Therefore, to indicate the assigned number of the spatial streams to STA for MU-MIMO, the spatial stream configuration field in the user field consists of 6bits.

## Slide 8: Summary
The User-specific field of EHT-SIG in EHT MU-PPDU can be configured with a user block field like 11ax.
  By taking into account the overhead, performance and decoding complexity, the user block field can be made up of 2 user fields .
The information for the number of spatial streams in EHT MU-PPDU is contained in the user field of the user-specific field in EHT-SIG.
  For MU-MIMO operation, the spatial stream configuration field of user field is used to indicate the allocated number of spatial streams to STA.
  And, the spatial stream configuration field consists of 6bits.

## Slide 9: Straw poll #1
Do you agree that the common field of EHT SIG in EHT PPDU that is sent to multiple user includes the CRC and tail bits?
  The number of bits for CRC is TBD.
  The number of tail bits is 6.
  The configuration of the common field is TBD.
  Y/N/A

## Slide 10: Straw poll #2
Do you agree that the user-specific field of EHT SIG in EHT PPDU that is sent to multiple user consists of the user block field(s) that is made up of 2 user fields?
  The user block field includes the CRC and tail bits.
    The number of bits for CRC is 4.
    The number of tail bits is 6.
  Y/N/A

## Slide 11: Straw poll #3
Do you agree that the user field in EHT PPDU that is sent to multiple user includes the a subfield that indicates the number of spatial streams for each user.
  For MU-MIMO allocation
    Spatial Configuration
      Indicates the number of spatial streams for a user in MU-MIMO allocation
  For non-MU-MIMO allocation
    NSTS
  Y/N/A

## Slide 12: Straw poll #4
Do you agree that the Nsts subfield of user field for non-MU-MIMO allocation consists of 4bits?

## Slide 13: Straw poll #5
Do you agree that the spatial configuration subfield of user field for MU-MIMO allocation consists of 6bits?
  Y/N/A

## Slide 14: Straw poll #6
Do you agree that the spatial configuration subfield is defined as described in slide 14~16?
  Y/N/A

## Slide 15: Reference
[1] 11-20/556r26, Compendium of straw polls and potential changes to the Specification Framework Document,(Edward Au, Huawei )
[2] 11-15/1059r2, SIG-B Encoding Structure Part II, (Ron Porat, Broadcom )

## Slide 16: Appendix

## Slide 17: Spatial configuration (1/3)
Nuser | B5…B0 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
2 | 000000-000011 | 1-4 | 1 |  |  |  |  |  |  | 2-5 | 10
 | 000100-000110 | 2-4 | 2 |  |  |  |  |  |  | 4-6 | 
 | 000111-001000 | 3-4 | 3 |  |  |  |  |  |  | 6-7 | 
 | 001001 | 4 | 4 |  |  |  |  |  |  | 8 | 
3 | 000000-000011 | 1-4 | 1 | 1 |  |  |  |  |  | 3-6 | 20
 | 000100-000110 | 2-4 | 2 | 1 |  |  |  |  |  | 5-7 | 
 | 000111-001000 | 3-4 | 3 | 1 |  |  |  |  |  | 7-8 | 
 | 001001 | 4 | 4 | 1 |  |  |  |  |  | 9 | 
 | 001010-001100 | 2-4 | 2 | 2 |  |  |  |  |  | 6-8 | 
 | 001101-001110 | 3-4 | 3 | 2 |  |  |  |  |  | 8-9 | 
 | 001111 | 4 | 4 | 2 |  |  |  |  |  | 10 | 
 | 010000-010001 | 3-4 | 3 | 3 |  |  |  |  |  | 9-10 | 
 | 010010 | 4 | 4 | 3 |  |  |  |  |  | 11 | 
 | 010011 | 4 | 4 | 4 |  |  |  |  |  | 12 | 
4 | 000000-000011 | 1-4 | 1 | 1 | 1 |  |  |  |  | 4-7 | 34
 | 000100-000110 | 2-4 | 2 | 1 | 1 |  |  |  |  | 6-8 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 |  |  |  |  | 8-9 | 
 | 001001 | 4 | 4 | 1 | 1 |  |  |  |  | 10 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 |  |  |  |  | 7-9 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 |  |  |  |  | 9-10 | 
 | 001111 | 4 | 4 | 2 | 1 |  |  |  |  | 11 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 |  |  |  |  | 10-11 | 
 | 010010 | 4 | 4 | 3 | 1 |  |  |  |  | 12 | 
 | 010011 | 4 | 4 | 4 | 1 |  |  |  |  | 13 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 |  |  |  |  | 8-10 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 |  |  |  |  | 10-11 | 
 | 011001 | 4 | 4 | 2 | 2 |  |  |  |  | 12 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 |  |  |  |  | 11-12 | 
 | 011100 | 4 | 4 | 3 | 2 |  |  |  |  | 13 | 
 | 011101 | 4 | 4 | 4 | 2 |  |  |  |  | 14 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 |  |  |  |  | 13-14 | 
 | 100000 | 4 | 4 | 3 | 3 |  |  |  |  | 14 | 
 | 100001 | 4 | 4 | 4 | 3 |  |  |  |  | 15 | 
 | 100010 | 4 | 4 | 4 | 4 |  |  |  |  | 16 | 

## Slide 18: Spatial configuration (2/3)
Nuser | B5…B0 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
5 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 |  |  |  | 5-8 | 49
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 |  |  |  | 7-9 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 |  |  |  | 9-10 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 |  |  |  | 11 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 |  |  |  | 8-10 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 |  |  |  | 10-11 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 |  |  |  | 12 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 |  |  |  | 11-12 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 |  |  |  | 13 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 |  |  |  | 14 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 |  |  |  | 9-11 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 |  |  |  | 11-12 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 |  |  |  | 13 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 |  |  |  | 12-13 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 |  |  |  | 14 | 
 | 011101 | 4 | 4 | 4 | 2 | 1 |  |  |  | 15 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 | 1 |  |  |  | 13-14 | 
 | 100000 | 4 | 4 | 3 | 3 | 1 |  |  |  | 15 | 
 | 100001 | 4 | 4 | 4 | 3 | 1 |  |  |  | 16 | 
 | 100010-100100 | 2-4 | 2 | 2 | 2 | 2 |  |  |  | 10-12 | 
 | 100101-100110 | 3-4 | 3 | 2 | 2 | 2 |  |  |  | 12-13 | 
 | 100111 | 4 | 4 | 2 | 2 | 2 |  |  |  | 14 | 
 | 101000-101001 | 3-4 | 3 | 3 | 2 | 2 |  |  |  | 13-14 | 
 | 101010 | 4 | 4 | 3 | 2 | 2 |  |  |  | 15 | 
 | 101011 | 4 | 4 | 4 | 2 | 2 |  |  |  | 16 | 
 | 101100-101101 | 3-4 | 3 | 3 | 3 | 2 |  |  |  | 14-15 | 
 | 101110 | 4 | 4 | 3 | 3 | 2 |  |  |  | 16 | 
 | 101111-110000 | 3-4 | 3 | 3 | 3 | 3 |  |  |  | 15-16 | 
6 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 |  |  | 6-9 | 54
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 |  |  | 8-10 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 |  |  | 10-11 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 |  |  | 12 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 |  |  | 9-11 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 |  |  | 11-12 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 |  |  | 13 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 |  |  | 12-13 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 |  |  | 14 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 | 1 |  |  | 15 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 | 1 |  |  | 10-12 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 | 1 |  |  | 12-13 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 | 1 |  |  | 14 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 | 1 |  |  | 13-14 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 | 1 |  |  | 15 | 
 | 011101 | 4 | 4 | 4 | 2 | 1 | 1 |  |  | 16 | 
 | 011110-011111 | 3-4 | 3 | 3 | 3 | 1 | 1 |  |  | 14-15 | 
 | 100000 | 4 | 4 | 3 | 3 | 1 | 1 |  |  | 16 | 
 | 100001-100011 | 2-4 | 2 | 2 | 2 | 2 | 1 |  |  | 11-13 | 
 | 100100-100101 | 3-4 | 3 | 2 | 2 | 2 | 1 |  |  | 13-14 | 
 | 100110 | 4 | 4 | 2 | 2 | 2 | 1 |  |  | 15 | 
 | 100111-101000 | 3-4 | 3 | 3 | 2 | 2 | 1 |  |  | 14-15 | 
 | 101001 | 4 | 4 | 3 | 2 | 2 | 1 |  |  | 16 | 
 | 101010 - 101011 | 3-4 | 3 | 3 | 3 | 2 | 1 |  |  | 15-16 | 
 | 101100 | 3 | 3 | 3 | 3 | 3 | 1 |  |  | 16 | 
 | 101101-101111 | 2-4 | 2 | 2 | 2 | 2 | 2 |  |  | 12-14 | 
 | 110000-110001 | 3-4 | 3 | 2 | 2 | 2 | 2 |  |  | 14-15 | 
 | 110010 | 4 | 4 | 2 | 2 | 2 | 2 |  |  | 16 | 
 | 110011-110100 | 3-4 | 3 | 3 | 2 | 2 | 2 |  |  | 15-16 | 
 | 110101 | 3 | 3 | 3 | 3 | 2 | 2 |  |  | 16 | 

## Slide 19: Spatial configuration (3/3)
Nuser | B5…B0 +B92 | Nsts[1] | Nsts[2] | Nsts[3] | Nsts[4] | Nsts[5] | Nsts[6] | Nsts[7] | Nsts[8] | Total Nsts | total entry
7 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 | 1 |  | 7-10 | 50
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 | 1 |  | 9-11 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 | 1 |  | 11-12 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 | 1 |  | 13 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 | 1 |  | 10-12 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 | 1 |  | 12-13 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 | 1 |  | 14 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 | 1 |  | 13-14 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 | 1 |  | 15 | 
 | 010011 | 4 | 4 | 4 | 1 | 1 | 1 | 1 |  | 16 | 
 | 010100-010110 | 2-4 | 2 | 2 | 2 | 1 | 1 | 1 |  | 11-13 | 
 | 010111-011000 | 3-4 | 3 | 2 | 2 | 1 | 1 | 1 |  | 13-14 | 
 | 011001 | 4 | 4 | 2 | 2 | 1 | 1 | 1 |  | 15 | 
 | 011010-011011 | 3-4 | 3 | 3 | 2 | 1 | 1 | 1 |  | 14-15 | 
 | 011100 | 4 | 4 | 3 | 2 | 1 | 1 | 1 |  | 16 | 
 | 011101-011110 | 3-4 | 3 | 3 | 3 | 1 | 1 | 1 |  | 15-16 | 
 | 011111-100001 | 2-4 | 2 | 2 | 2 | 2 | 1 | 1 |  | 12-14 | 
 | 100010-100011 | 3-4 | 3 | 2 | 2 | 2 | 1 | 1 |  | 14-15 | 
 | 100100 | 4 | 4 | 2 | 2 | 2 | 1 | 1 |  | 16 | 
 | 100101-100110 | 3-4 | 3 | 3 | 2 | 2 | 1 | 1 |  | 15-16 | 
 | 100111 | 3 | 3 | 3 | 3 | 2 | 1 | 1 |  | 16 | 
 | 101000-101010 | 2-4 | 2 | 2 | 2 | 2 | 2 | 1 |  | 13-15 | 
 | 101011-101100 | 3-4 | 3 | 2 | 2 | 2 | 2 | 1 |  | 15-16 | 
 | 101101 | 3 | 3 | 3 | 2 | 2 | 2 | 1 |  | 16 | 
 | 101110-101111 | 2-4 | 2 | 2 | 2 | 2 | 2 | 2 |  | 14-16 | 
 | 110000 | 3 | 3 | 2 | 2 | 2 | 2 | 2 |  | 16 | 
8 | 000000-000011 | 1-4 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 8-12 | 41
 | 000100-000110 | 2-4 | 2 | 1 | 1 | 1 | 1 | 1 | 1 | 10-12 | 
 | 000111-001000 | 3-4 | 3 | 1 | 1 | 1 | 1 | 1 | 1 | 12-13 | 
 | 001001 | 4 | 4 | 1 | 1 | 1 | 1 | 1 | 1 | 14 | 
 | 001010-001100 | 2-4 | 2 | 2 | 1 | 1 | 1 | 1 | 1 | 11-13 | 
 | 001101-001110 | 3-4 | 3 | 2 | 1 | 1 | 1 | 1 | 1 | 13-14 | 
 | 001111 | 4 | 4 | 2 | 1 | 1 | 1 | 1 | 1 | 15 | 
 | 010000-010001 | 3-4 | 3 | 3 | 1 | 1 | 1 | 1 | 1 | 13-14 | 
 | 010010 | 4 | 4 | 3 | 1 | 1 | 1 | 1 | 1 | 16 | 
 | 010011-010101 | 2-4 | 2 | 2 | 2 | 1 | 1 | 1 | 1 | 12-14 | 
 | 010110-010111 | 3-4 | 3 | 2 | 2 | 1 | 1 | 1 | 1 | 14-15 | 
 | 011000 | 4 | 4 | 2 | 2 | 1 | 1 | 1 | 1 | 16 | 
 | 011001-011010 | 3-4 | 3 | 3 | 2 | 1 | 1 | 1 | 1 | 15-16 | 
 | 011011 | 3 | 3 | 3 | 3 | 1 | 1 | 1 | 1 | 16 | 
 | 011100-011110 | 2-4 | 2 | 2 | 2 | 2 | 1 | 1 | 1 | 13-15 | 
 | 011111-100000 | 3-4 | 3 | 2 | 2 | 2 | 1 | 1 | 1 | 15-16 | 
 | 100001 | 3 | 3 | 3 | 2 | 2 | 1 | 1 | 1 | 16 | 
 | 100010-100100 | 2-4 | 2 | 2 | 2 | 2 | 2 | 1 | 1 | 14-16 | 
 | 100101 | 3 | 3 | 2 | 2 | 2 | 2 | 1 | 1 | 16 | 
 | 100110-100111 | 2-3 | 2 | 2 | 2 | 2 | 2 | 2 | 1 | 15-16 | 
 | 101000 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 16 |