## Slide 1: Hidden Node Protection in Coordinated AP Transmissions
Date: 2020-06-22
Authors:

## Slide 2: Abstract
802.11be shall define coordinated AP transmission mechanism, see section 9.4 in the SFD [1].
As coordinated AP transmission effectively increases the operational spatial domain, the likelihood of hidden nodes increases.
The increased hidden node problem emphasizes the need to adapt the TXOP protection mechanisms. This was discussed in [2].
This contribution focuses on the use of MU-RTS/CTS to protect against hidden nodes.

## Slide 3: Hidden Node Problem in Multi-AP
An example of the problem:
  AP1 is Sharing AP
  AP 2 is Shared AP
  AP3 is an independent BSS
  STA1 will not be protected without sending a CTS
  STA2 and AP3 are hidden to AP2 and AP1
STA1
STA2
AP1
AP2
AP3

## Slide 4: Option 1: Centralized
The sharing AP is in control of the MU-RTS/CTS procedure
Example: Change the MU-RTS such that the sharing AP can request CTS transmissions from STAs in neighboring BSSs
Pros:
Requires no extra overhead
Cons:
Does not provide as much coverage as the MU-RTS/CTS in each single BSS
Requires some global information (e.g. Global ID information)

## Slide 5: Option 2: Distributed
Each AP performs local MU-RTS/CTS frame exchanges within their BSS
Example: The sharing AP sends a trigger to the shared APs scheduling the local MU-RTS/CTS
Pros:
  Provides similar protection as single cell MU-RTS/CTS
  No changes needed to the MU-RTS/CTS frames
  Can be multiplexed with the AP coordination setup frames
Cons:
Requires some extra overhead compared centralized solution

## Slide 6: Straw Poll 1
Do you believe the increased hidden node problem in multi-AP environments (e.g. coordinated AP transmission) should be addressed by TGbe?
Yes/No/Abstain:

## Slide 7: Straw Poll 2
Do you prefer a centralized solution as in option 1 or a distributed as in
option 2 to address the problem in SP 1? (The exact nature of the solution is TBD)
Option 1/Option 2/Abstain:

## Slide 8: References
[1] https://mentor.ieee.org/802.11/dcn/19/11-19-1262-09-00be-specification-framework-for-tgbe.docx
[2] https://mentor.ieee.org/802.11/dcn/20/11-20-0643-00-00be-mu-rts-in-multi-ap-operation.pptx