## Slide 1: 6GHz LPI Range Extension
Date: 2020-06-30
Authors:
Name | Affiliations | Address | Phone | email
Ron Porat | Broadcom |  |  | ron.porat@broadcom.com

## Slide 2: Abstract
In the US, 1.2GHz is now approved for unlicensed use under low power indoor (LPI) rules.
This provides a huge boost (3x) to the spectrum available to 11be and 11ax devices although at a reduced power and PSD  5dBm/MHz for AP and -1dBm/MHz for STA.
Hence, we propose to define one lower rate SU mode to improve DL and UL range over the 11ax design

## Slide 3: Max LPI Power and 11ax Rates
Tx BW [MHz] | Max Power AP EIRP [dBm] | Lowest rate in 11ax [Mbps] 0.8uS GI with DCM
20 | 18 | 4.3
40 | 21 | 8.6
80 | 24 | 18
160 | 27 | 36
320 | 30 | -
Tx BW [MHz] | Max Power STA EIRP [dBm] | Lowest rate in 11ax [Mbps] 0.8uS GI with DCM
20 | 12 | 4.3
40 | 15 | 8.6
80 | 18 | 18
160 | 21 | 36
320 | 24 | -
It is desirable by AP and STA to use the maximum available BW in the BSS in order to maximize the transmission power
Dropping BW doesn’t provide better SNR  prefer to maintain BW while lowering rates

## Slide 4: Proposal
For SU80, SU160 and SU320 transmissions define a DUP mode of SU40, SU80 and SU160 limited to MCS0+DCM @Nss=1 to generate lower rates
  For SU20 and SU40 11ax rates are quite low already and we don’t see the need to define lower rates
  E.g., 160MHz rates –>
    160 MCS0 (72Mbps)
    160 MCS0+DCM (36Mbps)
    80MHz MCS0+DCM +DUP (18Mbps)
Beacons can already be sent in Non-HT DUP mode in 11ax @6GHz  80MHz-wide beacons provide range extension for STA that combine the four repetitions.

## Slide 5: Summary
Lower SU rate using DUP design is proposed for 11be for improved range of the new LPI spectrum.

## Slide 6: SP #1
Do you agree to define a DUP mode for SU80, SU160 and SU320 PPDUs limited to {MCS0, Nss=1}?