## Slide 1
Multi-link RTS-CTS operations with non-STR non-AP MLD
Date: 2020-07-03
Authors:

## Slide 2: Introduction
The multi-link operation includes the operation of non-STR multi-link operation[1]
Several presentations considered RTS-CTS operation of multi-link with non-STR non-AP MLD [2], [3]
This presentation continues to discuss the issue

## Slide 3: Recap: multi-link operation and channel access
Previous submissions proposed the PPDU alignment operation when multi-link operation is performed with non-STR non-AP MLD[2], [3]

## Slide 4: RTS-CTS transmission issue in non-STR operation
However, RTS-CTS operation may not be allowed in non-STR Multi-link operation

## Slide 5: RTS-CTS procedure for non-STR multi-link operation
Regarding the remaining transmission time in one link, the resolution may be different
  Opt. 1) When the remaining transmission time is less than a threshold, padding operation for RTS may be used

## Slide 6: Channel holding operation for simultaneous operation
When current remaining time of busy duration in one link is relatively small, the channel holding operation may be applied as well

## Slide 7: RTS-CTS procedure for non-STR multi-link operation
Regarding the remaining transmission time in one link, the resolution may be different
  Opt. 2) When the remaining transmission time is more than a threshold, no RTS-CTS may be applied for secondary link
    E.g. CTS-to-self for secondary link
  Opt. 3) Do not use RTS-CTS on Link2

## Slide 8: Conclusion
RTS-CTS for Non-STR MLD was discussed
In case of Non-STR MLD, when a channel access using RTS-CTS to a link is successful and a transmission is ongoing, modified RTS-CTS scheme shall be applied for the other link(s)
  Opt 1. Pre-padded RTS
  Opt 2. CTS-to-self based Transmission
  Opt 3. No RTS-CTS
Simplest solution is not using RTS-CTS but for a better protection CTS-to-self based transmission can be considered

## Slide 9: Reference
[1] 11-19/1262r6 Specification Framework for TGbe
[2] 11-19/1405 Multi-Link Operation Channel Access Discussion, Sharan Naribole (Samsung)
[3] 11-19/1546 Legacy Performance Impact on Multi-link Operation, Yongho Seok (MediaTek)
[4] 11-19/1916 MLO-Asynch-Qsynch-Synch, Matthew Fischer (Broadcom Inc)
[5] 11-19/1917 Considerations for multi-link channel access without simultaneous TX/RX capability, Insun Jang (LG Electronics)
[6] 11-19/1541 Performance aspects of Multi-link operations with constraints, Dmitry Akhmetov (Intel)