## Slide 1: Discussion on 11be PHY Capabilities
Date: 2020-07-05
Authors:
Name | Affiliations | Address | Phone | Email
Bin Tian | Qualcomm |  |  | btian@qti.qualcomm.com
Sameer Vermani |  |  |  | 
Steve Shellhammer |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
We want to discuss and collect feedback on several 11be PHY support capabilities
  MCS and encoding
  BW modes
  MIMO and sounding
Two main factors are considered
  PHY performance upgrade for each major amendment. Differentiation from 11ax
  Requirements from diverse use cases and different market segments for future 11be products

## Slide 3: MCS
Modulation
  Mandatory support
    Up to 64 QAM for 20 MHz only device
    Up to 256 QAM for all other devices
  Keep 1024 QAM and 4096 QAM optional
Encoding
  LDPC support: requirements are kept the same as in 11ax.
    Mandatory support if STA supports BW>20MHz or >4ss or >MCS9
  BCC support: already agreed in IEEE

## Slide 4: BW Mode
Prefer to have different requirements for AP and non-AP STA
AP: mandate to support 160 MHz in 6GHz band; 80MHz otherwise
  Encourage high throughput applications in 6 GHz band
Non-AP STA
  Mandatory support 80MHz except for 20MHz only client
  20 MHz only client
    Limited to 2.4GHz and 5GHz operation only in 11be
    Not allowed in 6GHz band
      In LPI channel with PSD limit, 20MHz only client may have link budget issue
      Encourage high throughput low latency applications in 6GHz band

## Slide 5: MIMO and Sounding Support
Beamformee STS capability: mandatory support up to Nss_total=4 EHT LTF in both sounding NDP and DL MU_MIMO in R1
  11ax also mandates Nss_total=4
DL MU-MIMO: the same as in 11ax
  Mandatory support for AP with >=4 antennas
  Mandatory support for client
UL MU-MIMO
  Mandatory support for AP with >=4 antennas
  Mandatory support for Client

## Slide 6: SP1
Do you agree that 11be device shall mandatorily support the following modulation order
  Up to 64 QAM for 20MHz only device
  Up to 256QAM for all other devices
Y/N/ABS

## Slide 7: SP2
SP2: Do you agree that the mandatory support requirement of LDPC in 11be is the same as in 11ax?
  Mandatory support if STA declares support for BW>20MHz or >4ss or >MCS9

## Slide 8: SP 3
Do you agree in 11be AP is mandatory to support
  160 MHz in 6GHz band
  80MHz otherwise
Y/N/ABS

## Slide 9: SP 4
Do you agree in 11be non-AP STA is mandatory to support 80MHz?
  Except for 20 MHz only client
Y/N/ABS

## Slide 10: SP 5
Do you agree that 11be defines 20MHz only client in 2.4/5GHz band only?
Y/N/ABS

## Slide 11: SP6
Do you agree with the following MU-MIMO support in 11be
  DL MU-MIMO
    Mandatory support for AP with >=4 antennas
    Mandatory support for client
    At least for full BW. RU/M-RU support TBD
  UL MU-MIMO
    Mandatory support for AP with >=4 antennas
    Mandatory support for client
    At least for full BW. RU/M-RU support TBD

## Slide 12: SP 7
Do you agree the support of Nss_total=4 EHT-LTFs is mandatory for 11be client in both sounding NDP and DL MU-MIMO, i..e Beamformee STS capability?
Y/N/ABS