## Slide 1: MLD Spatial Multiplexing Considerations
Date: 2020-07-15
Authors:

## Slide 2: Multi-link Spatial Multiplexing Background
Ideal Operation at non-AP MLD
  2x2 spatial streams capability on each link with dedicated receive chains
  In this case, independent SM Power Save mode can also be performed on each links
However, operating on two links or more, the receive chains may be shared between at least one pair of links
Receive chain sharing and switching between STAs of a non-AP MLD has been studied in a few TGbe contributions [1, 2, 3, 4]

## Slide 3: ML SM Default Operation Basic Example
In this example, non-AP MLD listens in 1x1 mode on each link and switches to 2x2 on one link upon receiving RTS on that link
Link A
Link B
AP A
STA A
AP B
STA B
DATA (2x2)
DATA (2x2)
BA
…
RTS
CTS
RTS
…
BA
CTS
Starts switching to 2x2
on Link B
Cannot perform
Listen/TX/RX on Link A
Switch back to 1x1
on Link A and B
Switching
Delay
Starts switching to 2x2
on Link A
Switch back to 1x1
on Link A and B
Switching
Delay
AP MLD needs to know that the 2 receive chains are being shared between STA 1 and STA 2 of non-AP MLD

## Slide 4: ML Spatial Multiplexing Capability Indication
For a subset of links, non-AP MLD indicates
  Maximum Spatial Streams on each link
  Flag to indicate if receive chain sharing among the links
    Alternatively, number of receive chains being shared
Preferred location is to include this information in the ML Element along with STR Capability signaling
Similar to dynamic STR Capability signaling [5] and OMI updates in 11ax, maximum spatial streams on a link can be updated after setup

## Slide 5: ML Spatial Multiplexing Capability Examples (1/2)
NA = 2, NB = 2, Shared = “1”
  In this case, non-AP MLD switches to 2x2 mode on the link TXOP is initiated by AP
NA = 2, NB = 1, Shared = “1”
  Non-AP MLD switches to 2x2 on Link A. On Link B, always uses 1x1 mode.
Link A
Link B
AP A
STA A
AP B
STA B
DATA (2x2)
DATA (2x2)
BA
…
RTS
CTS
RTS
…
BA
CTS
Link A
Link B
AP A
STA A
AP B
STA B
DATA (1x1)
DATA (2x2)
BA
RTS
CTS
RTS
…
BA
CTS
DATA (1x1)
BUSY
…
BA

## Slide 6: ML Spatial Multiplexing Capability Examples (2/2)
NA = 2, NB = 2, Shared = “0” or NA = 1, NB = 1, Shared = “0”
  In this case, no receive chain switching occurs between links.
  SM Power Save mechanisms can be applied on each link independently
NA = 2, NB = 2, NC =2 and Shared = “1”
  In this case, three links are sharing the receive chains
  When Link A switches to 2x2, both link B and link C are not accessible
Link A
Link B
RTS
CTS
AP A
STA A
AP B
STA B
DATA (2x2)
BA
Busy
DATA (2x2)
BA

## Slide 7: ML Spatial Multiplexing NAV Sync Issue
Identical to non-STR MLD losing NAV sync on other links during TX on one link
Link A
Link B
AP A
STA A
AP B
STA B
DATA (2x2)
BA
CTS
RTS
Starts switching to 2x2
on Link B
Cannot perform
Listen/TX/RX on Link A
Switch back to 1x1
on Link A and B
Switching
Delay
Switching
Delay
Proposal
  Use same rules that will be defined for non-STR MLD NAV Sync issue
NAV out of sync

## Slide 8: Non-Immediate Switching Operation Motivation
Default mode is Immediate Switching upon receiving RTS
Immediately switching to maximum streams on Link A may result in losing out on channel access on Link B (higher BW, better quality, etc.)
Therefore, in addition to default operation, AP MLD and non-AP MLDs may support additional switching operation as follows
Link A
Link B
RTS
CTS
AP A
STA A
AP B
STA B
DATA (1x1)
BA
Busy
DATA (1x1)
BA

## Slide 9: Non-Immediate Switching Operation Proposal
AP MLD sends RTS-type Trigger that includes information how to perform receive chain switching
  Countdown wait time/ PPDU limit before switch
    0 indicates immediate Switch (if only one PPDU in TXOP)
This operation can be limited to a specific link (e.g. smaller BW link)
  Non-AP MLD indicates which link it wants Non-Immediate Switching enabled
  By default, immediate switch enabled on all links
  Example: Link A on 5 GHz 80 MHz (non-immediate switching) and Link B on 6 GHz 320 MHz (default mode: immediate switching)

## Slide 10: MIMO Sounding in Multi-link Operation
Independent of receive chain sharing between links, in certain implementations, beamformee block may be shared among all STAs or subset of STAs of a non-AP MLD
Consequently, sounding procedure to generate Compressed Beamforming Report/CQI feedback can be performed only on one link at a time among those set of links
Sending no response may be detrimental to non-AP MLD’s performance
In case of receive chain sharing at non-AP MLD, AP MLD anyway can’t perform simultaneous sounding on multiple links that are sharing the receive chains. This same mechanism should be extended to above condition.
Option 1 (Preferred)
  AP shall not conduct overlapping sounding procedure for a non-AP MLD on multiple links
Option 2
  If AP MLD sends NDP-A and NDP to same non-AP MLD simultaneously on multiple links, a mechanism for non-AP MLD to request re-initiating sounding at least on one of the links. Accordingly, AP needs to re-perform sounding procedures on those links.

## Slide 11: Summary
MLD Spatial Multiplexing capability indication
  Maximum number of spatial streams on each link
  Receive chain sharing among links
Immediate switching to maximum spatial streams on a link should be default operation
Additional non-immediate switching operation may be used on specific links
Avoid simultaneous sounding of a non-AP MLD on multiple links

## Slide 12: Straw Poll #1
Do you agree to have following text added to TGbe SFD R1?
  A non-AP MLD shall indicate sharing of receive chain(s) among a set of setup links if the dynamic receive chain switching among these links may lead to non-AP MLD unable to listen temporarily on one or more links of this set.

## Slide 13: Straw Poll #2
Do you agree to have following text added to TGbe SFD R1?
  AP MLD shall not initiate sounding sequence with a non-AP MLD on a link if this sounding sequence would potentially overlap in time domain with an ongoing sounding sequence on another link with the same non-AP MLD.

## Slide 14: Straw Poll #3
Do you agree to have following mechanism defined in TGbe SFD R1?
  Non-AP MLD requests AP MLD to re-initiate sounding on a link. Consequently, AP initiates sounding for the non-AP MLD on this link.

## Slide 15: References
[1] 11-20/562, Enhanced Multi-link Single Radio Operation
[2] 11-20/659, TDM Multi-link Operation
[3] 11-20/883, Multi-link Spatial Multiplexing Considerations
[4] 11-20/900, NSTR MLD Operation
[5] 11-20/226, MLO Constraint Indication and Operating Mode