## Slide 1: DCM for range extension in 6GHz LPI
Date: 2020-05-28
Authors:
Name | Affiliations | Address | Phone | Email
Jianhan Liu | Mediatek | 2840 Junction Ave. San Jose, CA, 95134 |  | jianhan.liu@mediatek.com
Shengquan Hu |  |  |  | 
Thomas Pare |  |  |  | 
Dennis Liu |  |  |  | 

## Slide 2: Introduction: FCC Rules on 2.4GHz and 5GHz Band
Power Spectral Density |  |  |  |  |  |  | 
Country / Geo | 2.4 GHz | 5.15 - 5.25 GHz | 5.25 - 5.35 GHz | 5.47 - 5.65 GHz | 5.65 - 5.725 GHz | 5.725 - 5.85 GHz | Unit
Conductor | 33.2 | 11 (17 AP) | 11 | 11 | 11 | 33 | dBm / MHz
EIRP | 39.2 | 17 (24 AP) | 17 | 17 | 17 | 39 | dBm / MHz
Tx Power Limit |  |  |  |  |  |  | 
Conductor |  | 24 | 24 | 24 | 24 | 30 | dBm
EIRP |  | 30 | 30 | 30 | 30 | 36 | dBm

## Slide 3: Introduction: FCC Rules on 6GHz
PSD requirement in 6GHz low power indoor (LPI) is far more stringent than PSD requirement in 2.4GHz and 5GHz:
  EIRP 5dBm/MHz for APs in 6GHz LPI v.s EIRP 17dBm/MHz for APs in 5GHz
  EIRP -1dBm/MHz for non-AP STAs n 6GHz LPI v.s EIRP 11dBm/MHz for non-AP STAs in 5GHz

## Slide 4: The range issue in 6GHz LPI
6GHz LPI has much short range compared to 5GHz band
  For 20MHz transmission from AP: 5+13=18dBm in 6GHz LPI v.s. 17+13=30dBm in 5GHz, this is 12 dB difference, the range is just a quarter of 5GHz and the cover area of 6GHz LPI is about 1/16 of 5GHz.
  A new wide BW LPI long range (LR) PPDU is designed to solve the length issue.
To extend range for transmissions in 6GHz LPI bands, we propose to adopt DCM+MCS0 defined in 11ax into 11be.

## Slide 5
SU: 20MHz-Duplicate Preamble and wideband EHT-STF, EHT-LTF and LPI LR Payload
Duplicate 20MHz legacy preamble, U-SIG, EHT-SIG.
  Note EHT-SIG for LPI LR PPDU has 1111 structure in each 80MHz.
DCM or DCM+DUP are applied to the payload
EHT-STF and EHT-LTF can use large BW EHT-STF and EHT-LTF, for example, 80MHz LPI LR PPDU used 80MHz EHT-STF and EHT-LTF.
EHT Payload uses large BW with low rate full-BW transmission schemes.
Receiver need to do 80MHz packet detection (for example, 64 samples cross correlations instead 16 samples on L-STF) and channel estimation on L-LTFs.
  Maximum ratio combining (MRC) over four 20MHz sub-channels on L-SIG, RL-SIG, U-SIG, EHT-SIG.
For 80MHz, 6dB extra range can be obtained compared to 20MHz PPDU.

## Slide 6: Straw Poll #1
Do you agree that DCM+MCS0 for Nss=1 as defined in 11ax is a MCS in 11be?
  The detailed MCS # for DCM+MCS0 is TBD.
  This is a R1 feature.