## Slide 1: MLO mandatory/optional
Date: 2020-07-14
Authors:

## Slide 2: General MLO
It is clear that multi-link operation is a very important feature for 802.11be, which allows to improve performance:
  on many domains: low latency (worst case latency), throughput, QoS, reliability, …
  and for a very diverse range of devices: single radio, enhanced single radio, non-STR multi radio, STR multi radio
We believe that an EHT STA shall be part of an MLD, especially if it’s capable of operating on more than two bands/links
We also need to define what are the basic MLO framework (set of features) that needs to be supported by an EHT STA (AP and non-AP)

## Slide 3: Basic MLO framework
By current agreements in SFD, we think the following is already mandatory for an MLD
We propose that the following features constitute the mandatory basic MLO framework
  discovery procedure
  Setup procedures
  Security procedures
  default mapping (all TIDs mapped to all links, all setup links enabled)
  TIM indicating BUs at MLD level
  BA at MLD level
  Power save per link
  Power state change indications per link
  TSF alignment rules on AP MLD side TBD
Whether we allow in EHT single radio single band STA and AP TBD

## Slide 4: Straw poll #1
Do you agree to add the following to the SFD:
  An EHT STA that is capable of operating in at least 2 bands (or 2 channels within one band) shall be part of an MLD

## Slide 5: Straw poll #1 bis
Do you agree to add the following to the SFD:
  If an EHT AP is in the same co-located set as other EHT AP with the same SSID, all these APs shall be part of the same AP MLD

## Slide 6: Straw poll #2
Do you agree to add the following to the SFD
  the MLO basic framework support is mandatory for 11be AP and 11be STA
    discovery procedure, Setup procedures, Security procedures, default mapping (all TIDs mapped to all links, all setup links enabled), TIM indicating BUs at MLD level, BA at MLD level, Power save per link, Power state change indications per link
    Note: TSF alignment rules on AP MLD side TBD
    Note: Single radio single band capable STA and AP TBD
    Note: TID-mapping and other link operations (enable/disable/add/remove) are TBD

## Slide 7: Non-AP MLD
Capabilities for non-AP MLD:
  We have a capability bit for “single radio/multi radio”
  For multi radio, we have a capability bit for STR/NSTR
  For single radio, we’ll have something like a capability bit for regular single radio/enhanced single radio
If all capability bits set to 0, the non-AP MLD is a single radio/link non-AP MLD
Which means that a non-AP MLD shall be at least a single radio non-AP MLD, and may be single radio, enhanced single radio, non-STR multi-radio, STR multi-radio MLD

## Slide 8: Straw poll #3
Do you agree to add the following to the SFD
  A non-AP MLD shall be one of the following
    a single radio non-AP MLD
      it can be an enhanced single radio/link non-AP MLD or a regular single radio/link non-AP MLD
    a multi-radio non-AP MLD
      Per pair of links, it can be STR or non-STR

## Slide 9: AP MLD
There is a proposal to allow a AP MLD to be non-STR, but limited to a class of AP MLD (soft AP MLD)
There is therefore consensus that a regular AP MLD (that corresponds to an AP MLD that is not a soft-AP MLD) shall be STR capable.

## Slide 10: Straw poll #4
Do you agree to add the following to the SFD
  A regular AP MLD (that corresponds to an AP MLD that is not a soft-AP MLD, if defined) shall be an STR AP MLD

## Slide 11: AP MLD support for operation with single radio/link non-AP MLD
By just supporting the Basic mandatory MLO framework, an AP MLD has all the needed features to allow operation with a single radio/link non-AP MLD.
This is the most simple and basic mode for MLO.
It is therefore mandatory for an AP MLD to support operation with single radio/link non-AP MLD

## Slide 12: AP MLD support for operation with enhanced single radio/link non-AP MLD
We believe operation with an enhanced single radio/link non-AP MLD should be optional

## Slide 13: AP MLD support for operation with multi radio non-AP MLD
For asynch operation with a non-AP MLD, an AP needs the following:
  1) Be able to transmit concurrent PPDUs simultaneously on different links – Tx/Tx
  2) Be able to receive a PPDU on one each EHT AP link independently to the transmit/reception status on the other affiliated EHT APs links
  3) Be able to operate with asynch channel access
We believe that 2) and 3) should be mandatory for an AP MLD with at least 2 affiliated APs, as there are no additional complexity compared to what is needed and mandatory to support operation with a single radio non-AP MLD
For 1), there is more complexity involved on AP MLD side (scheduling, …)
  We therefore propose to loosen slightly the requirement on AP MLD side:
  Support for 1) is mandatory on at least 2 EHT APs for an AP MLD with 2 or more EHT APs

## Slide 14: Straw poll #5
Do you agree to add the following to the SFD
  An AP MLD shall support operation with single radio/link non-AP MLD
  Note: nothing additional needed compared to mandatory basic MLO framework

## Slide 15: Straw poll #6
Do you agree to add the following to the SFD
  the support by an AP MLD of operation for enhanced single radio/link non-AP MLD is optional

## Slide 16: Straw poll #7
Do you agree to add the following to the SFD:
  An STR AP MLD with 2 or more affiliated EHT APs
    shall be capable to receive a PPDU on one each EHT AP link independently to the transmit/reception status on the other affiliated EHT APs links
    shall be capable to transmit concurrent PPDUs simultaneously to the same non-AP MLD by at least two affiliated EHT APs on at least one pair of links among all the affiliated EHT APs possible pairs of links
    shall support asynch channel access across all the affiliated EHT APs links

## Slide 17: Multi-radio non-AP MLD
We believe that if a non-AP MLD is multi-radio and STR capable on a pair of links, then it shall support channel aggregation.

## Slide 18: Straw poll #8
Do you agree to add the following to the SFD:
  A multi-radio non-AP MLD that is operating on a pair of links on which it is STR capable shall be capable of operating with channel aggregation on that pair of links?