## Slide 1: Blindness issue for non-STR operations-followup
Date: 2020-07-03
Authors:
Name | Affiliations | Address | Phone | Email
Dibakar Das | Intel |  |  | Dibakar.das@intel.com
Dmitry Akhmetov |  |  |  | 
Laurent Cariou |  |  |  | 
Po-kai Huang |  |  |  | 
Duncan Ho | Qualcomm |  |  | dho@qti.qualcomm.com
George Cherian | Qualcomm |  |  | gcherian@qti.qualcomm.com
Yongho Seok | Mediatek |  |  | Yongho.Seok@mediatek.com

## Slide 2: Abstract
Follow up on the blindness issue during Tx of ML

## Slide 3: Introduction
We have agreed to allow non-STR operation in SFD:
  “802.11be shall allow a MLD that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links
    Signaling of these constraints is TBD.”
When non-STR STA is txing in link-1 it may miss frames transmitted on link 2.
As a result, when the transmission is over, the STA may falsely detect medium in link 2 to be idle (e.g., if the RSSI is between -82 and -62 dBm) and transmit during an ongoing activity on the other link => hidden node problem due to non-STR operation.
Link 1
AP MLD
AP 1
AP 2
Non-AP MLD 1
STA 1
STA 2
Link 2 (from STA-2 perspective)
time
: STA-2 not blind
: STA-2 blind
RTS (TA: STA1, RA: AP1)
CTS (RA: STA1)
DATA (TA: STA1, RA: AP1)
BA (RA: STA1)
Non-AP MLD 2
STA 3
RTS (TA: STA3)
CTS (RA: STA3)
DATA (TA: STA3, RA: AP2)
RTS (TA: STA2)
Collision at AP 2
Link 2 (from STA-3 perspective)

## Slide 4: Background (NAVsyncdelay)
For other STAs on the same channel, the impact of non-STR STA coming out of blindness and performing channel access is similar to the case of STA coming out of Doze to awake and doing the same.
Currently, the spec proposes to use the NAVSyncDelay timer to solve this problem for Doze-to-Awake transitions.
  The timer value is set by non-AP STA.
  The usage is defined in REVmd as: “A (11ah)non-S1G STA that is changing from doze to awake state in order to transmit shall perform CCA until a frame is detected by which it can set its NAV, or until a period of time indicated by the NAVSyncDelay from the MLME-JOIN.request primitive has transpired.”
Typically the NAVSyncDelay value is set by STA to be zero. This does not cause significant problems because the STA does not go from Doze to Awake frequently.
For non-STR operation we expect higher frequency of such transitions.

## Slide 5: Recap of solutions proposed
In 490r0 we analyzed the problem and proposed a solution to address it mainly from the associated BSS perspective.
  After blindness is over, STA refrains from transmitting for some timer value (similar to NAVSyncDelay) except for 1 RTS frame.
Concurrently in 444r1, two options were presented to address the problem from overall network perspective.
  Option 1: Similar to NAVSyncDelay, start a fixed timer during which countdown is prohibited. It expires after decoding preamble and/or NAV.
  Option 2: Lower ED level after transmission to -82 dBm.
Example of option 1 solution in 444r1.

## Slide 6: Revised solution
The solution in 490r0 prioritizes non-STR STA MLD performance while that in 444r1 is more protective of the network performance.
To balance the two requirements we propose a joint solution:
  Every non-STR STA start a timer, following the end of a transmission on the other link except in some cases where it is assumed to have the medium state information (see next slide).
    The value of this timer can be specified in spec or configured by AP.
  While the timer is running, STA can do EDCA using baseline CCA but a TBD ED threshold value (e.g., between -62 and -82dBm) whose value can be configured by AP; otherwise set to some default value (e.g., -62dBm). For example, managed APs configure ED threshold to a non-default value, stand-alone APs use default value.
  The first frame after EDCA countdown is an RTS frame; the max number of RTSs that STA can transmit while timer is running is configured by AP (at least 1)
    Improves STA UL throughput/latency.
  The timer expires early if at least either of the following events happens:
    any received PPDU with a valid MPDU (including response CTS to any txmitted RTS)
    a received PPDU with a valid TxOP_duration

## Slide 7: Revised solution (contd.)
Medium state information is assumed to be “known” if STA-2 just transmitted PPDUs with end-time alignment on both links.
Medium state information can also be assumed to be known if the NAV counter is non-zero at the end of transmission.
Link 1
AP MLD
AP 1
AP 2
Non-STR Non-AP MLD 1
STA 1
STA 2
Link 2
time
DATA (TA: AP1, RA: STA1)
DATA (TA: AP2, RA: STA2)
BA (RA: AP1)
BA (RA: AP2)
SIFS
SIFS
STA-1 and 2 resume regular EDCA
Link 1
AP MLD
AP 1
AP 2
Non-STR Non-AP MLD 1
STA 1
STA 2
Link 2
time
DATA (RA: AP1, TA: STA1)
BA (RA: STA1)
SIFS
STA-2 does not start timer at end of STA-1 tx
RTS (TA: STA3)
CTS (RA: STA3)
NAV duration
set from CTS
Notes: Simultaneous tx/tx case includes the collision case (e.g., when an UL RTS collide) as that case is similar to collision in single link.

## Slide 8: Example of proposed solution
Link 1
AP 1
AP 2
Non-AP MLD 1
STA 1
STA 2
Link 2
time
RTS (TA: STA1, RA: AP1)
CTS (RA: STA1)
DATA (TA: STA1, RA: AP1)
BA (RA: STA1)
: STA-2 not blind
: STA-2 blind
Initial timer duration
EDCA at TBD ED threshold
RTS (TA: STA2, RA: AP2)
CTS (RA: STA2)
Timer
expires

## Slide 9: Revised Solution (contd.)
The proposed solution only addresses the typical cases but does not attempt to resolve every possible blindness issue especially some that are naturally present in single link operation.
For example, if the STA missed any frame (e.g., new frame) during blindness that updates existing NAV information then it may still operate based on old NAV value. This is equivalent to STA missing frames due to collision that updates NAV.

## Slide 10: Summary
Proposed a simple solution to resolve non-STR MLO blindness for typical cases that attempt to find a balance from STA perspective and BSS perspective.

## Slide 11: SP
Do you support that if during a transmission of a STA (STA-1) of a non-STR non-AP MLD, another STA (STA-2) of the same MLD cannot detect its medium state when required (due to STA-1’s UL transmission interference), STA-2 shall start a MediumSyncDelay timer at the end of the transmission, unless the STA-2 ended a transmission at the same time:
  the MediumSyncDelay timer expires after a duration value that is either assigned by AP or specified in spec or if at least either of the following events happens:
    any received PPDU with a valid MPDU
    a received PPDU with a valid TxOP_duration
    whichever happens first
  while the MediumSyncDelay timer is running the STA is only allowed to attempt to initiate up to number of TxOPs assigned by the AP (at least 1) and shall attempt to initiate that TxOP with the transmission of an RTS frame using regular EDCA backoff using baseline CCA but a TBD ED threshold value
Note:
  The TBD ED threshold value has a default value specified in the spec (e.g., -62dBm) but can also be assigned by the AP MLD within a limited range such as between -82dBm and -62dBm

## Slide 12: References
11-20-044r1-MLA: Non-STR STA Behaviors
11-20-490r0-Impact of channel blindness during ML

## Slide 13: SP changes relative to r2
Do you support that if during a transmission of a STA (STA-1) of a non-STR non-AP MLD, another STA (STA-2) of the same MLD cannot detect its medium state when required (due to STA-1’s UL transmission interference), STA-2 shall start a MediumSyncDelay timer at the end of the transmission, unless the STA-2 has a non-zero NAV value or the STA-2 ended a transmission at the same time:
  the MediumSyncDelay timer expires after a duration value that is either assigned by AP or specified in spec or if at least either of the following events happens:
    any received PPDU with a valid MPDU
    a received PPDU with a valid TxOP_duration
    whichever happens first
  while the MediumSyncDelay timer is running the STA is only allowed to attempt to initiate up to number of TxOPs assigned by the AP (at least 1) and shall attempt to initiate that TxOP with the transmission of an RTS frame using regular EDCA backoff using baseline CCA but a TBD ED threshold value
  If the channel was busy immediately after the blind period, additional TBD rules to use RTS may apply.
Note:
  The TBD ED threshold value has a default value specified in the spec (e.g., -62dBm) but can also be assigned by the AP MLD within a limited range such as between -82dBm and -62dBm
  If either the intra-BSS NAV or the inter-BSS NAV is non-zero in STA-2 at the end of transmission of STA-1, there could be further TBD conditions and requirements to expire the MediumSyncDelay timer.