## Slide 1: On 802.11bd Mandatory Features: Input from the Car-2-Car Communications Consortium
Date: 2020-06-07
Authors:

## Slide 2: Background: The European CAR 2 CAR Communication Consortium is an industrial-driven, non-commercial association founded by European vehicle manufacturers https://www.car-2-car.org/

## Slide 3
Partners
GM
Honda
Hyundai
KTM
MAN
Groupe Renault
Toyota
Volkswagen
Volvo
Yamaha
32 associate members
Aptiv
Autotalks
Bosch
Cohda Wireless
Continental
Denso
Infineon
NXP
LG
u-blox
Siemens
Valeo
…
29 development members
DLR
Eurecom
Fraunhofer
IMST
KTH
TNO
…
Background, Car-2-Car members:

## Slide 4: Discussion – Interoperability with Wi-Fi
The current NPRM proposal by the FCC allocates the lower 45 MHz of the 5.9 GHz band for Wi-Fi operation (802.11a/n/ac/ax/be)
Operation of 802.11bd (either 10 MHz or 20 MHz) will not be an attractive solution for the 45 MHz as non-interoperable with Wi-Fi
A single 10 MHz channel for 802.11p/bd in the upper 30 MHz of the 5.9GHz band will not fulfill the needs of ITS
It is unlikely that automotive OEMs will deploy 802.11p/bd based systems if only 10 MHz of bandwidth is accessible to ITS
Could 802.11a/ac/ax be used or do we need a new 802.11bd 20 MHz mode?

## Slide 5: Discussion – 256 QAM modulation
This mode can be important for enabling high throughput, matching the specification of competitive solutions
The scope of 256-QAM however is limited to a few applications and not for a broad deployment (similarly to 2x2 MIMO)
Implementation and verification of this feature adds cost and complexity
802.11p only defines MCS 0, 2 and 4 as mandatory, yet there were no limitations due to this (vast majority of applications exclusively use QPSK)
NR-V2X (Rel. 16) also defines 256-QAM as an optional mode

## Slide 6: Proposal
Based on this discussion, the authors are making the following proposals. These were discussed during the C2C Week #10 meeting and were approved by the C2C Steering Committee
The definition of an additional 20 MHz mode which will be interoperable with Wi-Fi (802.11a/n/ac/ax/be)
The classification of 256-QAM modulation as an optional feature for 802.11bd

## Slide 7: Straw poll 1
Do you support the definition of an additional 20 MHz mode which will be interoperable with Wi-Fi (802.11a/n/ac/ax/be)?
Y / N / A

## Slide 8: Straw poll 2
Do you support the classification of 256-QAM modulation as an optional feature for 802.11bd?
Y / N / A