## Slide 1: Protected TWT Enhancement for Latency Sensitive Traffic
Date: 2020-07-29
Name | Affiliations | Address | Phone | email
Chunyu Hu | Facebook Inc. | 1 Hacker way Menlo Park, CA |  | chunyuhu@fb.com
Payam Torab |  |  |  | torab@ieee.org
George Cherian | Qualcomm Inc. | 5665 Morehouse Dr, San Diego CA 92131 |  | gcherian@qti.qualcomm.com
Duncan Ho |  |  |  | dho@qti.qualcomm.com
Laurent Cariou | Intel Corp. | 2111 NE 25th Ave, Hillsboro, OR 97124 |  | laurent.cariou@intel.com
Dave Cavalcanti |  |  |  | dave.cavalcanti@intel.com
Zhou Lan | Broadcom Inc. | 250 Innovation Dr., San Jose, CA 95034 |  | zhou.lan@broadcom.com
George Kondylis |  |  |  | george.kondylis@broadcom.com
Yongho Seok | MediaTek Inc. | 2840 Junction Ave, San Jose, CA 95134 |  | yongho.seok@mediatek.com
Boyce Bo Yang | Huawei Technologies, Co. LTD | Nanjing, China |  | yangbo59@Huawei.com
Ming Gan |  | Shenzhen, China |  | ming.gan@huawei.com
Oren Kedem |  | Israel |  | oren.kedem@huawei.com

## Slide 2: Abstract
Discuss a solution in R1 timeline based on TWT to provide latency sensitive traffic more predictable latency performance

## Slide 3: Background
11-20/1045 proposed a general channel access that provides a more predictable latency performance to latency sensitive traffic
  Can work with TWT/U-APSD for power saving gain
This contribution discusses an approach in R1 timeline based on TWT
  Intending to leveraging existing support to meet timeline
  Trade off with some flexibility
Time Slot structure
pEDCA
TWT
+
U-APSD e.g.
+
11-20/1045
Proposing in R1:
Restricted TWT
Channel access protection
Signaling (advertising, req/resp etc.)

## Slide 4: TWT Revisit
TWT is a mechanism where a set of Service Periods (SPs) are defined and shared between AP and non-AP STAs to reduce medium contention and improve the power efficiency of STAs.
TWT provides a periodic operation (implicit TWT) suiting periodic traffic
Broadcast TWT: AP can schedule TWT SP(s) with supporting STAs and shares schedule info in Beacon/Probe Response frames
  Reduced negotiation overhead compared to individual TWT, but further reduction of signaling overhead can be considered
  Information is shared on per TWT flow basis
Individual TWT: defined a protection mode using a NAV protection mechanism to protect medium access of TWT SP
  The session info is not shared in the beacon
TWT is associated with a STA but not associated with a traffic class (TID or AC)
TWT is defined for AP/STA pairs or TDLS peers
Notes: Individual TWT can be set up between STAs / TDLS case
Bcast TWT has to be between AP/STAs per 11ax
26.8.2 Individual TWT agreements
— May set the TWT Protection field to 1 to indicate that TXOPs within the TWT SPs shall be initiated
with a NAV protection mechanism, such as (MU) RTS/CTS, or CTS-to-self frame; otherwise it shall
set it to 0.
— An HE STA shall not use the RAW mechanism for protection of TWT SPs.

## Slide 5: Re-Cap: Latency Sensitive Traffic Characteristics
A latency sensitive traffic stream can be characterized by the following parameterized model:
  Bursty, periodic
  Traffic amount varies driven by application (e.g. compression) in addition to wireless medium dynamics
An application may contain multiple such streams of different parameters
Tethered link is a common design to balance computation power, network bandwidth and latency
  Require support of peer-to-peer communication
XR System Paradigms
Example:

## Slide 6: Proposal Highlight
Enhance channel access protection for TWT SP
Extend the concept of protected individual TWT to Broadcast TWT
Extend the usage of Broadcast TWT signaling for protected SPs
Extend the usage of TWT for low latency peer-to-peer communication
Define support of limiting a protected TWT flow to TID(s)

## Slide 7: Restricted TWT
Existing Protected TWT: TXOPs within TWT SPs shall be initiated with a NAV protection mechanism, such as (MU) RTS/CTS, or CTS-to-self frame. Under this rule:
  SP start time may vary if previous transmission didn’t finish
     resulting in unpredictability in delay and increased jitter
Propose additional rule: TXOP shall stop before a protected TWT SP starts
  Provide a more predictable latency performance: reduce jitter
  Reduce wake-up time: additional power saving
   Restricted TWT: term used in this presentation
Example:
Notes: cts-2-self
Trigger
Let other STA(s) to tx on themselves. We can avoid that.
P2p: softAP / GO they send trigger.

## Slide 8: TWT Protection Field
802.11ax D7.0 has defined:
  Individual TWT:
  Broadcast TWT
Propose: change bit-15 of the Request Type field to be <Restricted TWT>, to indicate Restricted TWT

## Slide 9: Support of Peer-to-Peer Communication
Existing TWT sessions only allows AP/STA and TDLS pairs to participate
Some examples of peer-to-peer links:
  TDLS: either non-AP STA can request TWT membership for their latency sensitive traffic, and follow corresponding channel access rules
  Tethered link using P2P (GO/GC): GO as non-AP STA associated with the AP, and request TWT membership for the latency sensitive traffic carried over the p2p link
  Tethered link using SoftAP: similar to above
Propose: extend restricted TWT for peer-to-peer STAs to participate

## Slide 10: What Else is Needed?
A STA needs to learn the restricted broadcast TWT sessions
  => The AP shall include sufficient info of these TWT sessions in the Beacon/Probe Response
A STA provides its own traffic information and minimum QoS requirement for the TWT setup
  => This allows the AP to perform resource allocation and admission control (accept/reject/suggest the request) and update its scheduling
To avoid abuse by the STAs, the AP can announce policies, which
  Limits the type of traffic that it can accept for the restricted TWT sessions, and/or
  Limits the amount of time allocated to each and total restricted TWT sessions.

## Slide 11: Summary
Introduced restricted TWT SPs with the following mechanisms where we:
  Enhance the channel access for restricted TWT SPs
  Extend the use of Broadcast TWT signaling
  Extend the usage of such TWT SPs for low latency peer-to-peer communications
  Introduce support of limiting a restricted TWT flow to TIDs
Discussed possible ways for AP to constrain the use of protected channel access

## Slide 12: SP #1 (NOT USED)
Do you agree to add to the TGbe SFD (in R1), a mode where an EHT AP may announce restricted service periods (SPs) such that:
  Any EHT non-AP STA that supports following the announced restricted SPs, and associated to the AP, shall end its TXOP before the start of the restricted SP(s)
  The support for the restricted SPs is optional for the EHT non-AP STA
  The support for this mode is optional for the EHT AP
  Note: such restricted SPs are intended to provide more predictable latency performance for latency sensitive traffic

## Slide 13: SP #2 (NOT USED)
Do you agree to add to the TGbe SFD (in R1),
  EHT non-AP STAs that are members of a restricted SP as described in SP#1 are allowed to ignore the quiet intervals (which are advertised in Quiet elements by the AP) if they overlap with the restricted SP.
  An EHT AP may announce quiet intervals with Quiet Elements that overlap with restricted SPs and allow above exception.
Notes: Q/A: any non-EHT STA (legacy STAs) still follows the baseline rule of Quiet elements. This is how SP2 is expected to help mitigate the legacy STA problem.

## Slide 14: Usage of Quiet Element
Quiet elements can be used to suppress the transmissions from legacy STAs, as an effective mechanism when applicable, at AP’s jurisdiction [10-20/1355]
  STAs supporting Quiet element will not transmit during the quiet intervals
  This can protect the restricted SPs reserved for restricted SPs participants
  Note: the channel access/protection for restricted SP is in general context is yet to be discussed and agreed in further development. But considering usage of Quiet elements can mitigate legacy STA issue.
Restricted SP
Quiet interval
STA1 and STA2 are participants of restricted SPs.
STA1 and STA2 can still transmit within restricted SPs per rules within, with SP2.

## Slide 15: SP #1A
Do you agree to add to the TGbe SFD (in R1), a mode where an EHT AP may announce restricted service periods (SPs) such that:
  Any EHT non-AP STA that supports following the announced restricted SPs, and associated to the AP, shall end its TXOP before the start of the restricted SP(s)
  EHT non-AP STAs that are members of restricted SPs are allowed to ignore the quiet intervals (which are advertised in Quiet elements by the AP) if they overlap with the restricted SP.
  An EHT AP may announce quiet intervals with Quiet Elements that overlap with restricted SPs and allow above exception.
  The support for the restricted SPs is optional for the EHT non-AP STA
  The support for this mode is optional for the EHT AP
  Note: such restricted SPs are intended to provide more predictable latency performance for latency sensitive traffic
Notes: Comment: AP shall not allocate Quiet intervals that overlaps with the restricted SPs if the quiet intervals are used for DFS scanning.

## Slide 16: SP #1A’ (Revised as in Motion 148)
Do you agree to add to the TGbe SFD (in R1), a mode where an EHT AP may announce restricted service periods (SPs) such that:
  Any EHT non-AP STA that supports following the announced restricted SPs, and associated to the AP, shall end its TXOP before the start of the restricted SP(s)
  EHT non-AP STAs are allowed to ignore the quiet intervals (which are advertised in Quiet elements by the AP) if they overlap with the restricted SP.
  An EHT AP may announce quiet intervals with Quiet Elements that overlap with restricted SPs and the above exception applies. The rules on transmitting Quiet Element for restricted SPs are TBD.
  The support for the restricted SPs is optional for the EHT non-AP STA
  The support for this mode is optional for the EHT AP
  Note: such restricted SPs are intended to provide more predictable latency performance for latency sensitive traffic
Notes: Comment: AP shall not allocate Quiet intervals that overlaps with the restricted SPs if the quiet intervals are used for DFS scanning.

## Slide 17: SP #2
Do you agree to add to the TGbe SFD (in R1)
  a mode where EHT STAs use TWT setup procedure as baseline to set up an restricted SP agreement, known as restricted TWT?
  The name “restricted TWT” is TBD.

## Slide 18: SP #3
Do you agree to add to the TGbe SFD (in R1):
  Restricted TWT schedule may be announced by the AP for peer-to-peer communication.
Notes: A: For low latency.
01/07/2021 vote: 32 Y / 36 N / 39 Abs / 31 NoAnswer, out of 138

## Slide 19: SP #4
Do you agree that the TGbe SFD shall add (in R1):
  Extend the per STA TWT setup procedure to allow limiting the usage of a restricted TWT session to indicated TID(s)

## Slide 20: SP #5
Do you agree to add to the TGbe SFD (in R1):
  Define a signaling mechanism for an AP to announce a QoS management policy for admitting a STA into a restricted TWT session
Notes: SP #1, 2 , 8 and 9

## Slide 21: SP #6
Do you agree to add to the TGbe SFD (in R1) the following:
  Define a signaling mechanism for a STA to convey its traffic information and QoS requirements (e.g., latency delay tolerance, throughput needs, periodicity, offset, etc.) when or before requesting a restricted TWT session
Notes: TBD / minimum

## Slide 22: SP #7
Do you agree that the TGbe SFD shall include (in R1) the support of restricted TWT in Broadcast TWT as described below:
  Change the Reserved bit in Figure 9-688a as in 802.11ax D7.0 to Restricted TWT
    Field name TBD