## Slide 1: Traffic indication of latency sensitive applications
Date: 2020-09-01
Authors:

## Slide 2: Motivations
For UL latency sensitive traffic, such as gaming control and industrial automation, some applications require periodic traffic transmission [1, 2]
  Traffic properties: bursty fixed amount of data in average
  Requirements: small jitter and lossless
Since 11ax, AP triggered UL transmission plays a more important role for UL traffic
  Current BSRP/BSR provides a protocol for AP to acquire buffer status of each ACs on the non-AP side, so that AP can send trigger frames to trigger UL traffic
  For latency sensitive and periodic UL traffic, waiting for BSRP is not sufficient to satisfy jitter requirement and latency is not guaranteed
  If characteristics of the period traffic are known to AP, AP can allocate proper resources in advance and can trigger UL transmission in time

## Slide 3: Ideas
STA can provide its periodic latency sensitive traffic indication to AP
  Instead of using TSPEC or other negotiation protocols, STA just provides informative indication
  Requires a simple, proactive and more dynamic way on the non-AP side
  Best effort on the AP side to provide quality of service
Options
  A-control subfield
  A new management frame to carry such information

## Slide 4: Methods to Carry Periodic Traffic Indication (PTI)
A-control
  Limited size to carry traffic information
  Flexible to be carried in the header
  May reuse of BSR capability to be solicited
  Many features compete to use A-control
New Management frame
  Contents are under security protection
  Easy to extend

## Slide 5: Thoughts of Periodic Traffic Indication Contents
Limited access categories (AC) for latency sensitive traffic
  VO and VI
  Only VO
Only important parameters to carry
  Active/inactive flag
  Traffic time period
  Delta time from the frame transmission time to the next instant the periodic traffic is coming
  Access categories of the periodic traffic
  Periodic traffic size in octet

## Slide 6: A-control Design Example of PTI
Periodic traffic indication
  Type: activate/deactivate the traffic corresponding to periodic traffic ID
  Periodic Traffic ID: 4 maximum in parallel
  AC: traffic corresponding AC (maybe limited to VI and VO)
  Period: period of the traffic in ms
  Delta period: delta time from the frame carrying the A-control to the next instant the period traffic is coming in ms
  Traffic size in octet
  Period scaling factor
  Traffic size scaling factor
26 bits are very enough to carry important information
Field | Type | Periodic Traffic ID | AC | Period (ms) | Delta period (ms) | Traffic size (octet) | Period scaling factor | Traffic size scaling factor
bits | 1 | 2 | 1 | 6 | 6 | 6 | 2 | 2

## Slide 7: Summary
Propose to design a method so that STA can provide UL periodic traffic indication (PTI) to AP
  A control subfield or a new management frame
The indication has to be simple and dynamic

## Slide 8: Straw Poll 1
Do you support to define a new mechanism so that a non-AP STA can provide AP TBD parameters to optimize AP’s scheduling for low latency applications in R1?
  NOTE: How to signal is TBD

## Slide 9: Straw Poll 2
Which option do you support to enable a non-AP STA to provide TBD parameters of low latency periodic applications to AP in R1?
  Option 1: A-control subfield
  Option 2: Management frame
  Option 3: None of the above
  Option 4: Abstain

## Slide 10: References
20-0418 QoS Management framework in 802.11be
19-0065 RTA TIG summary and recommendations

## Slide 11: backup

## Slide 12: Straw Poll 1 in R5
Do you support in R1 to reuse or define a mechanism so that a non-AP STA can provide AP TBD parameters to optimize AP’s scheduling for low latency applications?
  NOTE: How to signal is TBD