## Slide 1: IEEE 802.11-IETF Liaison Report
Date: 2020-07-15
Authors:

## Slide 2: Abstract
This presentation contains the IEEE 802.11 – IETF liaison report for July 2020.

## Slide 3: IETF Meetings
Upcoming Meetings:
  July 25-31, 2020 – Virtual (was Madrid)
  November 14-20, 2020 – Bangkok (Virtual?)
http://www.ietf.org
  Newcomer training: https://www.ietf.org/edu/process-oriented-tutorials.html#newcomers
  April 2016: Wireless Tutorial (Donald Eastlake), 802.11 & 802.15 tutorials (Dorothy Stanley, Charlie Perkins), see 11-16/500, July 2016: Pat Thaler & Juan Carlos – 802.1E (Privacy Considerations) and 802.c (Local MAC address usage) https://www.ietf.org/edu/tutorials.html
  http://tools.ietf.org/dailydose/

## Slide 4: IETF- IEEE 802 Liaison Activity
Joint meetings, agenda and presentations
  http://www.iab.org/activities/joint-activities/iab-ieee-coordination/
  Coordination topics include: Data Center Bridging, use of Local Address in virtualization and IoT, MAC randomization trial results, DETNET/TSN, YANG models, pervasive monitoring
  IETF-IEEE 802 coordination teleconferences: February 25, 2020 and June 15, 2020
802.11 related items
  Tracked: Intelligent Transportation Systems (ITS)- IETF IP Wireless Access in Vehicular Environments ipwave
  Approved by WG: Link-Layer Addresses Assignment Mechanism for DHCPv6: https://datatracker.ietf.org/doc/draft-ietf-dhc-mac-assign/. This specification provides a means of using DHCPv6 to assign MAC addresses to (virtual) devices at time of instantiation to prevent random address collisions in large device populations.

## Slide 5: IETF protocol use with 802.11 technology
No recent RFCs mention IEEE 802.11

## Slide 6: BOFs at IETF 108 July 25-31, 2020
See https://datatracker.ietf.org/wg/bofs/
BOF proposals were due June 12, 2020
loops | Local Optimizations on Path Segments
asdf | A Semantic Definition Format for Data and Interactions of Things
emailcore | Revision of core Email specifications
Notes: ila – splitting IPv6 node identity from location for improved mobility. Done efficiently without tunneling.
mls – generalized capability for message confidentiality, authentication, and integrity. Also membership verification, asynchronous key distribution, forward secrecy, post-compromise secrecy, and scalability.
Not clear that coms, ila, and mls will meet at IETF 102.

## Slide 7: IETF new groups being (re-)chartered
See https://datatracker.ietf.org/group/chartering/
asap | Automatic SIP trunking And Peering (external review)
nfsv4 | Network File System Version 4 (internal recharter review)

## Slide 8: YANG Model Catalog
YANG catalog development
  A YANG model catalog and registry that allows users to find models relevant to their use cases from the large and growing number of YANG modules being published.
  YANG Catalog was developed through a collaboration between the IETF and the Broadband Forum, and contains many data models, including from other Standards Development Organizations (SDOs) such as the IEEE, as well as some vendor-specific data models. Interest and participation from other SDOs, equipment vendors, open source projects and network operators is encouraged.
See https://www.ietf.org/blog/yang-catalog-latest-developments-ietf-100-hackathon/
See https://yangcatalog.org/ and https://1.ieee802.org/yangsters/

## Slide 9: IoT related work
6LO
  Working Group website: http://datatracker.ietf.org/wg/6lo/charter/
  Focus: IPv6 over Networks of Resource-constrained Nodes
  Updated: IPv6 over Constrained Node Networks Applicability & Use cases, see: https://datatracker.ietf.org/doc/draft-ietf-6lo-use-cases/ (Updated July 2020)
  RFC Editor Queue: Address Protected Neighbor Discovery for Low-power and Lossy Networks, see: https://datatracker.ietf.org/doc/draft-ietf-6lo-ap-nd/ (Updated: April 2020)
  RFC Editor Queue: IPv6 Backbone Router, see: https://datatracker.ietf.org/doc/draft-ietf-6lo-backbone-router/. No feedback received from IEEE 802.11, so publication requested. (Updated: March 2020)

## Slide 10: IoT related work (cont.)
6TiSCH: IPv6 over IEEE 802.15.4 Time-slotted Channel Hopping
  Working group slowly winding down with only one semi-active document in the WG, but may be re-chartered to cover other underlying layer 2 protocols. This could have a bearing on IEEE 802.11be activities.
ROLL: Working Group website: http://datatracker.ietf.org/wg/roll/
  Focus: Routing over Low Power and Lossy Networks
CORE: (Constrained RESTful Environments) Working Group website: http://datatracker.ietf.org/wg/core/
  Focus: framework for resource-oriented applications intended to run on constrained IP networks.
IoT Directorate:
  Reviews IETF drafts that are IoT related
  See: https://datatracker.ietf.org/group/iotdir/about/

## Slide 11: CAPPORT WG
CAPtive PORTal: https://datatracker.ietf.org/wg/capport/
The CAPPORT Working Group will define secure mechanisms and protocols to
  allow endpoints to discover that they are in this sort of limited environment,
  provide a URL to interact with the Captive Portal, - allow endpoints to learn about the parameters of their confinement,
  interact with the Captive Portal to obtain information such as status and remaining access time, and
  optionally, advertise a service whereby devices can enable or disable access to the Internet without human interaction. (RFC 7710 may be a full or partial solution to the first two bullets)
Updates [July 2020]
  Updated: RFC 7710bis, the CAPPORT architecture, and the CAPPORT API all updated within the last two months; see https://datatracker.ietf.org/wg/capport/documents/
  Experiment: Apple is shipping experimental support for CAPPORT in iOS 14 beta.

## Slide 12: EMU WG
See http://datatracker.ietf.org/wg/emu/
EAP Method Updates
  This working group has been chartered to provide updates to some commonly used Extensible Authentication Protocol methods including of EAP-TLS, EAP-AKA, EAP-AKA’ (for 5G), EAP-SIM, etc.
  The group should document any recently gained new knowledge on vulnerabilities or the possible implications of pervasive surveillance or other new concerns.
Updates
  Perfect-Forward Secrecy for the Extensible Authentication Protocol Method for Authentication and Key Agreement (EAP-AKA' PFS): https://datatracker.ietf.org/doc/draft-ietf-emu-aka-pfs/ (May 2020)
  EAP Session-Id Derivation: https://datatracker.ietf.org/doc/draft-ietf-emu-eap-session-id/ (May 2020)
  Using EAP-TLS with TLS 1.3: draft-ietf-emu-eap-tls13-06 (June 2020)
  New draft: Use Identity as Raw Public Key in EAP-TLS: https://datatracker.ietf.org/doc/draft-chen-emu-eap-tls-ibs/ (May 2020)
  New draft: EAP-TLS with PSK Authentication (EAP-TLS-PSK): https://datatracker.ietf.org/doc/draft-mattsson-emu-eap-tls-psk/ (March 2020)

## Slide 13: Operations Area Working Group
http://datatracker.ietf.org/wg/opsawg/
Updates [July 2020] Operations Area Working Group work group items
  Of interest: RFC 6632, An Overview of the IETF Network Management Protocols, see https://tools.ietf.org/html/rfc6632
  Automated network management, including YANG data models, see https://www.ietf.org/topics/netmgmt/
  Secure Device Install: https://datatracker.ietf.org/doc/draft-ietf-opsawg-sdi/ (June 2020)
  Newly adopted: A Layer 2 VPN Network YANG Model: https://datatracker.ietf.org/doc/draft-ietf-opsawg-l2nm/ (July 2020)
  Framework for Automating Service and Network Management with YANG: https://datatracker.ietf.org/doc/draft-ietf-opsawg-model-automation-framework/ (June 2020)
  Network Telemetry Framework: https://datatracker.ietf.org/doc/draft-ietf-opsawg-ntf/ (April 2020)

## Slide 14: Transport Layer Security (TLS)
Transport Layer Security Working Group website: http://datatracker.ietf.org/wg/tls/
Updates
  A Flags Extension for TLS 1.3: https://datatracker.ietf.org/doc/draft-ietf-tls-tlsflags/ (July 2020)
  Deprecating MD5 and SHA-1 signature hashes in TLS 1.2: https://datatracker.ietf.org/doc/draft-ietf-tls-md5-sha1-deprecate/ (IESG evaluation since May 2020)
  Deprecating TLSv1.0 and TLSv1.1: https://datatracker.ietf.org/doc/draft-ietf-tls-oldversions-deprecate/ (Still in AD evaluation for more than 6 months)
  TLS 1.3 Extension for Certificate-Based Authentication with an External Pre-Shared Key: Published as RFC 8773 (March 2020)

## Slide 15: Deterministic Networking (DETNET)
DETNET: https://datatracker.ietf.org/wg/detnet/charter/
  The Deterministic Networking (DetNet) Working Group focuses on deterministic data paths that operate over Layer 2 bridged and Layer 3 routed segments, where such paths can provide bounds on latency, loss, and packet delay variation (jitter), and high reliability.
  The IEEE 802.11be activities seem like they may fit in with DetNet and there was a joint IEEE-IETF DetNet discussion in Bangkok.
  Addresses Layer 3 aspects in support of applications requiring deterministic networking.
  The Working Group collaborates with IEEE 802.1 Time Sensitive Networking (TSN), which is responsible for Layer 2 operations, to define a common architecture for both Layer 2 and Layer 3.
  Example applications for deterministic networks include professional and home audio/video, multimedia in transportation, engine control systems, and other general industrial and vehicular applications being considered by the IEEE 802.1 TSN Task Group.
Of interest:
  DetNet Bounded Latency: https://datatracker.ietf.org/doc/draft-ietf-detnet-bounded-latency/ (Expired May 2020)
  Deterministic Networking (DetNet) Security Considerations: https://datatracker.ietf.org/doc/draft-ietf-detnet-security/ (Updated May 2020)
  DetNet Data Plane: IP over IEEE 802.1 Time Sensitive Networking (TSN): https://datatracker.ietf.org/doc/draft-ietf-detnet-ip-over-tsn/ (Updated June 2020)

## Slide 16: Reliable and Available Wireless (RAW)
RAW: https://datatracker.ietf.org/wg/raw/charter/
  Reliable and Available Wireless (RAW) provides for high reliability and availability for IP connectivity over a wireless medium. RAW extends the DetNet Working Group concepts to provide for high reliability and availability for an IP network utilizing scheduled wireless segments and other media, e.g., frequency/time-sharing physical media resources with stochastic traffic: …, IEEE 802.11ax/be…
  Of interest:
  RAW use cases: https://datatracker.ietf.org/doc/draft-bernardos-raw-use-cases/ (Updated July 2020)
  Reliable and Available Wireless Architecture/Framework: https://datatracker.ietf.org/doc/draft-pthubert-raw-architecture/ (Updated July 2020)
  Reliable and Available Wireless Technologies: https://datatracker.ietf.org/doc/draft-thubert-raw-technologies/ (Updated May 2020)

## Slide 17: IP Wireless Access in Vehicular Environments (IPWAVE)
IPWAVE: https://datatracker.ietf.org/group/ipwave/about/
Deliverable is: document that specifies the mechanisms for transmission of IPv6 datagrams over IEEE 802.11-OCB mode
For further information:
  Use cases and problem statement document: https://datatracker.ietf.org/doc/draft-ietf-ipwave-vehicular-networking/ (July 2020)
  Published as RFC 8691: Transmission of IPv6 Packets over IEEE 802.11 Networks operating in mode Outside the Context of a Basic Service Set (IPv6-over-80211-OCB): https://www.rfc-editor.org/info/rfc8691

## Slide 18: Autonomic Networking Integrated Model and Approach (ANIMA)
ANIMA: https://datatracker.ietf.org/group/anima/about/
ANIMA designs protocols to allow network operations to be carried out without requiring low-level management of individual devices
For further information:
  An Autonomic Control Plane (ACP): https://datatracker.ietf.org/doc/draft-ietf-anima-autonomic-control-plane/ (IESG telechat August 2020)
  Updated (April 2020): BRSKI is Bootstrapping Remote Secure Key Infrastructures: https://datatracker.ietf.org/doc/draft-ietf-anima-bootstrapping-keyinfra/ [RFC Editor’s Queue]
  Scenarios and Requirements for Layer 2 Autonomic Control Planes: https://datatracker.ietf.org/doc/draft-carpenter-anima-l2acp-scenarios/ (April 2020)

## Slide 19: References
RFC 7241, “The IEEE 802/IETF Relationship” (RFC 4441 update)
  https://datatracker.ietf.org/doc/rfc7241/
IEEE 802 Liaisons list is available
  http://ieee-sa.centraldesktop.com/802liaisondb/FrontPage