## Slide 1: Remaining Issues with New 11be Scrambler
Date: 2020-07-21
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Youhan Kim |  |  |  | 
Bin Tian |  |  |  | 
Notes: September 2012

## Slide 2: Background
11be introduces new 11-bit scrambler to reduce payload PAPR. The passed SP says
To place the 11 bits scrambling seed we may need to re-define the bits in SERVICE field for EHT PPDU. A natural way to do it is using the 1st 11 LSB bits for 11be scrambling seed and keeping the remaining 5 bits still reserved
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
s0
s1
s2
s3
s4
s5
s6
legacy 7-bit scrambling seed
Reserved
s7
s8
s9
s10
SERVICE field in EHT PPDU
11be 11-bit scrambling seed

## Slide 3: Scrambler Seed for CTS in Response to MU-RTS (1)
Multiple STAs send identical CTS in response to MU-RTS using non-HT DUP PPDU
  Modulated bits in CTS need to be same from all STAs, including scrambling sequence
In 11ax, STA copies the 1st 7 bits of SERVICE field in MU-RTS as its scrambling seed for CTS and fill them into the 1st 7 bits of SERVICE field in CTS
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
s0
s1
s2
s3
s4
s5
s6
SERVICE field of MU-RTS prior to descrambling
Reserved
X4 X3 X2 X1
X7 X6 X5
Data In
Scrambled Data Out
s6 s5 s4 s3 s2 s1 s0
During first 7 bits of SERVICE
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
s0
s1
s2
s3
s4
s5
s6
Reserved
MU-RTS RX
CTS TX
SERVICE field of CTS after scrambling. First 7 bits are identical to MU-RTS.

## Slide 4: Scrambler Seed for CTS in Response to MU-RTS (2)
If MU-RTS is transmitted using EHT PPDU, MU-RTS has 11 bits of scrambling ‘initial value’
  Can still use the first 7 bits of the SERVICE field in MU-RTS only to scramble the CTS data and fill in the first 7 bits of the SERVICE field of the CTS
  Need to make sure those 7 bits can’t be all 0 to guarantee scrambling
    Option 1: disallow 1st 7 bits to be all zero for MU-RTS
    Option 2: the receiving STAs use a default value for CTS scrambling seed, if the received scrambling seed in MU-RTS has 1st 7 bits being all zeros.
      For example, default value = 127 = all ones = “1111111”
  We recommend option 1 for its simplicity and robustness
    Option 2 needs all receiver to handle special condition
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
s0
s1
s2
s3
s4
s5
s6
SERVICE field of MU-RTS prior to descrambling
Reserved
X4 X3 X2 X1
X7 X6 X5
Data In
Scrambled Data Out
s6 s5 s4 s3 s2 s1 s0
During first 7 bits of SERVICE
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
s0
s1
s2
s3
s4
s5
s6
Reserved
MU-RTS RX
CTS TX
SERVICE field of CTS after scrambling. First 7 bits are identical to MU-RTS.
s7
s8
s9
s10
s7-s10 not used for CTS scrambling initialization

## Slide 5: SP 1
Do you support using the first 11 LSB bits in SERVICE field for 11be scrambling seed and keeping the remaining 5 bits as reserved?
Y/N/ABS
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
s0
s1
s2
s3
s4
s5
s6
legacy 7-bit scrambling seed
Reserved
s7
s8
s9
s10
SERVICE field in EHT PPDU
11be 11-bit scrambling seed

## Slide 6: SP 2
Do you support using the first 7 LSB bits of the SERVICE field in MU-RTS to scramble the CTS data and fill in the first 7 LSB bits of the SERVICE field of the CTS, when MU-RTS is transmitted using an EHT PPDU?
Y/N/ABS

## Slide 7: SP 3
Do you support in 11be to disallow the 7 LSB bits of the SERVICE field in MU-RTS to be all zeros?
Y/N/ABS