## Slide 1: 802.11be Architecture/Association Discussion
Date: 2020-08-24
Authors:

## Slide 2: Abstract
802.11 TGbe has been discussing MLDs for several months, but there has been little discussion of how MLD will fit in the 802 architecture. Top down design concepts may help progress the MLD work. This contribution discusses an MLD architecture that is well aligned with the current 802.11 basic architecture and will hopefully allow many existing 802.11 features to be reused to support MLD operation.
R3 – updated and refocused based on TGbe decisions and ARC SC discussions.

## Slide 3: Basic 802.11 Architecture/Association for Infrastructure (review)
Both the AP and non-AP STA are logical entities
802.11 defines a link as “link: In the context of an IEEE 802.11 medium access control (MAC) entity, a physical path consisting of exactly one traversal of the wireless medium (WM) that is usable to transfer MAC service data units (MSDUs) between two stations (STAs).” [1]
802.11 based devices provide a service to higher layer entities enabling the exchange of information (MPDUs) via the 802.11 MAC SAP
Association defines a SAP to SAP connection (a data link) between an AP MAC SAP to a non-AP MAC SAP to enable the transfer of MSDUs.
Reassociation redefines a SAP to SAP connection to either the same or a different AP MAC SAP, while maintaining some association status (e.g. security/IP address).
Disassociation is a means of tearing down a SAP to SAP connection.
802.11be should use/align with these existing functions/definitions as much as possible.

## Slide 4: 802.11be MLD Architecture Discussion
The introduction of the MLD concept will define an MLD MAC SAP [2]
An MLD MAC SAP of an AP MLD will connect to higher layers via the DS (for non-GLK APs) serving the same purpose as the current MAC SAP
The MLD MAC SAP of an non-AP MLD STA will connect to higher layers via the LLC sublayer, also serving the same purpose as the current MAC SAP.
The MLD MAC (lower and upper) will manage all aspects of MSDU/MPDU flow between the MAC SAP and the PHY SAP(s)
The MLD PHY(s) will manage all aspects of MPDU/PPDU flow between the PHY SAP(s) and the wireless media
This architecture is an extension of the current 802.11 architecture for STAs (AP and non-AP STA)

## Slide 5: 802 Reference Model – Review [3]
802.11
802.11 MAC service access point
802.11 PHY service access point
An 802 data link is from one LSAP to its peer LSAP
Likewise an 802.11 data link is from one 802.11 MAC SAP to its peer MAC SAP
OSI Reference Model

## Slide 6: IEEE Std 802.1AX – Link Aggregation [4]
802.1 has completed 802.1AX, published 30 Jan 2020.
The 802.1AX aggregates: “One or more parallel instances of point-to-point links to be aggregated together to form a Link Aggregation Group (LAG) so that a Link Aggregation Client can treat the LAG as if it were a single link.” This is done at the LLC layer.
Therefore MLO should not simply aggregate 802.11 non-AP and AP STAs at the MAC SAP layer.
802.11 MAC service access point

## Slide 7: Current Basic 802.11 Data Plane Architecture (non-GLK)

## Slide 8: Proposed MLD 802.11be Data Plane Architecture

## Slide 9: From 11-20/1639r1: “MLD-level” or “per-AP/link-level”
Implications:
MLD:
  802.1X controlled/uncontrolled filtering
  RX/TX MSDU rate limiting
  A-MSDU aggregation/deaggregation
  (  bufferable MMPDUs need to inject into the stack here, so Action frames’ functions??)
  PS Defer Queuing
   Management frames: Authentication/Association/Reassociation Request/Response
  Sequence Number assignment
  Packet Number assignment/Replay detection
  Block Ack Buffering and Reordering
  MPDU Encryption/Decryption
  Duplicate Detection
Per-link:
  Control frames (RTS/CTS, Acks, NDP, etc.)
  Management frames: Beacon generation, Probe Request/Response,

## Slide 10: From 11-20/1639r1:
So, something like:

## Slide 11: MLD Capability Goals
An MLD shall efficiently use/manage multiple PHY links:
  Data at the MLD MAC SAP can be efficiently moved to an associated MLD MAC SAP via multiple PHY links. Providing the 802.11 service to the LLC layer from a single MAC SAP.
  The point to point link established by Association is a data link between two MAC SAPs.
  Allowing the 802.11 MAC to manage the flow of frames via multiple PHY links will:
    Improve latency (via multi-channel access)
    Improve throughput (via PHY link aggregation and multi-channel access)
    Avoid the inefficacy of above the MAC SAP aggregation (dependance on higher layer management).
An MLD shall receive “Legacy” beacons and group addressed frames
  “Legacy” beacons are received on the PHY link they are transmitted on, the receiving non-AP MLD STA will know that the beacon information is for the associated MLD PHY link
  “Legacy” group addressed frames can be received and “processed” by the non-AP MLD STA, as any group addressed frame is processed, the MLD will know which group addressed frames it should receive, just as a STA is informed as to the group addressed frames it should receive.

## Slide 12: Current Concerns w/ MLD terms and concepts
The use of AP in MLO:
  An 802.11 AP is an 802.11 STA connected via a DSAF to a DS – an AP has a MAC SAP and a wireless media interface.
  Currently an AP MLD is defined as: “A MLD, where each STA affiliated with the MLD is an AP”, each AP has a MAC SAP and the MLD has “… one MAC SAP to LLC”
  This definition is not consistent with itself.
The use of non-AP STA in MLO:
  An 802.11 non-AP STA is a STA – with a MAC SAP and a wireless media interface.
  Currently a non-AP MLD is defined as: “A MLD, where each STA affiliated with the MLD is a non-AP STA”.
  This definition also not consistent with itself, as each STA has a MAC SAP.
Using these definitions for an AP MLD and a non-AP MLD STA create new 802.11 entities – hence their behavior needs to be defined throughout the specification.

## Slide 13: Proposed Way Forward
Define an AP MLD as an AP this will:
Allow an AP MLD to support all existing AP behavior/features with minimal specification changes.
Where AP MLD requirements must be or are desired to be different than current AP behavior, e.g. PS or “multiple PHY link” management, new requirements/behavior can be specified.
Define a non-AP MLD STA as a non-AP STA this will:
Allow a non-AP MLD STA to support all existing non-AP STA behavior/features with minimal specification changes.
Where non-AP MLD STA requirements must be or are desired to be different than current non-AP STA behavior new requirements/behavior can be specified

## Slide 14: Straw Polls
SP1: The definition of a MLD AP should be changed in the draft spec and the SFD to clearly state that an MLD AP is an AP. (Having a single MAC SAP.)
Yes/No/abs
SP2: The definition of a non-AP MLD STA should be changed in the draft spec and the SFD to clearly state that a non-AP MLD STA is a STA. (Having a single MAC SAP.)
Yes/No/abs

## Slide 15: Other Concerns w/ MLD terms and concepts
The use of the term “link”:
  In 802.11 and 802 the term “link” is used to describe a SAP to SAP (MSAP or LSAP, respectively) connection, a “data/networking link.
  In MLO the term link is being used to describe an “RF link”, a PHY to PHY connection via the wireless media. This use is consistent with “link budgets” and other RF uses of “link”.
  I suggest changing from multi-link to multi-PHY or multi-PHY-link.
The use of the term “device”:
  “device” is defined in [5] as: mechanism or piece of equipment designed to serve a purpose or perform a function – this is in line with the way 802.11 uses the term
  In 802.11 the term “device” is a physical entity not a logical entity like an AP or STA
  I suggest not using the term “device” to describe the MLO logical entities (e.g. AP/STA)

## Slide 16: Straw Polls (cont.)
SP3: Rename “multi-link” to:
“multi-PHY” (MPHY) yielding MPHYO, MPHY AP, non-AP MPHY STA
“multi-PHY-link” (MPL) yielding MPLO, MPL AP, non-AP MPL STA
Do not change the name: “multi-link” keeping MLO, MLD, MLD AP, non-AP MLD STA.
(note MP is already used in 802.11: MP: mesh protocol)
1, 2, or 3
SP4: Agree that the term “device” should not be used to describe a logical entity.
Yes/No/abs

## Slide 17: Beyond Point to Point Data Plane Services
While point to point data plane services are essential to 802.11 there are other services/functions and how MLO uses/receives “legacy” transmissions is critical.
  Beacons – are essential for infrastructure deployments, multiple-beacons and beacon bloat are critical issues. MLO information must be available in “legacy” beacons. An MLD should receive “legacy” beacons.
  Group addressed MSDUs – There should be no restriction on an MLD receiving “legacy” transmissions, MLDs can receive PPDUs with multiple addresses.
  Security – the P2P data link for MLD must be secure, hence the data link should be secured by pairwise security and this security should not be weakened by reuse.

## Slide 18: Conclusion
The proposed MLD architecture and suggestions:
Is a natural extension to the current 802.11 architecture
Allows the current association, reassociation, and disassociation services to be used to manage MLD connections
Allows for reuse of other defined 802.11 services/capabilities without changes throughout the entire 802.11 specification
While these issues and other 802.11be architecture issues will continue to be discussed in the ARC SC, it is TGbe’s responsibility define and agree the 802.11be architecture and terminology.
Hopefully, this contribution will help focus the TGbe discussions and assist TGbe in reaching a consensus on how to progress MLO.

## Slide 19: References
[1] Draft P802.11REVmd D5.0
[2] 11-200566r78 Compendium of straw polls and potential changes to the Specification Framework Document
[3] IEEE Std 802-2014 “IEEE Standard for Local and Metropolitan Area Networks: Overview and Architecture”
[4] IEEE Std 802.1AX-2020 “IEEE Standard for Local and Metropolitan Area Networks — Link Aggregation”
[5] ISO/IEC/IEEE 24765 second edition 2017-09 “Systems and software engineering – Vocabulary”

## Slide 20: Back-up slides

## Slide 21: Proposed MLD 802.11be Data Plane Architecture

## Slide 22: FST Architecture – For Reference

## Slide 23: Possible AP MLD/ Non-AP MLD Associations
Assuming the architecture shown on the “Proposed MLD 802.11be Architecture” slide with an AP MLD that can support 3 links and a non-AP MLD that can support 3 links:
The non-AP MLD can associate with:
  The AP MLD with 3 links
  The AP MLD with 2 links (there are 3 possible 2 link configurations)
  The AP MLD with 1 link (3 possible) – this is “standard” current 802.11 association
Therefore each of configuration needs an identifier (e.g. a MAC address)
  The identifier will be associated with a specific configuration, the configuration will provide the number and parameters of the links.
  The non-AP MLD will associate using the identifier to a specific configuration
  Hence the non-AP MLD only need to use association, reassociation, and disassociation services to manage its link configuration with the AP MLD.