## Slide 1: S1G EU New Band
Date: 2020-08-04
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
David Goodall | Morse Micro | In quarantine, on a desert island |  | dave@morsemicro.com

## Slide 2: Abstract
CID 4036
The EU has recently added a band suitable for use by S1G devices
1 MHz channels only
These newly available channels should be included in the global channels listing in Annex E
  Table E-4—Global operating classes
  That table references Table E-5 S1G operating classes
    So this table also needs to be updated

## Slide 3: CID 4036
CID 4036
CID | Commenter | Page | Clause | Comment | Proposed Change | Proposed Resolution
4036 | David Goodall | 4382.00 | E | The 915.8 MHz to 919.4 MHz band has become available for use by S1G devices in Europe. | Add an operating class for the new band available in Europe to table E-5. This will support 1 MHz channels only. It will also need a global operating class added to table E-4. | Revise – TGmd editor to make changes shown in 11-20-1182r1 which add operating classes to the Annex E Global operating classes table and the Annex E S1G operating classes table to include the new band and channels

## Slide 4: New Channels
The following channels are recently available in the EU, but are not included in the Global operating classes table in Annex E, nor in the S1G operating classes table in Annex E
1 MHz channels within the range:
  915.8 – 919.4 MHz
    i.e. 3 or 4 channels, depending on where you start

## Slide 5: Existing European Spectrum 863-868 MHz
EU 802.11ah devices are covered by the following:
  DECISION (EU) 2017/1483 (See References [2])
  This document contains the Annex: Harmonised frequency bands and technical parameters for short-range devices with the legal requirements for the SRDs in the European Union.
Band no | Frequency band | Category of short-range devices | Transmit power limit/field strength limit/power density limit | Additional parameters (channelling and/or channel access and occupation rules) | Other usage restrictions | Implementation deadline
84 | 863-868 MHz | Wideband data transmission devices [16] | 25 mW e.r.p. | Techniques to access spectrum and mitigate interference that provide at least equivalent performance to the techniques described in harmonised standards adopted under Directive 2014/53/EU must be used. Bandwidth: ≤ 1 MHz. Duty cycle [vi]: ≤ 10 % for network access points [26] Duty cycle [vi]: ≤ 2,8 % otherwise | This set of usage conditions is only available for wideband SRDs in data networks [26]. | 1 January 2018

## Slide 6: New spectrum 917.4-919.4 MHz
EU 917.4 – 919.4 MHz covered by:
  DECISION (EU) 2018/1538 (See References [3])
  See band 2 for wideband data transmission devices
    Same conditions as for 863-868MHz

## Slide 7: CID 4036 Updates
CID 4036 should be revised for a couple of reasons
  There is not yet a decision document for 915.8-917.4 MHz
    So only two new channels in 917.4 – 919.4 MHz can be added at this time
      This is counter to the request within CID 4036, which anticipated 3 or 4 available channels
    AND
      The current 2MHz channels in 863-868 MHz are no longer allowed by the latest applicable decision document for that band and therefore, should be removed
    Propose to remove S1G operating class 7 in Table E-5
      Attempt to reuse S1G operating class 7 for the new band might cause backwards compatibility problems

## Slide 8: Example Of S1G Operating Classes (1)
Table E-4—Global operating classes
Note that Channel Set is not provided directly (in contrast to non-S1G cases)
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
71 | E-5-4, E-5-25, E-5-29 | 0.902 | 8 | - | Reserved | -
72 | E-5-5 | 0.902 | 16 | - | Reserved | -
73 | E-5-8 | 0.9165 | 1 | - | Reserved | -
74 | E-5-14 | 0.9175 | 1 | - | Reserved | -
An existing example of S1G classes:
S1G Table references

## Slide 9: Determining S1G Channel Numbers
23.3.14 Channelization
  Extracted text:
  Channel center frequency determination:
    fc = ChannelStartingFrequency + fseparation x ChannelCenterFrequencyIndex
  fseparation has the value 0.5 MHz
  ChannelStartingFrequency and ChannelCenterFrequencyIndex are region and operating class specific and given in Annex E.
The global table entries show “reserved” – so you need to consult Table E-5 S1G operating class table
  See next slide

## Slide 10: Example Of S1G Operating Classes (2)
Table E-5—S1G operating classes
Currently, only S1G operating classes 6 and 7 are defined for the EU
S1G operating class | Global operating Class (See Table E-4) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel center frequency index | CCA Level Classification | Behavior limits set
4 (United States) | 71 | 0.902 | 8 | 44 | Type 1 (920-928 MHz) | -
 |  |  |  | 12, 28 | Type 2 (904-920 MHz) | 
5 (United States) | 72 | 0.902 | 16 | 20 | Type 2 (904-920 MHz) | -
6 (Europe) | 66 | 0.863 | 1 | 1, 3, 5, 7, 9 | Type 1 (863-868 MHz) | -
7 (Europe) | 67 | 0.863 | 2 | 2, 6 | Type 1 (863-868 MHz) | -
How to find S1G channels:
S1G Channel Numbers!

## Slide 11: Where Does the New EU Band Fit? (1)
Only two S1G operating classes currently defined for the EU
  They share a starting frequency which is different from the new one
  They share a channel number system/set/organization (with each other)
    Two classes exist because channel widths are different: 1 v 2 MHz
    As noted further above, 2 MHz should be removed
Some countries have multiple starting frequencies, i.e. “bands”
  China, Singapore
  Both of them restart the numbering for each “band” (i.e. class)
  See next slide

## Slide 12: Example Of S1G Operating Classes (3)
S1G operating class | Global operating Class (See Table E-4) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel center frequency index | CCA Level Classification | Behavior limits set
17 (Singapore) | 66 | 0.863 | 1 | 7, 9, 11 | Type 1 (866-869 MHz) | -
18 (Singapore) | 68 | 0.902 | 1 | 37, 39, 41, 43, 45 | Type 2 (920-925 MHz) | -
9 (China) | 61 | 0.755 | 1 | 1, 3, 5, 7, 9, 11, 13, 15, 17, 19, 21, 23, 25, 27, 29, 31, 33, 35, 37, 39, 41, 43, 45, 47 | Type 1 (755-779 MHz) | -
10 (China) | 62 | 0.779 | 1 | 1, 3, 5, 7, 9, 11, 13, 15 | Type 1 (779-787 MHz) | -
Table E-5 - Multiple bands for Singapore and China:

## Slide 13: Where Does the New Band Fit? (2)
EU needs a new starting frequency (i.e. new “band”)
  Based on existing examples:
    E.g starting channel frequency 901.4 MHz to allow band to grow down from 917.4-919.4 MHz as well as up, and less chance of repeating the channel index in EU bands (to save confusion)
    917.4-919.4 MHz can accommodate two 1 MHz wide channels with centers on 0.9 MOD 1 MHz frequencies
    Center of channel with channel center frequency indexes 33 and 35
      fc = ChannelStartingFrequency + fseparation x ChannelCenterFrequencyIndex
      917.9 = 901.4 + 0.5 * 33
      918.9 = 901.4 + 0.5 * 35

## Slide 14: Proposed Changes (1)
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
67 | E- 5-7, E-5-19 | 0.863 | 2 | - | Reserved | -
TGmd editor to make the following changes to Table E-4 – Global operating classes (note that one new row is being added to the table):
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
77-80 | -E-5-30 | Reserved0.9014 | Reserved1 | Reserved- | -Reserved | -Reserved
78-80 | - | Reserved | Reserved | Reserved | - | Reserved

## Slide 15: Proposed Changes (2)
S1G operating class | Global operating Class (See Table E-4) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel center frequency index | CCA Level Classification | Behavior limits set
7 (Europe) | 67- | 0.863Reserved | 2Reserved | 2, 6Reserved | Type 1 (863-868 MHz) Reserved | -Reserved
30 (Europe) | 77 | 0.9014 | 1 | 33, 35 | Type 1 (917.4-919.4 MHz) | -
TGmd editor to modify the following row in Table E-5 – S1G operating classes:

## Slide 16: Straw poll #1
Do you support the proposed changes to Draft P802.11REVmd_D3.4 Annex E Table E-4 – Global operating classes and Annex E Table E-5 – S1G operating classes as described in 11-20-1182-01-000m-S1G-EU-New-Band Proposed Changes (1) and Proposed Changes (2)?
  YES
  NO
  ABS

## Slide 17: References
[1] Draft P802.11REVmd_D3.4
[2] DECISION (EU) 2017/1483
  https://op.europa.eu/en/publication-detail/-/publication/ed3648d1-83e0-11e7-b5c6-01aa75ed71a1
  https://www.ecodocdb.dk/download/2787323d-d104/20171483EU.pdf
[3] Decision (EU) 2018/1538
  https://op.europa.eu/en/publication-detail/-/publication/7aa9ee9d-d053-11e8-9424-01aa75ed71a1/language-en/format-PDF/source-142398249
  https://www.erodocdb.dk/download/913676aa-f35b/EC%20Decision%202018%201538.pdf

## Slide 18: Appendix
More complete description of Reference [2]
  COMMISSION IMPLEMENTING DECISION (EU) 2017/1483 of 8 August 2017 amending Decision 2006/771/EC on harmonisation of the radio spectrum for use by short-range devices and repealing Decision 2006/804/EC (notified under document C(2017) 5464).
More complete description of Reference [3]
  Commission Implementing Decision (EU) 2018/1538 of 11 October 2018 on the harmonisation of radio spectrum for use by short-range devices within the 874-876 and 915-921 MHz frequency bands (notified under document C(2018) 6535) (Text with EEA relevance.)