## Slide 1: Architecture Issues
Date: 2020-08-11
Authors:

## Slide 2: Background
802.11bc considers both downlink and uplink broadcast modes
  Downlink: AP to non-AP STA
  Uplink: non-AP STA to AP
There are UL (uplink) frames defined but no DL (downlink) ones
  This appears to be unusual
There is a DMG restriction in clause 11
  I missed it in the comment collection
Here are some possible issues to consider before D1.0 is produced

## Slide 3: Frame definition issues
Frames have been defined to be specifically UL or something else.
  Frames should be used in any situation. The behaviour can then restrict operation, if required.
  There do not appear to be any DL frames. Should there be?
Perhaps re-consider some UL frames for general operation:
  eBCS UL Capabilities
    Consider a general frame which has an initial UL/DL control sub-field and different payload contents (e.g. see FILS discovery frame)
  eBCS UL frame
    Restrictive name
    Consider a new name describing it’s use

## Slide 4: For example, eBCS UL Capabilities field
 | Element ID | Length | Element ID Extension | eBCS UL Capabilities
Octets: | 1 | 1 | 1 | variable
 | B0 | B1 B3 | B4 B15
 | DL/UL | Other sub-fields | Reserved
Bits: | 1 | 2 | 11

## Slide 5: Why not DMG?
Clause 11.bc.1 states:
  “This subclause describes enhanced Broadcast Services (eBCS) procedures that are used for eBCS STAs. eBCS is only supported in a non-DMG non-S1G infrastructure BSS. Add/change text to enable A-MDPU for broadcast BSS (10.13).”
Why is DMG being excluded?
  Is it because there is no use case for DMG broadcast?