## Slide 1
Authors:
ML CCA and Channel Access
for non-STR Links
Date: 2020-08-13
Name | Affiliation | Address | Phone | Email
Yonggang Fang | ZTE (TX) |  |  | yfang@ztetx.com
Bo Sun | ZTE |  |  | 
Zhiqiang Han | ZTE |  |  | 
Liuming Lu | ZTE |  |  | 
Notes: doc.: IEEE 802.11-yy/xxxxr0
Month Year
        John Doe, Some Company
Page 1

## Slide 2: Abstract
This contribution discusses the ML CCA issue in a pair of non-STR links and proposes solutions to address this issue.

## Slide 3: Introduction
  ML Operation Scenario
  SFD [1] indicates the R1 shall support two cases:
    STR AP MLD with STR non-AP MLD
    STR AP MLD with non-STR non-AP MLD
  In this contribution, it will discuss the scenario 2)

## Slide 4: Issues of non-STR Related Operations
  Definitions
  STR or non-STR refers to a pair of links
    STR Channel Access [1]: 802.11be shall allow the following asynchronous multi-link channel access:
      Each of STAs belonging to a MLD performs a channel access over their links independently in order to transmit frames.
      Downlink and uplink frames can be transmitted simultaneously over the multiple links.
    Non-STR Operation:
      An MLD that is not capable of simultaneous Tx/Rx on multiple links for the given set of links (i.e., it can only do Tx/Tx or Rx/Rx on a pair of links)
  In [3], it discusses the operation of a pair of non-STR links in wide bandwidth. The non-STR link is possible to separate into three parts
    STR part
    STR constraint part
    Non-STR part

## Slide 5: Issues in a pair of non-STR Links
  ML Channel Access for A Pair of non-STR Links
  A pair of non-STR links does not support transmitting and receiving simultaneously. It may lead to the following constraints on the ML channel access:
    A MLD may have some constraints on CCA mechanism on a non-STR link when it is transmitting PPDU(s) on another non-STR link.
    A MLD should not transmit a PPDU on an idle non-STR link when it is receiving PPDU(s) on another non-STR link.
Rx sensitivity
Self- Interference
PDT
EDT
RSSI at
receiving antenna
Signal from other STA
Signal from other STA
Baseline CCA
ML CCA
with self-interference
RSSI at
receiving antenna
Rx sensitivity

## Slide 6: Issues in a pair of non-STR Links
  CCA Blindness
  When a MLD transmits a frame on a non-STR link, the transmitting signal from that link may leak out to interfere to the other non-STR link in listening mode:
    The CCA in other non-STR link would not be able to detect the preamble or the signal energy from other STAs if the cross link interference is strong enough
    If the other non-STR link is in the EDCA backoff, the backoff procedure would be suspended by the cross link interference.
Link 1
Link 2
Transmit UL PPDU
Interference causes CCA blind
Non-STR non-AP
MLD
interference from link 1
Interfere to CCA of other link
Time

## Slide 7: Issues in a pair of non-STR Links
  Reception Interruption
  Case 1: If one non-STR link is in the receiving mode already, another non-STR is going to start CCA and transmit a PPDU. The cross-link interference from the non-STR transmitting link would interrupt the reception on the non-STR receiving link.
  Case 2: This is a race condition. When one non-STR link is receiving a preamble, but another non-STR link is in EDCA backoff procedure. If the EDCA backoff reaches to 0 and starts to transmit, the cross-link interference from the non-STR transmitting link may interrupt the reception on the non-STR receiving link.
Link 1
Link 2
Transmit UL PPDU
Time
Cause reception interrupted
Non-STR non-AP
MLD
Receiving a PPDU
interference from link 1
Interfere to reception of other link
Preamble
Link 1
Link 2
Transmit UL PPDU
Time
Cause reception interrupted
Non-STR non-AP
MLD
Receiving a PPDU
interference from link 1
Interfere to reception of other link
Preamble
OBSS
(1)
(2)

## Slide 8: A Proposal of Channel Access
  Baseline Channel Access
  Physical CCA Carrier Sensing is used to assess the channel occupancy state
    CCA Preamble Detection: If the CCA detects a preamble of a frame and its signal strength is less than PDT (-82dBm), the channel is assessed as idle. Otherwise, the channel is busy.
      The PD can be used to set NAV.
    CCA Energy Detection: If the CCA detects a signal other than the preamble and its signal strength is less than EDT (-62dBm), the channel is assessed as idle. Otherwise, the channel is busy.
      The ED has to detect the signal in every time slot to determine whether the signal exists or not time.
      It may not be used to set NAV.

## Slide 9: A Proposal of Channel Access
  Constraint Period
  Tx Constraint Period is the time period that a frame is being transmitted on a non-STR link and interferes to another non-STR non-transmitting link.
  ML CCA Rules in Tx Constraint Period (1)
  Option 1: The MLD should set CCA state to “Busy” on the non-STR non-transmitting link during Tx Constraint period.
    Note: During the Tx Constraint period, the cross-link interference from the non-STR transmitting link would interfere CCA measurement accuracy on the non-STR non-transmitting link.
Time
Link 1
Link 2
CH Busy (OBSS)
Transmit UL PPDU
Transmits a PPDU
Tx Constraint Period
Set CCA state = Busy
Non-STR
MLD

## Slide 10: A Proposal of Channel Access
  ML CCA Rules in Tx Constraint Period (2)
  Option 2: An affiliated STA of MLD may perform ML CCA on a non-STR non-transmitting link during the Tx Constraint Period using the adjusted CCA measurement method with ED threshold.
    The adjusted CCA measurement is the measured signal strength on a link minus the interference on that link from the non-STR transmitting link (e.g. link1) in the Tx Constraint Period.
    If the adjusted CCA measurement < ED threshold, the channel is assessed as idle and the affiliated STA starts the EDCA backoff procedure (e.g. on link2).
    The adjusted CCA provides flexibility for asynchronous transmission over a pair of non-STR links.
Tx Constraint Period
Link 1
Link 2
CH Busy (OBSS)
Transmit a UL PPDU
Transmits a UL PPDU
Time
Perform the adjusted ML CCA
Non-STR
MLD

## Slide 11: A Proposal of Channel Access
  Constraint Period
  Rx Constraint Period is the time period that the frame addressed to the MLD is being received on a non-STR link and the reception will be interrupted if the MLD starts to transmit on another non-STR link.
  ML CCA Rules in Rx Constraint Period
  MLD may notify Rx Constraint Period to its STA on the non-STR non receiving link.
  During the Rx Constraint Period, the affiliated STA of the MLD may holds the backoff counter at “0” and the channel access on the non-STR non-receiving link.
  Note 1: This is to address the case (1) of reception interruption.
  Note 2: The non-STR links may need to synchronize the transmissions after the Rx Constraint period.
Rx Constraint Period
Link 1
Link 2
CH Busy (OBSS)
Receiving a DL PPDU
Transmit a UL PPDU
Time
Hold the BC at “0” and channel access
Non-STR
MLD
Transmit a UL PPDU

## Slide 12: Summary
This contribution
  Discuss the issue of cross-link interference to CCA in the non-STR links
  Suggest in the Tx constraint period to restrict the CCA or use adjusted CCA for the channel assessment to compensate cross-link interference from the non-STR transmitting link.
  Suggest in the Rx constraint period to hold the backoff counter at “0” and channel access on the non-STR non-receiving link.

## Slide 13: Straw Poll (1)
Do you support to include the following in SFD ?
  During the Tx Constraint period, a MLD should set the CCA state to “busy” on a non-STR non-transmitting link.
    Note: Tx Constraint Period is the time period that a frame is being transmitted on a non-STR link and interferes to another non-STR non-transmitting link.
YES/NO/ABS

## Slide 14: Straw Poll (2)
Do you support to include the following in SFD ?
  During the Tx Constraint period, a MLD may perform the adjusted ML CCA on a non-STR non-transmitting link.
    Note: Tx Constraint Period is the time period that a frame is being transmitted on a non-STR link and interferes to another non-STR non-transmitting link.
YES/NO/ABS

## Slide 15: Straw Poll (3)
Do you support to include the following in SFD ?
  During Rx Constraint Period, a MLD may perform ML CCA sensing on a non-STR non-receiving link, and EDCA backoff procedure if the ML CCA senses the link idle. The MLD should hold the backoff counter after reaching at “0” and the channel access on the non-STR non receiving link.
    Note: Rx Constraint Period is the time period that the frame addressed to the MLD is being received on a non-STR link of the MLD.
YES/NO/ABS

## Slide 16: References
[1] 11-20-0566-53-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[2] 11-20-0026-02-00be-mlo-sync-ppdus
[3] 11-20-1220-00-00be-STR and non-STR capability indication
[4] 11-20-0069-05-00be-multi-link-communication-mode-definition

## Slide 17
Thank you!