## Slide 1: SIG contents discussion for EHT sounding NDP
Date: 2020-08-20
Authors:
Name | Affiliations | Address | Phone | email
Ross Jian Yu | Huawei |  |  | ross.yujian@huawei.com
Mengshi Hu | Huawei |  |  | 
Ming Gan | Huawei |  |  | 

## Slide 2: Background
In [1], U-SIG and EHT-SIG contents have been very well discussed (see the table on the right).
There are some parts we want to discuss in this proposal (marked in red).
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | PPDU BW | 3
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU format | 1
 |  | Reserved | 6
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 |  | EHT-SIG Compression | 2
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 3
 |  | Number of EHT-LTF symbols and midamble periodicity | 3
 |  | Reserved | 1
 |  | Pre-FEC padding | 2
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 2
 |  | PE disambiguity | 1
 | Total # of Overflow Bits |  | 17

## Slide 3: Background: EHT-SIG for single user case [1]
[1] proposes: Overflow bits kept to <=17 to make sure EHT-SIG can fit to 2 symbols at MCS0 for single user case.
  17 bits overflow bits, together with 3 bit number of non-OFDMA users, 22-bit user field, 10 bit CRC + Tail, 52 bits in total.
  EHT-SIG with MCS0 (BSPK, R 1/2) can carry 26 uncoded bits per symbol.
Subfield | Number of Bits
STA-ID | 11
Spatial Configuration | 6
MCS | 4
Coding | 1
User field for a Non-MU-MIMO allocation
User field for an MU-MIMO allocation
Subfield | Number of Bits
STA-ID | 11
NSTS | 4
Beamformed | 1
MCS | 4
Reserved | 1
Coding | 1

## Slide 4: Background: EHT-SIG for sounding NDP in [1]
[1] proposes the same format of NDP as single user case EHT MU PPDU.
  Can lead to additional 2 more symbols overhead compared with HE sounding NDP
    11ax: 2 symbols HE-SIG-A
    11be: 2 symbols U-SIG + 2 symbols EHT-SIG (with MCS 0)
      EHT-SIG carries a meaningless number of non-OFDMA users subfield (3bits, 1-8) + 32 bits padding of “User Block”  the 2nd symbol of EHT-SIG is all padding+CRC+Tail.
Padding or dummy user field
to make length same as SU
U-SIG overflow needs to be 17 bits or lower for a 2 symbol EHT-SIG at MCS0
U-SIG overflow + 3 bits (#of users) + 22 (user-field)+10 bits CRC/tail needs to be within 52 bits
SU and DUPed SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  | Padding |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | Padding |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | Padding |  |  | 

## Slide 5
Propose to have a sounding NDP always with one symbol EHT-SIG to save overhead.
Still have the same U-SIG contents and U-SIG Overflow contents as other EHT MU PPDU for consistency and unification.
Propose to have 16 bits U-SIG Overflow for all modes of EHT MU PPDU. 10 bits CRC+Tail in EHT-SIG SYM 1 for EHT sounding NDP.
Updated in r2: Propose to still enable separate indication of Number of EHT-LTF Symbols and Nss.
Proposed EHT sounding NDP
SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  |  |  |  | 
Content channel #1 | U-SIG Overflow | CRC+Tail |  |  |  | 
Content channel #2 | U-SIG Overflow | CRC+Tail |  |  |  | 
16 bits U-SIG overflow + 10 bits CRC/tail = 26 bits
U-SIG overflow needs to be 16 bits or lower
16 bits U-SIG overflow + 3 bits (#of users) + 22 (user-field)+10 bits CRC/tail + 1 bit padding bit = 52 bits

## Slide 6
Three options are proposed in [1] to signal NDP:
Signaling of NDP
SU | Common Field |  | User Specific Field |  |  | 
Content channel #1 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
Content channel #2 | U-SIG Overflow | #User = 1 | User field 1 |  |  | 
NDP | Common Field |  |  |  |  | 
Content channel #1 | U-SIG Overflow | CRC+Tail |  |  |  | 
Content channel #2 | U-SIG Overflow | CRC+Tail |  |  |  | 
Options [1] | My comment
Option 1: Use the L-SIG length along with N_LTF and number of EHT-SIG symbols to tell that there is no data in this packet Similar way is used by 11ax and 11ac | still applicable for 11be
Option 2: Set the EHT-SIG MCS to 0 and number of EHT-SIG symbols to 1 Update in r2: for EHT NDP with one symbol EHT-SIG, besides Option 1, this can act an explicit indication of EHT NDP | provides early/easy detection of NDP, don’t consume additional signaling bits/entries. Only applicable to the proposed sounding NDP (most preferred)

## Slide 7
Updated in r2: several fields are not needed for EHT NDP:
  Pre-FEC padding (2 bit)
  LDPC extra symbol segment (1bit)
  PE Disambiguity (1 bit)
  Reserved (4 bit to 3 bit for EHT NDP)
Propose to indicate Nss (4bit) by reusing Pre-FEC padding factor + PE disambiguity + LDPC extra symbol segment indication.
The reserved bits are still kept for other potential purposes.
Nss indication in EHT NDP
Field | Category | Subfield | Bits
U-SIG | Version Independent | Version identifier | 3
 |  | PPDU BW | 3
 |  | UL/DL | 1
 |  | BSS color | 6
 |  | TXOP | 7
 |  | Reserved | 6
 | Version Dependent | Punctured channel indication(global for non-OFDMA) | 5
 |  | Reserved | 1
 |  | PPDU type & Compression Mode | 2
 |  | Reserved | 1
 |  | EHT-SIG MCS | 2
 |  | Number of EHT-SIG symbols | 5
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6
 | Total # of Bits in U-SIG |  | 52
EHT-SIG | Version Dependent (U-SIG Overflow) | Spatial reuse | 4
 |  | GI+LTF size | 2
 |  | Number of EHT-LTF symbols | 3
 |  | Pre-FEC padding | 2
 |  | PE disambiguity | 1
 |  | LDPC extra symbol segment | 1
 |  | Reserved | 3
 | Total # of Overflow Bits |  | 16
 | CRC & Tail | CRC in U-SIG | 4
 |  | Tail in U-SIG | 6

## Slide 8: Summary
In [1], U-SIG and EHT-SIG contents have been very well discussed and some parts are discussed in this proposal regarding sounding NDP and its signaling, PPDU format + EHT-SIG compression, and BSS color.
An efficient sounding NDP format is proposed, in which case one symbol EHT-SIG is enough for MCS 0. And provide a signaling method for early detection of sounding NDP.

## Slide 9: Straw Poll #2
Do you agree to add the following text in the TGbe SFD:
  The EHT-SIG of EHT sounding NDP is always modulated with BPSK R 1/2, and has only one symbol.
    The EHT-SIG of EHT sounding NDP contains 16 bit U-SIG overflow bits and 4 bit CRC and 6 bit Tail.
    This is for R1.

## Slide 10: Straw Poll #3
Do you agree to add the following text in the TGbe SFD:
  An EHT sounding NDP is signaled through:
    Number of EHT-SIG symbols is set to 1, and
    EHT-SIG MCS is set to BPSK R ½
    This is for R1.

## Slide 11: Straw Poll #4
Do you agree to add the following text in the TGbe SFD:
  Pre-FEC padding factor + PE disambiguity + LDPC extra symbol segment indication are repurposed to signal NSS in an EHT sounding NDP.
    This is for R1.

## Slide 12
https://mentor.ieee.org/802.11/dcn/20/11-20-1238-00-00be-open-issues-on-preamble-design.pptx, Sameer Vermani, Qualcomm
https://mentor.ieee.org/802.11/dcn/20/11-20-0566-60-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document.docx, Edward Au, Huawei
https://mentor.ieee.org/802.11/dcn/20/11-20-1015-02-00be-eht-ndpa-frame-design-discussion.pptx, Chenchen Liu, Huawei
https://mentor.ieee.org/802.11/dcn/20/11-20-1474-00-00be-ndp-design-for-eht.pptx, Eunsung Jeon
References