## Slide 1: Enhancements for QoS and low latency in 802.11be R1
Date: 2020-08-28
Authors:

## Slide 2: Introduction
This contribution builds on the QoS management (Doc#418r3) for low latency reliable services (LLRS)
The proposed simple enhancements address the worst case latency and jitter issues caused by congestion and can be enabled in R1
Minimum basic support in R1 is required to ensure no coexistence issues between R1 and R2 EHT STAs

## Slide 3: Problem: how to protect low latency data that have a “deadline” from congestion delay
It is difficult to guarantee access to a given STA(s) at certain times, due to
  Unlicensed band
  Legacy devices
A general solution applicable in all conditions is challenging (not the goal of this contribution)
Focus on EHT capabilities
Need to enable more controlled access in the MAC to reduce the impact on congestion
Leverage 802.11be and previous tools
  Contention-based channels access

## Slide 4: Scope and goals for latency enhancements in 11be
Our goal in R1 is to provide minimal support to avoid creating a new category of EHT “legacy” devices that do NOT coexist with EHT R2 low latency/channel access enhancements
    Need to avoid coexistence issues between R1 and R2 EHT devices
There are many tools already in 802.11be (and previous specs) to improve latency such as MLO, TWT, TF that reduces the impact of intra-BSS congestion on low latency traffic
  In R1, we intend to mostly leverage and propose simple enhancements to those tools and improve latency for traffic that can be identified/classified through QoS negotiation
Further performance enhancements can be introduced in R2

## Slide 5: Approach: Enable periods of time during which low latency traffic can be protected from intra-BSS congestion
Minimal Spec requirements in R1
  Non-AP STA and AP negotiate establishment of or participation in a protected period
    If negotiation is successful, non-AP STA is a member of the protected period
    AP advertises the “protected” period(s) (Broadcast TWT can be reused/enhanced)
  Access rules for all associated EHT STAs during the “protected” periods:
    STAs shall finish their TXOPs before the period
    If a STA is not a member, it shall not transmit during the period
Low latency traffic is prioritized/ protected from congestion
Normal operation outside

## Slide 6: Example: Protected TW SP set up and operation

## Slide 7: Access Rules for Participating EHT STAs – Announced by the AP
Protected period
Normal operation (any TID and EDCA access resumed)
Trigger-enabled
  AP triggers STAs and prioritize allowed traffic (including P2P)
Trigger SU PPDU would help make this mode more used
Normal operation (no changes)
(allowed STAs/TIDs and access rules)
Configuration 1:
Non-trigger-enabled
  EDCA access between members of the protected period (including P2P)
Configuration 2:

## Slide 8: Conclusions
We presented an approach to protect low latency traffic from intra-BSS congestion and avoid coexistence issues between R1 and R2 EHT STAs
The approach leverages existing tools and capabilities
The Spec changes required include
  Announcement of “protected” periods (BTWT signaling can be re-used/enhanced)
  Access rules for EHT STAs during the “protected” periods
Further enhancements can be considered in R2

## Slide 9: SP #1
Do you agree to add to the TGbe SFD
  A mechanism for defining protected periods
    AP and STA negotiate the creation of or the participation in a protected service period
      If negotiation is successful, non-AP STA is a member of the protected period
      AP advertises the “protected” period(s) in beacons (Broadcast TWT could be reused/enhanced)
    Access rules for all associated EHT STAs during the “protected” periods:
      STAs shall finish their TXOPs before the period
      Other requirements TBD

## Slide 10: backup

## Slide 11: Simulation scenario 1
Single BSS: 6 STAs (2 Low Latency, 4 BE - 6 Mbps), 20 MHz channel
  LL traffic streams: 10Mpbs streaming video DL, Periodic 100 Byte every 4 ms UL
LLS: low latency traffic using AC_VO + protected windows
  1 ms windows every 5 ms
VO: low latency streams using AC_VO
Channel access: EDCA + Protected window for LLRS traffic

## Slide 12: Scenario 1 - Results (20 MHz)
LLS: low latency streams with protected windows
VO: low latency as AC_VO (no protected windows)

## Slide 13: Scenario 1 - Results (80 MHz)
LLS: low latency streams with protected windows
VO: low latency as AC_VO (no protected windows)

## Slide 14: Scenario 1 - Results (40 MHz)
LLS: low latency streams with protected windows
VO: low latency as AC_VO (no protected windows)

## Slide 15: Simulation scenario 2
Single BSS: 6 STAs (2 Low Latency, 4 BE - 6 Mbps), 20 MHz channel
  LL traffic streams: 100Bytes every 4 ms
LLS: low latency traffic using AC_VO + protected windows
  500 microseconds windows every 4 ms
VO: low latency traffic using AC_VO
Case 1: EDCA in protected window (AP and STAs contend)
Case 2: Trigger based in protected window

## Slide 16: Scenario 2- Case 1 Results
LLS: low latency stream with protected windows
VO: low latency as AC_VO (no protected windows)

## Slide 17: Scenario 2 - Case 2 Results
LLS: low latency stream with protected windows
VO: low latency as AC_VO (no protected windows)