## Slide 1: Further Discussion about Blindness for non-STR MLD
Date: 2020-08-18
Authors:
Name | Affiliations | Address | Phone | Email
Yiqing Li | Huawei | Shenzhen, China |  | liyiqing3@huawei.com
Yunbo Li |  |  |  | 
Yuchen Guo |  |  |  | 
Ming Gan |  |  |  | 
Guogang Huang |  |  |  | 
Rob Sun |  |  |  | 
Mengyao Ma |  |  |  | 
Hongjia Su |  |  |  | 
Notes: September 2012

## Slide 2: Motivation
How to handle the blindness issue at non-STR non-AP MLD side is discussed in [1];
There are three main points
  Introduce a MediumSyncDelay parameter
  Decrease the ED threshold, [-82dBm, -62dBm]
  Allow to transmit limited times of RTS while MediumSyncDelay timer is running
Allow RTS transmission while MediumSyncDelay timer is running will be risk in certain case, it should be avoided.

## Slide 3: Issues to Tx RTS in MediumSyncDelay
It is a typical scenario that AP3 in link2 can be heard by STA2, but STA3 (associated with AP3) is hidden from STA2;
After the blindness period, channel will be busy for STA2 due to the transmission of PPDU3, but when PPDU3 is finished, STA2 will sense the channel becomes idle;
If STA2 start to backoff, and transmit RTS, it will collide with BA from STA3 to AP3;
The standard should avoid it happens.
Blindness period
CCA busy
MediumSyncDelay
link1
link2
STA1
STA2
link2
STA3
AP1
AP2
AP3
AP MLD
Non-AP MLD
PPDU1 from STA1 to AP1
RTS from STA2 to AP2
PPDU3 from AP3 to STA3
BA3 from STA3 to AP3
Interference to BA3

## Slide 4: Solution 1: Disallow backoff in EIFS
A potential solution 1 is that if the channel is busy right after the blindness period base on the ED sensing results, STA2 is not allowed to backoff within EIFS time;
So it will leave time for STA3 to transmit BA3 to AP3;
If there are following PPDU4 from AP3 after BA3, STA2 will decode PPDU4 to set NAV.
Blindness period
CCA busy
MediumSyncDelay
link1
link2
STA1
STA2
link2
STA3
AP1
AP2
AP3
AP MLD
Non-AP MLD
PPDU1 from STA1 to AP1
PPDU3 from AP3 to STA3
BA3 from STA3 to AP3
EIFS

## Slide 5: Solution 1: Disallow backoff in EIFS
No matter STA3 is hidden or not, disallow backoff within EIFS following a immediate busy will not hurt the system performance
  For the case that STA3 is hidden from STA2, it is the scenario we want to protect STA3’s transmission
  For the case that STA3 is not hidden from STA2, STA2 will set NAV by BA3 from STA3, and MediumSyncDelay time expires.
The channel busy may caused by Wi-Fi signal or non-Wi-Fi signal. Since it is hard to distinguish them when preamble is missed, it is better to treat them as Wi-Fi signal;
Solution 1 is preferred.
Blindness period
CCA busy
MediumSyncDelay
link1
link2
STA1
STA2
link2
STA3
AP1
AP2
AP3
AP MLD
Non-AP MLD
PPDU1 from STA1 to AP1
PPDU3 from AP3 to STA3
BA3 from STA3 to AP3
EIFS

## Slide 6: Solution 2: Disallow backoff in MediumSyncDelay
Solution 2 is to disallow backoff in within the MediumSyncDelay period;
It is a more conservative solution, which is not so necessary;
Solution 2 is not preferred.
Blindness period
CCA busy
MediumSyncDelay
link1
link2
STA1
STA2
link2
STA3
AP1
AP2
AP3
AP MLD
Non-AP MLD
PPDU1 from STA1 to AP1
PPDU3 from AP3 to STA3
BA3 from STA3 to AP3
Backoff Disallow

## Slide 7: Summary
Allow RTS transmission while MediumSyncDelay timer is running will be risk if the channel is busy right after the blindness period base on the ED sensing results, the standard should avoided it happens.
Two potential solutions are provided, and solution 1 is preferred
  Solution 1: disallow backoff in EIFS
  Solution 2: disallow backoff in whole MediumSyncDelay

## Slide 8: Straw Poll 1
Do you agree that if the channel is busy right after the blindness period base on the ED sensing results, a STA that affiliate with a NSTR MLD is not allowed to backoff within EIFS time?
  It is for R1.
Y/N/A

## Slide 9: Reference
[1] 11-20-1009-01-00be-multi-link-hidden-terminal-followup