## Slide 1: EHT NLTF Design
Date: 2020-08-27
Authors:

## Slide 2: Introduction
In IEEE, decoupling NLTF and Nss is proposed in [1].
  1~2dB SNR gain is observed for various SU/MU cases.
We validate the performance gain.
  All MCS, 1~2dB better sensitivity can be achieved.
  High QAM 4096, relax transmitter design or improves range.
Low hanging fruit for SNR gain with limited design effort.

## Slide 3: NLTF and Nss in EHT
11ax mandatory support for DL-MUMIMO and OFDMA
  11ax STAs support receiving more LTF than allocated Nsts in MU.
  Hardware is already in the silicon to process extra LTFs.
  SU with extra LTFs disallowed in 11ax signaling to reduce modes.
EHT preamble uses unified format for SU and MU
  There is no separate SU mode.
  NLTF signaling is already decoupled from Nsts for SU.
Performance gain
  Better channel estimation SNR translates to sensitivity gain.
  On top of any channel smoothing techniques.
  Much easier gain than HARQ.

## Slide 4: Simulations
Settings:
  80MHz
  SU MIMO with beamforming
  DNLos: 1000 channels
  CFO

## Slide 5: 8x2-2ss: DNLos
  ~1.5dB gain with doubled LTF number
  Addition 0.7dB gain with 4 times LTF number

## Slide 6: 8x4-3ss: DNLos
  ~1.5dB gain with doubled LTF number
  Addition 0.7dB gain with 4 times LTF number

## Slide 7: 8x8-6ss: DNLos
  ~1.2dB gain with doubled LTF number
  Addition ~0.5dB gain with 4 more LTFs

## Slide 8: 4x1-1ss
  ~1dB gain with doubled LTF number
  Additional ~0.5dB gain with 4 times LTF number

## Slide 9: Discussions
Extra LTF provides good sensitivity gain.
  >1dB gain by doubling NLTFs
  Additional ~0.5dB gain with extra 3 times of original NLTFs
  Most of the sensitivity gain is achieved by 2 times of NLTFs.
Limited design efforts.
  11ax silicon already supports processing of extra LTFs for OFDMA (including partial BW MUMIMO).
  EHT preamble decouples signaling of Num of LTFs and Num of Nss.
Propose EHT to add support of up to 2 times of NLTFs for non-OFDMA transmissions.
  Optionally for EHT STA to support.

## Slide 10: 11ax NLTF Capability Settings
Transmissions | NLTF vs Nsts | Capability of Max NLTF
SU | NLTF = Nsts | Same as Nss capability
MUMIMO | NLTF = Nsts_tot | Same as Beamformee NSTS capability
NDP | NLTF = Nsts | Same as Beamformee NSTS capability
MU OFDMA | NLTF >= Nsts/Nsts_tot | “Max NLTF for MU OFDMA” capability same as Beamformee NSTS capability 8

## Slide 11: 11be NLTF Capability Settings
Transmission | NLTF vs Nsts | M/O | Capability of Max NLTF
SU | NLTF >= Nsts | O | Max NLTF for SU
MUMIMO | NLTF >= Nsts_tot | O | Max NLTF for MU/OFDMA, NDP
NDP | NLTF >= Nsts | O | Max NLTF for MU/OFDMA, NDP
MU OFDMA | NLTF >=Nsts/Nsts_tot | M | Max NLTF for MU/OFDMA, NDP
  One capability bit to indicate support of extra LTF for SU/MUMIMO/NDP
  One capability element to indicate maximum NLTF for SU
  Extend 11ax “MU max NLTF” capability element to indicate maximum NLTF for MU and NDP

## Slide 12: SP1
Do you agree that the number of EHT-LTF in 11be non-OFDMA transmissions, is larger than or equal to the initial number of EHT-LTF determined by the number of total space-time streams?
  The maximum number of EHT-LTFs supported by the receiving STA(s) can be claimed by capability.
  The Num of EHT-LTFs is signaled separately from Nsts or Nsts_total.
  This feature is optional for receiver.
  The allowed number of extra LTFs is TBD
  Y
  N A

## Slide 13: SP2
Do you agree that 11be defines three PHY capability elements to indicate an EHT STA’s maximum supported number of EHT-LTFs
  One bit to indicate the support of Extra LTFs for non-OFDMA PPDU
  One element to indicate the maximum number of LTFs supported for data transmission to non-OFDMA single user
    Note: Larger than or equal to Nsts capability
  One element to indicate the maximum number of LTFs supported for data transmission to multiple users and NDP
    Note: Larger than or equal to beamformee Nsts capability
  Y
  N
  A

## Slide 14: SP3
Do you agree that the allowed values of
  max NLTF receive capability for single-user transmission,
  max NLTF receive capability for multiple users transmission and NDP
  are 4, 8 and 16?
  Y
  N
  A

## Slide 15: SP4
Do you agree that, if extra LTF is applied to non-OFDMA transmission, the number of EHT-LTF should be
  chosen from the set [2 4 8 16].
    NLTF=12 is supported if P12 is real binary matrix.
  Up to 2 times of initial NLTF for all Nss.
  Y
  N
  A

## Slide 16: Reference
[1] “decoupling-channel-training-from-nsts”, IEEE 11-20/0486