## Slide 1: EHT Sounding Discussion
Date: 2020-09-12
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Sounding in 11ac
HT sounding includes many flavors: explicit sounding, implicit sounding.
VHT sounding is simplified by including explicit sounding only:
  Sounding with single beamformee:
  Sounding with more than one beamformee:
  When the sounding feedback is longer than 11454 octets, the feedback is fragmented to multiple frames which are transmitted in one PPDU.
    The typical implementation of 11ac’s sounding feedback doesn’t need the fragmentation.
  The sounding feedback can be polled in the following TXOP or in the same TXOP.
    The segments of sounding feedback can be partially polled in the sounding feedback retransmission.

## Slide 3: Recap: Sounding in 11ax
HE sounding is simplified by including explicit sounding only:
  NTB sounding with single beamformee:
  TB sounding with more than one beamformee:
  When the sounding feedback is longer than 11454, the feedback is fragmented to multiple frames to be transmitted in one PPDU.
    The typical implementation of 11ax’s sounding feedback doesn’t need the fragmentation.
HE sounding is further simplified:
  In NTB sounding, the beamformer can’t poll the sounding feedback.
  In TB sounding the sounding feedback can be polled in the same TXOP more than one time.

## Slide 4: EHT Sounding Observation and Potential Simplification
With the wider BW (>160MHz) and more spatial streams (>8), the fragmentation of sounding feedback will become popular.
  If we follows 11ax’s sounding protocol, the beamformee needs to send the partial sounding feedback per beamformer’s request.
The NTB sounding procedure of 11be is same as the NTB sounding of 11ax.
  In NTB sounding, the beamformer can’t poll the sounding feedback.
In a TB sounding sequence initiated by NDPA and NDP, an EHT AP is not allowed to poll a beamformee more than one time.

## Slide 5: Straw Poll
Do you support that in 11be sounding the following rules are defined:
  In NTB sounding, the beamformer shall not poll the sounding feedback
  In a TB sounding sequence initiated by NDPA and NDP, an EHT AP shall not poll a beamformee more than one time